## Slide 1: 5G – a quick overview
Yaakov (J) Stein
February 2020
Notes: When I say 5G what are the first things come to you mind ?

## Slide 2: Why 5G ?

## Slide 3: 5G is coming fast!
Source: Ericsson Mobility Report, Nov 2019
5G standardization was accelerated and proceeded at an unprecedented pace
Release 15 had an early drop completed Dec 2017 (a year earlier than originally planned)
and the majority of the work was approved in June 2018
Release 16 will be frozen in March 2020 and completed by June 2020
WRC-19 approved 17.25 GHz of new spectrum in November 2019
and the ongoing FCC auction has already surpassed $8B

## Slide 4: 5G is already here!
WorldTimeZone Dec 12, 2019
>7000 deployments >100 operators

## Slide 5: Generations of cellular technologies
 | 1G | 2G | 3G | 4G | 5G
3GPP releases |  |  | 4 - 7 | 8-9, 10-14 | 15, 16
era | 1980s | 1990s | 2000s | 2010s | 2020s
services | analog voice | digital voice messages | WB voice packet data | voice, video always on Internet | everything
devices |  |  |  |  | 
data rate | 0 | 100 kbps (GPRS) | 10 Mbps (HSPA) | 100+ Mbps (LTE/LTE-A) | 10 Gbps (NR)
delay |  | 500 ms | 100 ms | 10s ms | 5 ms

## Slide 6: What’s wrong with 4G?
4G made possible:
fast Internet access
video reception and creation
apps relying on location and identity
always-on behavior
but suffers from numerous limitations:
for some applications: data-rate too low
for some applications: delay too high
too few simultaneous connections (insufficient density)
coverage too low / drop rate too high
weak (if any) QoS guarantees
price per bit too high (inefficient spectral use)
power consumption too high (and thus battery life too low)
poor support for new applications/markets (e.g., IoT, AR/VR, connected cars)
no support for new mobility requirements (mobile hot spots, high speed)
insufficient security/privacy
5G is designed to address 4G limitations

## Slide 7: Verticals
Unlike earlier generations
which were designed for general purpose connectivity
without considering requirements for specific use cases
initial 5G work focused on vertical markets of interest, such as
● fixed and mobile broadband ● entertainment and gaming
● AR/VR ● wearables
● first responders ● critical infrastructure
● smart city ● smart utilities
● automotive (V2X) ● mass transit
● e-health ● e-government
Industry 4.0 (incl. industrial robots) ● agriculture
and collected specific requirements for each
Requirements were found to fall into 3 main categories
● eMBB enhanced mobile (or fixed wireless) broadband
● URLLC ultra-reliable and low latency communications
● mMTC (AKA mIoT) massive machine type communications

## Slide 8: 5G usage categories
eMBB
mMTC
(MIoT)
URLLC
10 Gbps, 10 Mbps/m2
1 Million / km2
1 ms, 5 nines
from M.2083.0

## Slide 9: IMT-2020 goals
ITU-R published M.2083.0
IMT Vision – Framework and overall objectives
of the future development of IMT
for 2020 and beyond
which defined performance targets for 5G
that are 10 to 100 times more than 4G :
Peak data rate (up to 20 Gbps/device)
User experienced data rate (100 Mbps/device)
Latency (as low as 1 ms)
Mobility (500 km/h and seamless transfer)
Connection density (1 million devices/km2)
Energy efficiency (1/100 Joule/bit for both air interface and network)
Spectrum efficiency (3 times the bps/Hz of LTE-A)
Area traffic capacity (10 Mbps/m2)
However, it is recognized that it may not be possible (or needed)
to attain all of these at the same time

## Slide 10: Business services
Due to LTE’s limited data-rates and availability
until now mobile-only operators could not provide profitable business services
which typically require fiber or symmetric DSL
With 5G, business sites can be connected to the feature-rich 5G core using
5G NR - Fixed Wireless Access (fixed, since CPE isn’t mobile!)
Fiber using the Access Gateway Function (being defined by 3GPP and BBF)
Local
Network
LAN
FWA
5G Fiber CPE
Fiber
Customer Sites
5G Cellular CPE
Content/Apps
Internet
Data Network
Core DC
VNFs
Mobile Core
AMF
UPF
AGF
gNB

## Slide 11: From 4G to 5G

## Slide 12: 5G changes all cellular segments
User Equipment
Air Interface(s)
Base Station
BTS, NB, eNB, gNB
FDMA, TDMA, CDMA, NR
Radio Access Network
(backhauling)
GRAN, GERAN, UTRAN, E-UTRAN,
NextGen (R)AN
core network
NSS, UMTS core, EPC, 5GC
other networks

## Slide 13: How does 5G attain higher speed?
Air interface
NR more efficient (factor of 3 improvement)
wider spectral bands (100 MHz, 1GHz), which requires
  new RF bands (sub-1GHz, mmWave: 24/28 GHz, 30-90GHz)
  use of licensed/unlicensed unshared/shared spectrum
smaller cells and densification
Massive (16 or more, up to 256) MIMO
    < 6 GHz use multipath for spatial mux and multiuser MIMO
    > 6 GHz use coherent beamforming (personal cells)
RAN
functional split options – split 2 and 7.2 standardized
upgrade backhauling from 1Gbps to 10Gbps to 100Gbps
25 GbE (802.3by), 1-lane 50 GbE (802.3cd), NG 100/200/400 GbE (802.3bs)
FlexE bonding

## Slide 14: R15 operating bands
FR1 (< 6GHz)
FR2 (>6GHz)
WRC-19 Sharm El-Skeikh Nov 2019
expanded RF bands available for 5G from 1.9 GHz to 17.25 GHz
New bands:
24.25-27.5 GHz
37-43.5 GHz
45.5-47 GHz
47.2-48.2 GHz
66-71 GHz
Additional bands will be considered for WRC-23
including low and mid frequencies

## Slide 15: How does 5G attain lower latencies?
Air interface
more flexible frame structure
self contained integrated subframe
RAN
Software Defined Networking or Segment Routing
Network Functions Virtualization
Mobile Edge Computing (moving functionality closer to UE)
Time Sensitive Networking / Deterministic Networking
  IEEE 802.1CM for Ethernet fronthaul
  IEEE 802.1Qbv scheduled traffic enhancements
  IEEE 802.1Qbu frame pre-emption
  IETF DetNet (Deterministic Networking) for IP
Network slicing

## Slide 16: Network slicing
5G must support coexistence of traffic with wildly diverging requirements
It can’t necessarily reach all of its goals simultaneously, but it doesn’t have to
For example:
enhanced mobile broadband
  needs high data rates
  doesn’t need very low latency
massive IoT
  needs high connection density
  doesn’t need high data rates
5G uses network slicing to satisfy these widely divergent needs
Network slices are dynamically established strong-isolated networks

## Slide 17: Network slicing
5G can support coexistence of traffic with wildly diverging requirements
by using network slicing in the air interface, xhaul, and core
on-demand (i.e., dynamic) assignment of networking/computational resources
  bandwidth, forwarding tables, processing capacity, etc.
each slice acts as an end-to-end independent network
resources can be physical or virtual, but
each slice acts as a strongly isolated network or cloud
  isolation of management, security, and performance
3GPP defines a slice by
Slice/Service type (SST) expected slice behaviour (features and services)
  3 types mandated, but many other types possible
    for example, MVNOs, specific enterprises, etc.
Slice Differentiator (SD) to differentiate between different slices of the same Slice/Service type
Slice/Service type | SST value
eMBB | 1
URLLC | 2
MIoT | 3

## Slide 18: How does 5G support new applications?
New cloud-based Service Based Architecture core
SDN/SR, NFV and network slicing
Network Functions and exposure functions (NRF, NEF)
client/server with RESTful interfaces (CRUD operations)
Application Functions

## Slide 19: How do we get there from here?
Initial 5G deployments focus on eMBB
and simply locate a gNB next to existing eNB (“deployment option 3”)
In order to facilitate this first stage 3GPP defined Non StandAlone (NSA)
i.e., 5G supported by the existing 4G infrastructure (E-UTRAN, EPC)
and thus not delivering all 5G’s potential
3GPP has also defined 3 StandAlone options
The obvious two are pure SA 4G (option 1) and 5G (option 2)
For the distant future there is option 5 for supporting legacy phones
with a 4G LTE air interface connecting to a 5G core
LTE
NR
gNb
eNB
EPC
5GC
4G data
4G ctrl
5G data
5G ctrl
Option 1
Option 2
5GC
Option 5
LTE
ng-eNB

## Slide 20: Option(s) 3
The most important NSA option in the near term is called option 3
which assumes installation of a gNB (to gain the advantages of NR)
but does not (yet) upgrade the core to 5GC
and so provides higher data rates but not full 5G capabilities
This will enable fast deployment of gNBs for eMBB
In option 3 there is no direct connection between gNB and EPC
user and control data flow through the eNB via X2-U and X2-C interfaces
In option 3A there is an S1-U connection from gNB to EPC (but no X2-U)
Option 3X has both X2 and S1 to enable load balancing
LTE
NR
gNB
eNB
EPC
4G data
4G ctrl
5G data
5G ctrl
Option 3
LTE
NR
gNB
eNB
EPC
Option 3A
LTE
NR
gNB
eNB
EPC
Option 3X

## Slide 21: Other options
For the distant future there are options 4 and 7
which only have a 5G core (no EPC)
but support 4G legacy UEs via upgraded ng-eNBs
In option 4 gNB is the master and ng-eNB connects via Xn interface
In option 7 ng-eNB is the master and gNB connects via Xn interface
These too have variations (4, 4A, 7, 7A, and 7X)
4G data
4G ctrl
5G data
5G ctrl
LTE
NR
gNB
ng-eNB
Options 4
5GC
LTE
NR
gNB
ng-eNB
Options 7
5GC
4A only
7A and 7X
4 only
7A,7X

## Slide 22: 5G Radio Access Network

## Slide 23: Splitting up the RAN
In 3G the RAN was a pure backhaul network
In 4G this changed in 2 ways
the X2 interface interconnected eNBs (at least logically)
fronthaul (CPRI)
In 5G this changes more drastically
RNC
NB
NB
NB
NB
MSC/SGSN
fronthaul
BBU
backhaul
CORE
RH
eNB
eNB
eNB
eNB
X2
S1
Notes: What’s the problem?

## Slide 24: 5G RAN Functional Splits
Decomposed base station transceiver
PHY – Physical layer processing
MAC – Medium Access Control
RLC – Radio Link Control
PDCP – Packet Data Convergence Protocol
Network based control functionality
RRC – Radio Resource Control
LTE uses splits 1 and 8
3GPP has standardized split 2 (CU/DU split)
ORAN has developed split 7.2 (RU/DU split)
↓
A/D
Option
1
Low-
PHY
High-
PHY
Low-
MAC
High-
MAC
Low-RLC
High-
RLC
PDCP
RRC
Data
Option
2
Option
5
Option
6
Options
7.x
Option
8
Option
3
Option
4
Latency tolerance increases
L1
conventional
fronthauling
L2
L3
conventional
backhauling
CoMP
HARQ
Bandwidth increases with user traffic
Bandwidth PHY dependent
RU
xHauling
DU
CU
ORAN
split
3GPP
split
Notes: To enable resource sharing and delay reduction
we can do some portion of the L1/L2/L3 processing locally
For example, after the FFT we only need active subcarriers, < 50%

## Slide 25: Units and interfaces
Using intermediate split options decomposes the BBU into
Central Unit
Distributed Unit
Radio Unit
Possible decompositions:
RU+DU+CU (no splits)
RU+DU – CU (one split)
RU – DU+CU (one split)
RU – DU – CU (two splits!)
F2
fronthaul
DU
CU
F1
midhaul
RU
DU
NG
backhaul
5GC
F1
midhaul
F2
fronthaul
RU
RU
RU
RU
RU

## Slide 26: Why split 2 and not 1?
Why did 3GPP prefer to standardize split 2 over conventional backhaul ?
DU close to antenna handles time critical functionalities
  scheduling
  retransmission
Many DUs but few CUs
  reduces cost
  facilitates densification
  simplifies management
  increases security
Centralized CU handles pool-able functionalities
  enables hoteling and use of resources in the cloud
  since PDCP and Xn interfaces are in the CU
    end-end encryption (terminated in PDCP in CU)
    minimal in-network connectivity
    optimized dual connectivity (delay-less CoMP) and handoff

## Slide 27: Why 7.2 and not 8 (CPRI)?
Why did ORAN prefer 7.2 over conventional (CPRI) fronthaul ?
Split 7.2 is a packet interface
which can be transported using eCPRI over Ethernet links
Conventional fronthaul data rates become impractical for 5G
and while split 7.2 still represents the air interface (not user traffic)
its data-rate scales with actual usage, not only with system bandwidth!
  While 4G had system bandwidths up to 20MHz
  5G has more options
      for RF bands under 6 GHz
        5, 10, 15, 20, 25, 30, 40, 50, 60, 70, 80, 90, 100 MHz
      for RF bands above 6GHz
        50, 100, 200, 400 MHz (and higher rates will come later)
  Bit-rate > 2 BW Nbits/sample Nsectors NMIMO (> due to overhead and coding)
    with 400 MHz, 16 bits, 3 sectors, 16 MIMO this exceeds 614 Gbps !
The Low-PHY functionality is amenable to hardware

## Slide 28: eCPRI
Traditional fronthaul (split 8) utilizes a proprietary Constant Bit Rate physical layer
such as the Common Public Radio Interface
other splits use packet interfaces, in particular split 7.x uses the evolved CPRI protocol
eCPRI runs over UDP/IP or directly over Ethernet (EtherType AEFE)
between eCPRI Radio Equipment and an eCPRI Radio Equipment Controller
An eCPRI packet contains multiple eCPRI messages
each consisting of a 4-byte eCPRI Common Header and a payload of up to 64K bytes
The payload contains user plane, OAM, control, and synchronization data
8 message types are defined:
  0 IQ Data (for split 8)
  1 Bit Sequence (for split 7.x)
  2 Real-Time Control Data (information on how to process the following message)
  3 Generic Data Transfer
  4 Remote Memory Access (read/write specific peer memory location)
  5 One-way Delay Measurement
  6 Remote Reset
  7 Event Indication

## Slide 29: CRAN, CRAN, and vRAN
Already in 4G it sometimes made sense
to have one (remote) BBU serve many base-stations
The fronthaul links now need to be much longer (not at the base of the tower!)
but processing mandates strict limits on the round-trip delay
and thus on the fronthauling distance (e.g., 20 km for LTE)
This architecture is called Centralized RAN (CRAN)
and was first promoted by China Mobile in 2010
in order to improve scaling of the world’s largest mobile network
Using load-balancing/resilience techniques developed for cloud computing
may allow a central site to service 100s of RRHs
This is called BBU Hoteling or Cloud RAN (also CRAN)
If we are already using cloud techniques
we may implement at least some of the BBU functionality in software
(e.g., packet processing, control functionality)
running as virtual machines inside a Data Center
This architecture is called Virtualized RAN
DU
CU
DU
DU

## Slide 30: Integrated Access Backhaul
Due to cell densification, fiber xHaul will be prohibitively expensive
Use of cellular bands/techniques for xHaul was introduced in R10 (LTE relaying)
but becomes practical with 5G’s mmWave bands
IAB transports midhaul (F1) traffic over a QoS enabled, multi-hop IP network
Topology adaptation changes multi-hop path as needed
Starting with R16 DU and MT may use same band (in-band IAB)
  with time, frequency, or space (multi-beam MIMO) multiplexing
UE – IAB node – IAB node – … – IAB donor
  first IAB node terminates UE’s
    HARQ for fast ARQ
    RLC for optimal scheduling
  IAB donor terminates UE’s PDCP and RRC
    improved handoff decisions
    hiding Dus in network from core improves security
each IAB node consists of DU and Mobile Termination, while the IAB donor consists of DU and CU
Notes: Fiber installation in metro areas estimated at 100 K$ per km
BAP = Backhaul Adaptation Protocol

## Slide 31: Potential 5G RAN transport technologies
The 3 main challenges for the 5G transport segment are:
data-rate
latency
reliability (including very low Packet Loss Ratios)
Multiple transport innovations aid supporting 5G xHaul requirements
10GbE, XGS-PON, NG-PON2
  but 10 Gbps is only satisfactory for initial 5G deployments
25 GbE (802.3by), 1-lane 50 GbE (802.3cd)
100/200/400 GbE (802.3bs)
FlexE
Mobile (Multi-access) Edge Computing
Synchronization (SyncE, IEEE 1588, DGM)
Network slicing
Time Sensitive Networking (and Deterministic Networking)
Frame Replication and Elimination (IEEE 802.1CB)
high data rates
low latency
ultra high reliability

## Slide 32: Slicing, again
Slicing is not only about dynamically separating transport flows
The decomposition of the gNB and virtualized functions
play an essential role in network slicing
A slice that requires a definitive response within a short time
needs edge computation which is only possible after the PDCP in the CU
and probably needs edge computation (MEC)
A slice that serves video can benefit from local breakout and CDN
voice + browsing
Massive IoT
video
V2X
DU
CU
CORE
DU+CU
CDN
MEC
DU+CU
V2X AF
V2X server
DU
AMF
UPF
Video server
transport
cloud
UPF
CU
other
networks
vFW

## Slide 33: Implementing slicing
Slicing must be end-to-end - both RAN and core network must support slicing
Slicing requires programmability, flexibility, and modularity
in order to create multiple virtual networks over a common network
Different slices can be labeled using VLAN ID, VXLAN, IPv6 flow label, DSCP
but a slice is different from a separate physical network or a VPN
because of dynamic set-up / release requirements
and separate management
SDN techniques (network softwarization) are used to achieve slicing
APIs provided to specify requirements
service definition may include NFV/MEC elements
  particularly useful for ultra low latency cases
use of global orchestrator
  for rapid yet highly optimized slice creation

## Slide 34: SDN and NFV for 5G
Software Defined Networking or Segment Routing
and
Network Functions Virtualization or
are widely considered to be essential technologies for 5G
Slicing depends on SDN to be dynamic, obey constraints, efficient, and end-to-end
Mobile (Multi-access) Edge Computing depends on NFV to dynamic place functionality where needed
SDN advocates replacing standardized networking protocols
with centralized software applications
that configure whitebox switches in the network
SR achieves SDN-like control over packet forwarding by adding routing information to packet headers
NFV advocates replacing hardware network elements
with software running on whitebox servers
that may be housed in data-centers or POPs or cell-sites

## Slide 35: Source routing is evil
The IP suite (RFCs) provides a mechanism called Source Routing
IPv4 source routing options (Loose SR, Strict SR)
IPv6 type 0 routing header extension (Rh0)
which inserts sequences of router addresses into packet headers
Yet there are major problems with source routing
complicated processing for core routers
DoS attack – attacker forces packets to traverse selected routers, thus overloading them
amplified DoS attack – attacker forces packet to oscillate between 2 selected routers
infiltration attack – attacker bypasses ACLs by forwarding through a permitted waypoint
The IETF has not yet completely deprecated it
but highly recommends that it be disabled
Core Internet routers drop packets with options
(Linux kernels no longer process Source Routing)

## Slide 36: Safe policy-based routing
But without Source Routing, how can we achieve policy based routing?
There are 2 alternatives
Software Defined Networking
SDN give the network administer full control over routing
particular flows can be configured to traverse arbitrary paths
But SDN
requires relatively large architectural changes
risks attacks (and plain bugs) at control plane level
Segment routing is similar to Source Routing, but
the path is specified by an ingress router, not by the source host
thus blocking Source Routing attacks (unless a router is compromised)

## Slide 37: MPLS-based Segment Routing
MPLS forwards packets using a simple universal paradigm
read ToS Label
look up label in LFIB
perform label stack operation (swap, push, pop) in NHLFE
forward packet according to NHLFE
In regular MPLS networks
most of the time the label stack operation is swap
pop is used by egress LERs and FRR
MPLS segment routing reuses the standard MPLS mechanism
ingress LER inserts an entire stack of labels, one per hop
each LSR pops a label revealing the next hop
MPLS SR doesn’t require LDP or RSVP-TE (but extends the IGP)

## Slide 38: MPLS Segment Routing example
Ingress LER inserts label stack with 3 labels : A (ToS), B, C (BoS)
1st LSR reads A, pops label, forwards over link for A
2nd LSR reads B, pops label, forwards over link for B
3rd LSR reads C, pops label, forwards over link for C
desired path
label = A
ingress LER
egress LER
label = B
label = C
A
B
C
ToS
BoS
B
C
C
1
2
3

## Slide 39: Synchronization
Frequency and time accuracy requirements are defined
to assure efficient and proper functioning of the air interface
5G RAN timing requirements
are stricter, especially for fronthauling (which uses packet based eCPRI instead of CBR CPRI)
When distributing timing over packet networks for 5G using IEEE 1588, ITU defines
Enhanced Primary Reference (Time) Clock (ePRC, ePRTC)
Telecom Grand Master Clock (T-GM)
Telecom Boundary Clocks (T-BC)
Telecom Slave Clocks (T-TSC)
ITU introduced two new T-BC accuracy levels for 5G - classes C and D
  Class A (up to 10 clocks, ±1.5µs E2E) 100 ns Time Error
  Class B (up to 20 clocks, ±1.5µs E2E) 70 ns Time Error
  Class C (up to 20 clocks, ±130ns E2E) 30 ns filtered Time Error
  Class D (long chains, FlexE, FlexO) 5 ns filtered Time Error

## Slide 40: 5G Core Network

## Slide 41: Mobile core networks
Like all core networks, the mobile core handles transport of user data, with
very high data rates
relatively small number of network elements and links
relatively stable environment
Mobile core networks were originally circuit switched (SDH)
but have migrated to packet switching
The mobile core network is more like a PSTN core than an Internet AS core since it supports:
voice traffic (at least until 4G)
user (not necessarily true end-user) management
  mobility management (tracking where users are)
  user profile, home location
  authentication and registration
  billing (charging)
session management (call establishment, management and termination)
lawful interception (CALEA)
QoS (network neutrality may not be relevant for mobile)

## Slide 42: Architectures from 3G to 5G
3G data the Nb+RNC connect to the SGSN and GGSN
SGSN and GGSN handle both data and control
4G Nb+RNC were unified into the eNB
eNB connects to S-GW and P-GW
Mobility management was separated
4G CUPS (R14) separates into UPF and CPFs
S-GW-C and S-GW-U, P-GW-C, P-GW-U
5G
decomposes the MME into AMF and SMF
unifies all user plane functions (S-GW-U and P-GW-U) into the UPF
unifies S-GW-C, P-GW-U and MME session management into SMF
reorganizes functions as micro-services

## Slide 43: Upgrading the core
5G service and network requirements
necessitate a fundamental change to the core architecture
Some 4G network cores presently support 10s of millions of subscribers
5GC will need to support many more subscribers and sessions
The only technology proven to scale up to such sizes is cloud computing
3GPP has defined a new 5G Core architecture
that uses a cloud-native Service Based Architecture (SBA)
with modular Network Functions instead of Network Elements (boxes)
NFs can be hardware or (virtual) software – even VMs in a cloud
NFs are more atomic for improved scaling
NFs in control plane enable authorized functions to directly access services
reference points are defined between NFs, not Network Elements
single interface to NF rather than interface between every two NFs
use of Representational State Transfer (stateless, client-server, with CRUD operations) principles

## Slide 44: Simplified 5G core – SBA
The new core’s Service Based Architecture is based on Network Functions – not Network Elements (boxes)
NF can be hardware or (virtual) software – even software hosted in the cloud
core NFs can be located anywhere – even near the antenna
to enable scaling, core NFs are designed as micro-services connected using function chaining
the core utilizes a unified database and single authentication server
The core NFs are interconnected via a logical bus (every NF can communicate with every other NF)
and the Network Repository Function allows every NF to discover the services offered by other NFs
SBA
SBIs
NFs

## Slide 45: UPF
The User Plane Function performs all the user plane functions
handled in 4G by S-GW, P-GW, and TDF, including:
anchor for mobility
connection to external data networks (e.g., Internet)
optionally Firewall and Network Address Translation (NAT) functions
packet queuing
packet routing and forwarding
packet inspection (optionally DPI), classification, QoS handling
policy enforcement
packet marking
lawful intercept
traffic usage statistics collection and reporting
IPv4 ARP and IPv6 neighbor solicitation

## Slide 46: AMF and SMF
The 4G MME has 2 distinguishable functions
access/mobility management
session management
A single RRC message usually performs both access and session attaches!
But a single UE can simultaneously participate in multiple sessions
In 5G the access/mobility and session management are separated into micro-services
the AMF performs the access and mobility functions
that were handled by the 4G MME, S-GW-C and P-GW-C
the SMF performs the session management functions
that were handled by the 4G MME, SGW-C, and PGW-C
The AMF and SMF are stateless, but often need access to state information
For this purpose there is a secure and resilient Unified Data Management function
that provides data storage, e.g., the UE’s subscription data (like 3G HLR and 4G HSS)
The Authentication Server Function performs authentication based on keys stored in the UDM

## Slide 47: Slicing, yet again
A single UE can participate in more than one slice
Each UE is served by a single AMF
but each slice from a UE has its own SMF and UPF
The AMF can use a Network Slice Selection Function to select the needed network slices
based on Network Slice Selection Assistance Information from the UE
UE
AMF
UPF
UPF
SMF
SMF
DN
DN

## Slide 48: AFs and capability exposure
In order to enable new service types and integrate with vertical industries
5G core functionalities will be made available to 3rd parties, including
    application service providers
    value added service providers
    end-users (vehicles, factories, smart cities, etc.)
5G learned from MEC the importance of capability exposure
and defined the Network Exposure Function
which is similar to the core’s own NRF
The NEF, like MEC’s Mobile Edge Platform, can be queried via an API
to discover available services
Capability exposure is a very common feature of web-based services
and the modern way of providing such services is via RESTful APIs

## Slide 49: The End