## Slide 1: MPLS a mini-course
Your Network’s Edge
Presented by:
Yaakov (J) Stein
CTO
July 2018

## Slide 2: Course Outline
Forwarding and routing
Forwarding Equivalence Classes
Problems with IP routing
Label Switching
MPLS
MPLS control plane(s)
LDP and BGP – in-depth slides
MPLS-TP (including the GACh, OAM, APS)
Pseudowires
Some PW-specific mechanisms
PWE3 control protocol
TDM PWs
Ethernet PWs (and VPWS, VPLS)
Other PW types

## Slide 3
Forwarding and routing

## Slide 4: Buses (e.g., Ethernet LANs)
The simplest way to interconnect hosts is via a bus
each message is sent to all possible recipients
all receivers check the message’s destination address
if message destination address does not match receiver’s address
  message ignored (except in promiscuous mode)
if message destination address matches receiver’s address
  message received
not for me
not for me
for me!!
not for me
not for me
not for me
not for me

## Slide 5: Packet Switched Networks
Bus topologies are only practical for very small networks (LANs)
Ethernet fixes this by defining a bridge that can filter traffic
Packet Switched Networks contain Network Elements (routers, switches)
that perform two distinct functions :
forwarding (data plane component)
routing (control plane component)
From the forwarding point of view
  there are two different types of Packet Switched Network:
ConnectionLess (e.g., IP)
Connection Oriented (e.g., ATM, MPLS???)

## Slide 6: Connectionless Forwarding
A PSN is connectionless (CL) if
no setup is required before sending a packet
each router makes an independent forwarding decision
packets are self-describing
packet inserted anywhere will be properly forwarded
Note:
  the address must have global significance
  IP only runs between routers
    it relies on a L2 protocol (Ethernet, PPP) from router to host
CL forwarder (router)
host
host

## Slide 7: IP Routing
Distance Vector (Bellman-Ford), e.g. RIP
  send <addr,cost> to neighbors
  routers maintain cost to all destinations
  need to solve “count to  problem“
Path Vector, e.g. BGP
  send <addr,cost,path> to neighbors
  similar to distance vector, but w/o “count to  problem“
  like distance vector has slow convergence*
  doesn’t require consistent topology
  can support hierarchical topology => exterior protocol (EGP)
Link State, e.g. OSPF, IS-IS
  send <neighbor-addr,cost> to all routers
  determine entire flat network topology (Dijkstra’s algorithm)
  fast convergence*, guaranteed loopless => interior routing protocol (IGP)
*convergence time is the time taken until all routers work consistently
before convergence is complete packets may be misforwarded, and there may be loops

## Slide 8: IP Forwarding
IPv4 and IPv6 are CL PSNs
what field(s) are parsed for forwarding?
field used depends on application
regular: use longest destination prefix match
ToS: use longest destination prefix match + exact match on ToS
multicast: use longest/exact match on source/group address
how is forwarding performed?
forwarding algorithm depends on routing algorithm!
for Distance Vector - forward by cost
for Path Vector - forward by cost and path
for Link State - Dijkstra’s algorithm

## Slide 9: Connection Oriented Forwarding
each forwarder maintains forwarding table (or table per input port)
control component:
route must be set-up (table must be updated) before data sent
set-up may be manual or signaled
once route no longer needed it should be torn-down
input ports
output ports
1
2
3
4
5
1
2
3
4
5
CO forwarder (switch)

## Slide 10: CO Forwarding
CO addresses need not have global significance
by using locally defined addresses:
addresses are smaller in size
lookup is faster
no need for global allocation mechanism (purchasing, DHCP)
no need to maintain global database
L2 forwarding is based on address read and swap
Note:
when addresses are purely local
  CO forwarding is often called called L2 (link layer) forwarding
12
17
23

## Slide 11: CO Forwarding Table
input port | input address | output port | output address
1 | 21 | 2 | 21
1 | 37 | 1 | 21
2 | 12 | 5 | 12
3 | 5 | 5 | 12
4 | 15 | 3 | 37
Note: never really have an input port column
either it is irrelevant (CO address is per switch not per input port),
or if needed (e.g. ATM) we keep separate tables per input port (more efficient)

## Slide 12: CO Control Plane
For CO forwarding we need to find and set-up a path
These can be done via
  manual configuration (strict explicit route)
  use routing protocols (e.g. P-NNI for ATM)
CO routing protocols search for a global path
  hence they can guarantee global characteristics (SLA)
  pure CL routing can not guarantee path QoS
Information source usually knows the desired characteristics
  so usually use source routing
  can force route to go through specific forwarders (loose explicit route)
  can reject forwarders that can not guarantee needed characteristic
  can request resource reservation in selected forwarders

## Slide 13
Forwarding Equivalence Classes

## Slide 14: Forwarding Equivalence Classes
Simple routers typically search for IP prefix
and immediately perform forwarding
e.g., the UNIX router LSDB Dijkstra returns forwarding information
Today’s routers decouple (as much as possible)
routing protocol(s) (building LSDB, RIBs)
building FIB
packet parsing/classification/search
forwarding decision
All packets that are to be forwarded in the same way
are grouped together to form a FEC
Thus the search algorithm returns a FEC label
and then a second lookup is performed
to find the forwarding information

## Slide 15: Equivalence Classes
In set theory we define an Equivalence Class as:
set of elements that can be considered equivalent for some purpose
Theorem
any equality relation (e.g., common features)
    divides elements into non-overlapping equivalence classes
Example:
equality modulo 3 for positive integers
A = B (mod 3) if and only if A = 3a + c and B = 3b + c
or (A-B) divides by 3
there are three equivalence classes :
{ 0, 3, 6, 9, 12, … }
{1, 4, 7, 10, 13, …}
{2, 5, 8, 11, 14, … }
note that every positive integer is in exactly one EC
reflexive: a ~ a
symmetric : a ~ b  b ~ a
transitive : a ~ b and b ~ c  a ~ c

## Slide 16: Forwarding Equivalence Classes
A FEC is the set of all packets that are to be treated in the same way
By the theorem every packet belongs to one unique FEC
So the router’s forwarding job is now :
parse packet
search and classify packet as belong to a particular FEC
forward based on FEC’s forwarding information
Packets in the same FEC should follow the same path
but in IP this is not directly enforced
since each successive router reclassifies the packet’s FEC
If the router could insert information into the packet
informing the next router of its FEC
this would save a lot of processing at the following routers
the subsequent forwarding would be CO instead of CL
Unfortunately, this is impossible (without label switching)!

## Slide 17: FECs
What constitutes a FEC ?
For plain IP routing
  all packets w/ same destination IP prefix
  that prefix being the longest in the routing table
We would like more control
coarsest granularity
  all packets with a destination address
    served by a given router
finest granularity
  all packets from given source socket
    to given destination socket
    with specified handling requirements
IP address
IP prefix
IP prefix + ToS/DSCP

## Slide 18
Problems with IP routing

## Slide 19: Problems with IP routing
IP is great – but not perfect !
scalability
  router table overload
  routing convergence slow-down
  increase in queuing time and routing traffic
  problems specific to underlying L2 technologies
hard to implement load balancing
QoS and Traffic Engineering
problem of routing changes
difficulties in routing protocol update
lack of VPN services

## Slide 20: Scalability
When IP was first conceived, scalability was not a problem
but as number of hosts increases, routing shows stress
Simplistic example
  N hosts
  each router serves M hosts
  each router entry takes a bytes
hence
  router table size a N ~ N
  N / M ~ N routers (more routers => slower convergence)
  packet processing time* ~N (since have to examine entire table)
  ~N routers send to ~N routers tables of size ~N
  so routing table update traffic increases ~N 3 (or ~N 4 )
* IP routing requires 1000s of clocks per decision

## Slide 21: L2 Backbone Doesn’t Help!
Instead of expensive and slow IP routers
  operators once used faster and cheaper ATM switches in core
but this actually makes things worse!
ATM switches are transparent to routers
ATM switches do not participate in IP routing protocols
so every IP router becomes logically adjacent to every other
  and we need ~ N2 ATM VCs !
If only the ATM switches could understand IP routing protocols…
Unfortunately, this is impossible (without label switching)!
ATM
Classical IP over ATM

## Slide 22: Load Balancing
were C,D,E, and F ATM switches there would be no problem
  (1Gb over ACDG, 500Mb over BCEFG)
with standard IP hop-count cost function, all traffic over CDG
  resulting in 1.5Gb there (congestion) and CEFG idle
with administrative cost on CDG we can force all the traffic to CEFG
  even worse congestion !
finally with administrative cost and Equal Cost MultiPath (ECMP)
  750 Mb over CDG and CEFG, link EF is still congested !
solution requires traffic engineering
It would be great if we could add TE to IP
Unfortunately, this is hard (without label switching)!
A
B
C
D
E
F
G
traffic from A to G = 1Gb
traffic from B to G = 500Mb
all links 1Gb except EF - 500 Mb
1
0.5
“fish diagram”

## Slide 23: QoS and TE
CL networks can not guarantee path QoS
you can’t reserve resources for handling a packet
since you don’t know where the packet is going to go !
But other protocols in the IP suite can help
TCP adds CO layer compensating for loss and mis-ordering
but that is correcting for mishaps that already occurred
IntServ (RSVP) sets up path with reserved resources
but that modifies IP so much that it never caught on
DiffServ (DSCP) prioritizes packets
but that doesn’t provide any guarantees
So IP network managers use network engineering
  throw BW at the problem
rather than traffic engineering
  optimally exploiting the BW that is there
TE is great, but not possible in IP (without label switching)!

## Slide 24: Routing Changes
IP routing is satisfactory in the steady state
  but what happens when something changes?
Any change in routing information
  (new router, router failure, new inter-router connection, etc)
necessitates updating of tables of all routers
Convergence is generally slow
A change in the routing protocol is even worse
  (e.g. Bellman-Ford to present, classed to classless, IPv4 to IPv6)
since it necessitates upgrade of all router software
Upgrades may have to be simultaneous
What we need is a more complete separation
of forwarding from routing functionality (ForCES)
Unfortunately, this separation is only recently starting to appear!

## Slide 25: VPN Services
IP was designed to interconnect networks
  not to provide VPN services
When we connect routers from different customers
the security isolation is weak
LANs may use non globally unique addresses (present solution - NAT)
Interconnect may entail complex provider-customer relationships
192.115.243.19
192.115.243.19
192.115.243.79
IP

## Slide 26
Label Switching

## Slide 27: Solution - Label Switching
label switching adds the strength of CO to CL forwarding
label switching involves three stages:
  routing (topology determination) using L3 protocols
  path setup (label binding and distribution) perhaps using new protocol(s)
  data forwarding
label switching the solution to all of the above problems
  speeds up forwarding
  decreases forwarding table size (by using local labels)
  enables support for QoS and arbitrary granularity FECs
  load balancing by explicitly setting up paths
  complete separation of routing and forwarding algorithms
    no new routing algorithm needed
    but new signaling algorithm may be needed
CO forwarder (switch)
CL forwarder (router)
LSR

## Slide 28: Where is it?
Unlike TCP, the label switching CO layer lies under the CL layer
If there is a broadcast L2 (e.g. Ethernet), the CO layer lies above it
Hence, label switching is sometimes called layer 2.5 switching
higher layers
layer 3 (e.g. IP)
label switching (layer 2.5)
layer 2 (e.g. ethernet)
physical layer
shim header

## Slide 29: Labels
A label is a short, fixed length, structure-less address
The following are not labels:
telephone number (not fixed length, country-code+area-code+local-number)
Ethernet address (too long, note vendor-code is not meaningful structure)
IP address (too long, has fields)
ATM address (has VP/VC)
Not an explicit requirement, but normally only local in significance
Label(s) added to CL packet, in addition to L3 address
Layer 2.5 forwarding
requires a flow setup process and signaling protocol
may find a different route than the L3 forwarding
  and thus support higher granularity FECs
may be faster than L3 forwarding

## Slide 30: Label Switching Architecture
Label switching is needed in the core, access can be L3 forwarding*
Core interfaces the access at the edge (ingress, egress)
LSR router that can* perform label switching
LER LSR with non-MPLS neighbors (LSR at edge of core network)
LSP unidirectional path used by label switched forwarding (ingress to egress)
* not every packet needs label switching
L3 router
L3 router
Label Edge Router
Label Edge Router
Label Switched Routers
L3 link
L3 link
Label Switched Path
ingress
egress
downstream direction
upstream direction

## Slide 31: Label Switched Forwarding
LSP needs to be setup before data is forwarded
  and should be torn down once no longer needed
LSR performs
  label switched forwarding* for labeled packets
label space may be
  per platform (unique to LSR) or
  per port (unique to input interface - like ATM)
LSRs optionally support L3 forwarding for unlabeled packets
ingress LER
  assigns packet* to FEC
  labels packet
  forwards it downstream using label switching
egress LER
  removes label
  forwards packet using L3 forwarding
  exception: PHP (discussed later)
* once packet is assigned to a FEC and labeled
no other LSR looks at the L3 headers

## Slide 32: Hierarchical Forwarding
Many networks use hierarchical routing
  decreases router table size
  increases forwarding speed
  decreases routing convergence time
telephone numbers
Internet URLs
ATM
Ethernet/802.3 address space is flat (even though written in byte fields)
Country-Code Area-Code Exchange-Code Line-Number
972 2 588 9159
host … SLD TLD
myrad . rad . co . il
VP
VC
VC
VC

## Slide 33: IP Routing Hierarchy
IPv4
  originally flat space (1st come - 1st) until router tables exploded
  then 3 classes
  now CIDR <RFC1519>
AS=Autonomous System
IP exploits hierarchy by employing interior/exterior routing protocols
IP can even support arbitrary levels of hierarchy
  by advertising aggregated addresses
but the exploitation is not optimal
ASany host
0 net7 host24
A
10 net14 host16
B
110 net22 host8
C
AS12
AS13
AS13
AS14

## Slide 34: Label Stacks
since labels are structure-less, the label space is flat
label switching can support arbitrary levels of hierarchy
  by using a label stack
label forwarding based only on top label
before forwarding, three possibilities (listed in NHLFE) :
  read top label and pop
  read top label and swap
  read top label, swap, and push new label(s)
top label
another label
yet another label
bottom label

## Slide 35: Example Uses of Label Stack
Example applications that exploit the label stack
  fast rerouting
  VPNs
  PWE3
  Segment Routing

## Slide 36: Fast ReRoute
IP has no inherent recovery method (like SDH)
  in order to ensure resilience we can provide local detours
to reroute quickly we pre-prepare labels for the bypass links
10
11
12
swap
swap
swap
+
push
pop
swap
swap
11
13
11
14
11
from here on
no difference! *
when link is down
change fwd table
protection LSP
* label space per LSR
not per input port

## Slide 37: Label Switched VPNs
Key
C Customer router
CE Customer Edge router
P Provider router
PE Provider Edge router
customer 2 network
customer 1 network
C
C
C
C
C
C
C
CE
C
C
C
C
C
CE
P
PE
P
P
CE
PE
P
P
CE
provider network
customer 2 network
customer 1 network
AC
AC
AC
AC

## Slide 38: Label Switched VPNs (cont.)
If customers 1 and 2 use overlapping IP addresses
C-routers have inconsistent tables
Ingress PE (LER) inserts two labels
Only PEs know about customers
P-routers see only the label of the egress PE-router
  P-routers don’t see IP addresses, so there is no ambiguity
  they don’t know about VPNs at all
  no need to understand customer configuration
  smaller tables
  no rerouting if customer reconfigures
Ingress PE router only knows about CE routers
  no need to understand customer configuration (C-routers)
egress PE
egress CE
IP header
payload

## Slide 39: PWE3
native
service
A tunnel may contain many PWs
native
service
PE
router
P router
P router
P router
PE
router
P router
tunnel label(s)
PW label
PW control word
payload
PW label is not a real label
it just identifies native service instance
P routers don’t know about PWs
just how to get to egress PE
With MS-PWs, PW labels becomes real labels

## Slide 40: Segment Routing
Sometimes we need to force a packet to travel a particular path
for example, in order to have it inspected or manipulated
IP had a source routing option (specified by end host)
but it raised security concerns (RFCs 5095, 7126)
and was deprecated
MPLS label stacking provides a natural alternative
source specification is specified by the ingress router
requires deep label stacks
The principle is simple (this is only one way to perform SR)
IGP advertises label for each adjacency (segment)
ingress router inserts a label for each segment to be traversed
each router pops a label (or leaves it w/o swapping)
packet arrives at egress router its label stack depleted
SID 1
SID 2
SID n
payload
...

## Slide 41
MPLS
Label (20b) TC(3b) S(1b) TTL (8b)

## Slide 42: MPLS history
Many different label switching schemes were invented
Cell Switching Router (Toshiba) <RFC 2098,2129>
IP Switching (Ipsilon, bought by Nokia) <RFC 2297>
Tag Switching (Cisco) <RFC 2105>
Aggregate Route-based IP Switching (IBM)
IP Navigator (Cascade bought by Ascend bought by Lucent)
so the IETF decided to standardize a single method
This method is called MPLS

## Slide 43: MPLS
Of all possible label switching technologies
what is special about MPLS ?
multiprotocol - from above and below
label shim header (label may also be in legacy L2)
single forwarding algorithm, including for multicast and TE
control plane consisting of
  topology discovery via IP routing protocols
  and label distribution via
    piggybacked on existing routing protocols
    via the Label Distribution Protocol
    via RSVP-TE (and historically CRLDP) for Traffic Engineering

## Slide 44: MultiProtocol Label Switching
IPv4 IPv6 MPLS PWs
MPLS
Ethernet SDH/OTN legacy
(ATM, FR)
(GFP, HDLC)
(everything)

## Slide 45: MPLS Shim Header
when a shim header is used, its format is:
Label there are 220 different labels (+ 220 multicast labels)
Traffic Class (ex-EXP)
was CoS in Cisco Tag Switching
may influence packet queuing
QoS may be via E-LSP or L-LSP
Stack bit S=1 indicates bottom of label stack
TTL decrementing hop count
used to eliminate infinite routing loops
and for MPLS traceroute
  generally copied from/to IP TTL field
S=0 top label
S=0 another label
S=0 yet another label
S=1 bottom label
Special (reserved) labels
  0 IPv4 explicit null
  1 router alert
  2 IPv6 explicit null
  3 implicit null
  7 entropy label indicator
  13 MPLS-TP GAL
  14 Y.1711 OAM label
Label (20b) TC(3b) S(1b) TTL (8b)

## Slide 46: Single Forwarding Algorithm
IP uses different forwarding algorithms
  for unicast, unicast w/ ToS, multicast, etc.
LSR uses one forwarding algorithm (LER is more complicated)
  read top label L
  consult Incoming Label Map (forwarding table) [Cisco terminology LFIB]
  perform label stack operation (pop L, swap L - M, swap L - M and push N)
  forward based on L’s Next Hop Label Forwarding Entry
NHLFE contains:
  next hop (output port, IP address of next LSR)
    if next hop is the LSR itself then operation must be pop
    for multicast there may be multiple next hops, and packet is replicated
  label stack operation to be performed
  any other info needed to forward (e.g. L2 format, how label is encoded)
ILM contains:
  a NHLFE for each incoming label
  possibly multiple NHLFEs for a label, but only one used per packet
for TTL processing see RFC 3443

## Slide 47: LER Forwarding Algorithm
LER’s forwarding algorithm is more complex
check if packet is labeled or not
if labeled
  then forward as LSR
  else
    lookup destination IP address in FEC-To-NHLFE Map
    if in FTN
      then prepend label and forward using LSR algorithm
      else forward using IP forwarding
[Cisco terminology LIB]
LER
LSR
IP
router
pure IP link
MPLS link

## Slide 48: MPLS flavors
We now distinguish four flavors of MPLS :
plain vanilla MPLS (usually with LDP, perhaps with RSVP-TE for FRR)
not true CO – pinned to route not to NEs
used in Internet core
MPLS for L3VPN services (RFC 4364 <ex-2547> using BGP)
used to deliver VPN services to businesses
MPLS-TE (currently with RSVP-TE)
true CO with resource reservation
used when SLA guarantees given
MPLS-TP (usually with management system, can use RSVP-TE)
does not assume the existence of IP forwarding plane
does not require control plane – can work with management OSS
implements OAM and APS functionality

## Slide 49
Special mechanisms

## Slide 50: Penultimate Hop Popping
the egress LER E also may have to work overtime:
  read top label
  lookup label in ILM
  find that in NHLFE that the label must be popped
  lookup IP address in IP routing
  forward to CE using IP forwarding
we can save a lookup (and the first 3 steps) by performing PHP
but pay in loss of OAM capabilities
penultimate LSR PH performs the following:
  read top label
  lookup label in ILM
  pop label revealing IP address of CE router
  forward to CE using IP forwarding
I
E
PH
CE
IP link
MPLS domain

## Slide 51: Route Aggregation (VC merge)
traffic from both network 1 and network 2 is destined for network 3
scalability advantages
  fewer labels
  conserve table memory
disadvantages
  IP forwarding may be required
  OAM backwards trail is destroyed
E
3
IP link
MPLS domain
1
2
IP link
IP link
12
22
13
23
31
32
net 2
net 3
net 1

## Slide 52: Entropy Labels
Ethernet and IP enable load balancing using LAG and ECMP
which map flows based hashing header fields
MPLS labels have no spare information = entropy
and peeking under the MPLS requires DPI (warning - layer violation)
One approach is to use multiple different labels for the same FEC
but that increases control plane complexity
RFC 6790 defines entropy labels (and RFC 6391 defines a FAT PW)
ingress LER hashes IP header fields as for ECMP
it pushes an entropy label
it pushes the Entropy Label Indicator (reserved label 7)
it pushes the MPLS transport label
RFC 8012 defines ping and traceroute mechanisms
based on entropy labels

## Slide 53: FAT PW and Entropy Labels
The Flow Aware Transport PW label and the entropy label
are never signaled (but their capability is signaled)
are used as key for ECMP-like hashing
packets in a single flow share the same entropy label
are slightly different in format and placement
MPLS label(s)
PW label
FAT label (S=1, TTL=1)
PW Control Word
PW payload
MPLS label(s)
ELI (label = 7, S=0))
Entropy label (TTL=0)
payload
optionally more label(s)

## Slide 54
MPLS control plane
B
13 data
A
I need a label
I allocated 13

## Slide 55: Data and control planes
all IP routing protocols (OSPF, BGP, etc)
procedure to bind label to FEC (label assignment)
protocol to distribute label binding information
procedure to create forwarding table
procedure to label incoming packet
forwarding procedure
  forwarding table lookup
  label stack operations
control plane
user (data) plane

## Slide 56: Label Distribution Protocols
When an LSR creates/removes a FEC - label binding
  it needs to inform other LSRs of its decision
MPLS allows piggybacking label distribution on routing protocols
  protocols already in use (don’t need to invent or deploy)
  eliminates race conditions (when route or binding, but not both, defined)
  ensures consistency between binding and routing information
  only for distance vector or path vector routing protocols (not OSPF, IS-IS)
  not all routing protocols are sufficiently extensible (RIP isn’t)
  has been implemented for BGP-4
MPLS WG invented a new protocol LDP for “plain” label distribution
  messages sent reliably using TCP/IP
  messages encoded in TLVs
  discovery mechanism to find other LSRs
… and extended RSVP to LSPs for QoS - RSVP-TE
New approaches use OpenFlow (SDN) and OSPF (for segment routing)

## Slide 57: LER Architecture
control plane
user (data) plane
IP routing protocols
IP
routing
tables
label binding and distribution protocols
IP
forwarding
table
MPLS
forwarding
table
IP routers
labeling procedure
LSRs
free label table
egress LER
FTN

## Slide 58: All the Tables
FEC table
Free Labels 128-200 presently free
FTN
ILM
NHLFE
FEC | protocol | input port | handling
192.115/16 | IPv4 | 2 | best-effort
FEC | port/label in | port/label out
192.115/16 | 2/17 | 3/137
port/label in | port/label out | next hop | operation
2/17 | 3/137 | 5.4.3.2 | swap

## Slide 59: Binding and Distribution Options
label binding (assignment)
  per port or per LSR label space
  control driven vs. data driven (traffic driven)
  liberal vs. conservative label retention
label distribution (advertisement)
  downstream vs. upstream
  downstream on-demand (dod) vs.
  downstream unsolicited (du)
  independent vs. ordered

## Slide 60: Per Port Label Space
LSR may have a separate label space for each input port (I/F)
  or a single common label space
  or any combination of the two
Separate labels spaces means separate forwarding tables per port
ATM LSR had only per port label spaces (leads to interleave problem)
per port label spaces increases number of available labels
common label space facilitates several MPLS mechanisms (e.g. FRR)

## Slide 61: Control vs. Data Driven
there are two philosophies as to when to create a binding
data-driven (traffic-driven) binding (Toshiba CSR, Ipsilon IP-Switching)
automatically create binding when data packets arrive
  (from first packet?, after enough packets? when tear LSP down?)
control-driven binding (Cisco Tag Switching, IBM ARIS)
create binding when routing updates arrive
  (only update when topology changes? update upon request?)
although not specifically stated in the architecture document
  MPLS assumes control driven binding *
* two implementations of control driven:
  topology-driven (routing tables are consulted)
  control-traffic driven (only routing update messages are used)

## Slide 62: Liberal vs. Conservative Retention
LSR receives “advertisements” (label distribution messages)
from other LSRs
conservative label retention:
  LSR retains only label-to-FEC bindings that are presently needed
liberal label retention
  LSR stores all bindings received (more labels need to be maintained)
using liberal retention can speed response to topology changes
LSRs must agree upon mode to be used
A advertises label
B is previous hop LSR
  but C retains label anyway
later routing change makes C the previous hop
  C immediately can start forwarding
C
A
B

## Slide 63: Downstream vs. Upstream
binding means to allocate a label to a FEC
LSR allocates the label from “free label” pool
Which LSR allocates the label ?
Unicast MPLS uses downstream binding
label allocated by LSR downstream from the LSR that prepends it
label distribution information flows upstream
reverse in direction from data packets
to set up LSP through link from LSR A to LSR B
LSR B binds label 13 to FEC
B advertises label to LSR A
LSR A sends packets with label 13 to B
downstream
13
A
label 13
B

## Slide 64: On-demand vs. Unsolicited
downstream on-demand label distribution:
  LSRs may explicitly request a label from its downstream LSR
unsolicited label distribution:
  LSR distributes binding to upstream LSR w/o a request
  (e.g. based on time interval, or upon receipt of topology change)
LSR may support on-demand, unsolicited, or both
adjacent LSRs must agree upon which mode to be used
LSR A needs to send a packet to LSR B
LSR A requests a label from LSR B
B binds label 13 to the FEC
B distributes the label
A starts sending data with label 13
B
13 data
A
I need a label
I allocated 13

## Slide 65: Independent vs. Ordered
independent binding (Tag Switching)
  each LSR makes independent decision to bind and distribute
ordered binding (ARIS)
egress LSR binds first and distributes binding to neighbors
LSR that believes that it should be the penultimate LSR
  binds and distributes to its neighbors
binding proceeds in orderly fashion until ingress LSR is reached
LSRs must agree upon mode to be used
B sees that it is egress LSR for 192.115.6
B allocates label 13
B distributes label to C and D
C distributes label to E
192.115/16
A
B
D
C
E
13
13

## Slide 66: LDP tasks
A label distribution protocol is a signaling protocol
  that can perform the following tasks:
discover LSR peers
initiate and maintain LDP session
signal label request
advertise binding
signal label withdrawal
loop prevention
explicit routing
resource reservation

## Slide 67: Label Distribution Protocols
Label distribution can be performed using various protocols
There are presently the following options:
Management protocols
LDP
  MPLS-enhanced IP networks
  used as basis for PWE3 control protocol
BGP4-MPLS
  mainly for RFC 4364 VPNs
RSVP-TE
  traffic engineering support
CR-LDP
  constraint based (no longer recommended by IETF)

## Slide 68
LDP and BGP
slides for those who love protocols

## Slide 69: LDP vs. BGP
both use TCP for reliable transport (LDP uses UDP for hellos)
both are hard-state protocols
both use TLV format for parameters
BGP
multiprotocol (IPv4, IPv6, IPX, MPLS)
highly complex protocol
provides routing / label distribution
built-in autodiscovery mechanism
LDP
MPLS only
simpler protocol
only label distribution
no built-in autodiscovery

## Slide 70: LDP
Major focus of the IETF MPLS WG was the design of LDP
based on similar TDP from Cisco
LDP sets up a bidirectional LDP session
  both sides can request or advertise labels
LDP usually uses TCP
  needs reliable transport (e.g. what happens if miss a binding)
  needs in-order delivery (e.g. binding+withdrawal)
  hard to develop new reliable transport protocols
  single acknowledgement timer for session
  piggybacking ACK on data packets
Use UDP for discovery (hello) messages
Periodic keepalive messages (if not received, session terminated)
All messages encoded in TLV (Type Length Value) form

## Slide 71: LDP Setup
Discovery
Hello (UDP)
Session
Initialization (TCP)
Distribution
Label Request (TCP)
Label Distribution (TCP)
Hello (UDP)
Initialization (TCP)

## Slide 72: Discovery Phase
LSR periodically multicast transmits hello to “LDP discovery” UDP port
  to “all routers on subnet” multicast group
  to preconfigured IP address (when not all LSRs on same subnet)
  (extended discovery) “targeted LDP”
LSRs listen on this UDP port for hello messages
Hello message contains:
  hold time
  LSR Identifier
when LSR receives Hello from another LSR
  it opens a TCP connection to that other LSR (if needed)
    or (for extended discovery)
  it unicast transmits a hello back to the other LSR
LDP session can now be established

## Slide 73: Session Initialization
The LSR with higher identifier sends (TCP)
  a session initialization message to the other LSR
session initialization message contains:
  LDP Protocol version
  label distribution and control method
  timer values
  label space ranges
If receiving LSR accepts these parameters
  then it transmits a KeepAlive
  else it transmits a reject
Notes: If one LSR proposes Downstream Unsolicited and the other proposes Downstream on Demand, the rules for resolving this
difference is:
- If the session is for a label-controlled ATM link or a
label-controlled Frame Relay link, then Downstream on Demand
must be used.
- Otherwise, Downstream Unsolicited must be used.
Independent or Ordered Control is LSR (interface) specific – Independent and Ordered can co-exist in the same network

## Slide 74: Distribution Messages
label mapping
  downstream LSR advertisement of a label mapping for a FEC
  two FEC types: host address, IP address prefix
label withdrawal
  reverse of mapping message
  downstream LSR informs upstream LSR
    that it has revoked a previous binding
  upstream LSR can not longer use the label
label release
  upstream LSR informs downstream LSR
    that it no longer needs a binding
  typically when downstream is no longer next hop
    and operating in conservative retention mode
Notes: An LSR may transmit a Request message under any of the following conditions:
1. The LSR recognizes a new FEC via the forwarding table, and the next hop is an LDP peer, and the LSR doesn't already have a
mapping from the next hop for the given FEC.
2. The next hop to the FEC changes, and the LSR doesn't already have a mapping from that next hop for the given FEC.
Note that if the LSR already has a pending Label Request message for the new next hop it should not issue an additional
Label Request in response to the next hop change.
3. The LSR receives a Label Request for a FEC from an upstream LDP peer, the FEC next hop is an LDP peer, and the LSR doesn't
already have a mapping from the next hop.
Note that since a non-merge LSR must setup a separate LSP for each upstream peer requesting a label, it must send a separate
Label Request for each such peer. A consequence of this is that a non-merge LSR may have multiple Label Request messages
for a given FEC outstanding at the same time.

## Slide 75: Request Messages
In dod mode upstream LSR must request binding
Upstream LSR sends label request message when:
  FEC in FEC table
  next hop LSR is LDP peer
  FEC not in forwarding table
  FEC next hop changes
  upstream LSR doesn’t have a mapping from new next hop
  receives FEC label request from upstream LDP peer
  next hop LSR is LDP peer
  upstream LSR doesn’t have a mapping from next hop
Upstream LSR sends label request abort message when:
  upstream LSR needs to revoke request before satisfied
  for example, next hop LSR for FEC has changed

## Slide 76: Notifications
There are two types of notifications:
  error notifications (fatal errors - terminate session)
  advisory notifications (status messages)
LSR sends notification messages when:
  received LDP message with unsupported protocol version
  received LDP message with unknown type
  KeepAlive timer expired
  session initialization fails due to unacceptable parameters
  etc.

## Slide 77: LDP state machine
LSR periodically transmits hello UDP messages
  multicast to “all routers on subnet” group
  targeted to preconfigured IP address
LSRs listen on this UDP port for hello messages
When LSR receives hello from another LSR
  it opens a TCP connection to that other LSR
    or (for extended discovery)
  it unicast transmits a hello back to the other LSR
LSR with higher ID sends session initialization
Other LSR LDP accepts (sends keepalive) or rejects
Informative or keepalive messages sent
3.2

## Slide 78: LDP packet format
version – presently 1
length - PDU length, excluding version and length fields
LDP-ID – identifies label space of sending LDP peer
  LSR-ID(4B) globally unique LSR ID
  label space ID (2B) for per-port label spaces
    (zero for per-platform label spaces)
message TLVs – zero or more message TLVs (see next page)
version
(2B)
length
(2B)
LDP-ID
(6B)
message TLVs
(variable)
header (10B)

## Slide 79: LDP message TLVs
U – unknown message bit
    if message type unknown to receiver
    U=0 – receiver returns notification to sender
    U=1 – receiver silently ignores
length - message length, excluding type and length fields
message-ID – unique ID for message (for matching with returned notification)
If there are mandatory parameters
they must appear in a specific order
optional parameters may appear in any order
type
(15b)
length
(2B)
message-ID
(4B)
mandatory
parameter
TLVs
(variable)
optional parameter
TLVs
(variable)
U

## Slide 80: All LDP message types
Hello (0x0100)
Initialization (0x0200)
KeepAlive (0x0201)
Notification (0x0001)
Address (0x0300)
Address Withdraw (0x0301)
Label Mapping (0x0400)
Label Withdraw (0x0402)
Label Request (0x0401)
Label Release (0x0403)
Label Abort Request (0x0404)

## Slide 81: LDP parameter (sub)TLVs
U – unknown message bit
  if message type unknown to receiver:
    U=0 – receiver returns notification to sender
    U=1 – receiver silently ignores
F – forward unknown message bit
  if U=1 and message type unknown to receiver
    F=0 – do not forward
    F=1 – forward
type - TLV type (FEC TLV, label TLV, address list TLV, hop count TLV, path vector TLV, status TLV )
length - length of value field in bytes
type
(14b)
length
(2B)
value
U
F

## Slide 82: FEC TLV
there may be more than one FEC element for mapping messages only
the FEC elements are not themselves TLVs (no length needed), instead
  wildcard FEC (0x01)
  prefix FEC (0x02) + address family (IPv4, IPv6, Ethernet, E.164, etc.) + prefix length in bits + prefix
  host address FEC (0x03) + address family + length + address
type (2B)
U=0 F=0 type=0x0100
length (2B)
FEC element 1
…

## Slide 83: Generic Label TLV
this is the generic label TLV
there are also special label TLVs for ATM and FR based MPLS
type (2B)
U=0 F=0 type=0x0200
length (2B)
label (20 bits)

## Slide 84: Status TLV
Status TLVs : mandatory parameters in notification messages
optional parameters in other messages
U=0 when status in notification message, else U=1
E - fatal error bit E=1 for fatal error E=0 for advisory notification
the two F bits are equal and have the normal meaning
status code data = 0 means success
message ID - the message to which the status refers
message type - the message type to which the status refers
type (2B)
U F type=0x0300
length (2B)
status code data (30b)
message ID (32b)
E
F
message type (16b)

## Slide 85: Example full message - label mapping
mapping message
type = 0x0400
length=24
(2B)
message-ID
(4B)
U=0
FEC TLV (2B)
U=0 F=0 type=0x0100
length=8 (2B)
prefix FEC element (8B)
type = 0x02 family=1(IPv4) prefix-length=16 prefix=192.115/16
label TLV (2B)
U=0 F=0 type=0x0200
length=4 (2B)
label = 17

## Slide 86: BGP4 Label Distribution
BGP peers exchange VPN routes
  can easily associate a label with these routes
all BGP procedures are immediately available for use
for label distribution messages
BGP4 is a very extensible protocol
  multiprotocol extensions support address families
  (originally for IPv4,IPv6, etc)
  MPLS defines a new address family

## Slide 87: BGP
marker can be used for authentication (TCP MD5 signature)
length is total BGP PDU length, including header
type
  OPEN (for session initialization)
  UPDATE (add, change and withdraw routes)
  NOTIFICATION (return error messages, terminate session)
  KEEPALIVE (heartbeat)
KEEPALIVE packet consists of 19B header only
marker
(16B)
length
(2B)
type
(1B)
data
(variable)
header (19B)

## Slide 88: BGP state machine
idle – no session (awaiting session initialization)
connect – attempting to connect to peer
active – started TCP 3-way handshake (router busy)
open sent – have sent OPEN message
open confirm – after receiving TCP SYN for OPEN message
established – BGP session up and running

## Slide 89: BGP OPEN
version (3 or 4) must be 4 for MPLS
my AS – identifier of autonomous system
hold time – max time (sec) between receipt of messages
BGP ID – sender’s BGP identifier
op len – length (bytes) of optional parameters
opt parameters - TLVs
version
(1B)
my AS
(2B)
hold time
(2B)
opt parameters
(variable)
BGP-ID
(2B)
op len
(1B)

## Slide 90: BGP UPDATE
Withdrawn Routes – list of routes no longer to be used (NLRI format- see below)
Path Attributes – route specific information (see next page)
Network Layer Reachability Information – (classless) routing information
  the NLRI is a list of address-prefixes
  each prefix must be masked from the left to the length specified
WR len
(2B)
withdrawn
routes
(var)
PA len
(2B)
NLRI
(var)
path attributes
(var)
len
(1B)
prefix
(variable)

## Slide 91: BGP UPDATE - Path Attributes
flags
  O – optional/well-known bit
    if 1 must be recognized by all BGP implementations
    if W=1 and unrecognized attribute, BGP sends notification and session closed
  T – transitive/nontransitive bit
    if 1 and attribute unrecognized it is passed along, else silently ignored
    well-known attributes are always transitive
  C – complete/partial bit (for optional transitive attributes only)
  L – attribute length bit (=0 attribute length is 1B, =1 length is 2B)
type code
  ORIGIN, AS_PATH, NEXT_HOP, MED, LOCAL_PREF,
  AGGREGATOR, COMMUNITY, ORIGINATOR_ID…
flags
(1B)
type code
(1B)

## Slide 92: BGP NOTIFICATON
all notification messages cause BGP session to close
error codes include:
  message header error
  open message error
  update message error
  hold timer expired
  state machine error
  other fatal error
error
code
(1B)
error
subcode
(2B)
data
(var)

## Slide 93: MPLS-TP

## Slide 94: Background
IP is the most popular packet-switched protocol
MPLS and Ethernet are the most popular server layers under IP
but neither is a transport network
At least some Service Providers want a
  packet-based transport network
  similar to present transport networks
  optimized for carrying IP

## Slide 95: Characteristics of transport networks
High availability
  Fault Management OAM
  Automatic Protection Switching
Efficient utilization, SLA support, and QoS mechanisms
  high determinism
  Connection Oriented behavior
  Performance Management OAM
Management plane (optionally control plane)
  configuration management similar to traditional
  efficient provisioning of p2p, p2m and m2m services
Scalability - must scale well with increase in
  end-points
  services
  bandwidth

## Slide 96: Possible solutions
There are two popular server network protocols for carrying IP
Ethernet
MPLS
(in the past there were ATM, frame relay, IP over SDH, etc.)
Extensions to both were proposed :
Provider Backbone Transport (which became PBB-TE)
Transport-MPLS (which became MPLS-TP)
PBT advanced in IEEE standardization (802.1ah + 802.1Qay)
but is now dead in the market
MPLS-TP was developed by both the IETF and the ITU-T
which eventually led to 2 incompatible versions

## Slide 97: MPLS-TP
MPLS-TP is a profile of MPLS, that is
it reuses existing MPLS standards
its data plane is a (minimal) subset of the full MPLS data plane
it interoperates with existing MPLS (and PWE) protocols
without gateways
TP is similar to other transport networks (including look and feel)
TP is multi-vendor (in a single domain and between domains)
TP supports static provisioning via management plane
a control plane is defined but not mandatory to use
TP networks can be configured and operate w/o IP forwarding
TP’s data plane is physically/logically separated from management/control planes

## Slide 98: The OAM issue
Since it strives to be a carrier-grade transport network
TP has strong OAM requirements
OAM has been the most contentious issue in standardization
OAM is carried in a Generic Associated Channel (GACh)
Two different OAM protocols break MPLS-TP into two distinct flavors
IETF bases its OAM on Bidirectional Forwarding Detection
BFD is a “hello” protocol originally between routers
before TP IETF standardized it for IP, MPLS, and PWs (in VCCV)
ITU bases its OAM on Ethernet OAM Y.1731 (802.1ag)
The mechanisms do not interoperate

## Slide 99: The APS issue
MPLS-TP requires linear and ring protection mechanisms
Similar to what happened in OAM
the IETF and ITU developed different APS
The ITU adapted Ethernet APS mechanisms to MPLS
The IETF developed new mechanisms with the same functionality
The mechanisms can not interoperate

## Slide 100: Planes
TP supports static provisioning via management plane
a control plane (CP) is defined but not mandatory to use
TP networks can be configured and operate w/o IP forwarding
TP’s data plane is physically/logically separated from management/control planes
Data plane continues to operate normally (forwarding, OAM, APS) even if the management/control plane that configured it fails
TP can always distinguish user packets from control/management

## Slide 101: Data plane
TP is a CO PS network
TP defines PWs, LSPs, and segments (single links of LSP or PW path)
TP clients: IP, Ethernet, MPLS, MPLS-TP and can be extended to others
TP servers: Ethernet, MPLS-TP, SDH, OTN
TP supports
traffic-engineered p2p and p2mp transport paths
unidirectional/co-routed bidirectional/associated bidirectional flows
mesh, ring, interconnected ring topologies
TP paths must be identifiable by a single label
The path’s source must be identifiable at destination
TP P2MP can exploit P2MP capabilities of a server layer
TP mechanisms can detect sub-SLA performance

## Slide 102: Topologies and connection types
TP paths are strictly Connection Oriented
and may be Traffic Engineered
TP supports :
unidirectional p2p and p2mp connections
co-routed bidirectional p2p paths
associated bidirectional point-to-point transport p2p paths
TP should safeguard against forwarding loops
TP paths can span multiple (non-homogenous) domains
TP supports rings (with at least 16 nodes)
TP supports arbitrarily interconnected rings (1 or 2 interconnections)

## Slide 103: QoS
The main aim of TP is to enable SPs to guarantee SLAs
Thus QoS mechanisms are an essential part of TP
These mechanisms include:
DiffServ traffic types and traffic class separation
provisioning end-to-end bandwidth
flexible BW allocation
support for delay- and jitter- sensitive services
guarantee of fair access to shared resources
guaranteed resources for control/management-plane traffic, regardless of the amount of data-plane traffic

## Slide 104: OAM
TP OAM applies to PWs, LSPs, and to segments, and may cross domains
TP OAM works independently and distinguishably at any label-stack depth
TP OAM fate-shares with user traffic, but is distinguishable from user traffic
TP OAM functionality can be configured by management or control plane
It should be possible to change configuration without impacting user traffic
Supported functionality:
proactive CC
proactive CV
on-demand route tracing
on-demand diagnostics (e.g., intrusive loopback)
on-demand lock (administratively configured test state)
proactive defect reporting (FDI and RDI)
proactive client failure indication (CSF)
proactive or on-demand packet loss measurement
on-demand (and proactive) 1-way and 2-way delay measurement
TP OAM must not cause network congestion
MEPs and MIPs are defined

## Slide 105: APS
TP APS is similar to APS in other transport networks
APS may be triggered by lower-layer/OAM/mngt/control plane
APS mechanism should be the same for p2p and p2mp
link, segment, and end-end protection are possible
Requirements:
standard 50 ms switching time for 1200 km
100% protection must be supported
priority logic is required but extra traffic is not required
it must be possible to preconfigure protection paths
it must be possible to test/validate protection mechanisms
race conditions with other layers must be avoided
Protection types
revertive/nonrevertive
uni and bidi 1+1 for p2p
uni 1+1 for p2mp
bidi 1:n (including 1:1) for p2p
uni 1:n for p2mp

## Slide 106: Control and Management
Every MPLS-TP network element must connect
(directly or indirectly) to an Operations System
When the connection is indirect, there must be a
Management Communication Channel
When there is a control plane, there is also a
Signaling Communication Channel
TP management plane functionality includes:
configuration management (of system, CP, paths, OAM, APS)
fault management (supervision, validation, alarm handling)
performance management (characterization, measurement)
security management
TP defines a control plane (but it is not mandatory to use)
for setting up LSPs MPLS-TP uses
  RSVP-TE and extensions
  OSPF-TE (RFC 4203 and 5392) or ISIS-TE
for setting up PWs MPLS-TP uses the PWE3 control protocol RFC4447

## Slide 107: Identifiers
In order to configure, manage, and monitor network elements
they require unique identifiers
In IP networks, IP addresses serve as a unique identifiers
but MPLS-TP must function without IP
PWs set up by PWE3 control protocol have unique identifiers
RFC 4447 defines Attachment Individual Identifiers
In carrier networks network elements can be uniquely identified by Country_Code:ICC:Node_ID
Country_Code is two upper case letters defined in ISO 3166-1
ICC is a string of one to six alphabetic/numeric characters
Node_ID is a unique 32-bit unsigned integer
For MPLS-TP any of these can be used

## Slide 108: Generic Associated Channel
MPLS-TP must be able to forward
management and control plane messages
without an IP forwarding plane
MPLS-TP must be able to inject OAM messages
that fate-share with the user traffic
MPLS-TP needs to send status indications
MPLS-TP must support APS protocol messages
How are all these messages sent ?

## Slide 109: Associated channels
PWs have an Associated Channel (ACh)
in which one can place OAM (VCCV)
that will fate-share with user traffic
The ACh is defined in RFC 4385
and is based on use of the PWE3 Control Word
MPLS-TP also needs an ACh for its OAM
but MPLS LSPs do not have a CW!
Y.1711 defined a mechanism for MPLS (pre-TP) OAM
based on use of reserved label 14 and an OAM type code
The ITU wanted to use this mechanism for T-MPLS as well
but the IETF did something a little bit different
0 0 0 1 VER RES=0 Channel Type

## Slide 110: GACh
RFC 5586 defines the Generic Associated Channel (GACh)
based on the Generic Associated channel Label (GAL)
For the simplest case :
GAL label = 13 TC S TTL
MPLS label TC S TTL
0001 0000 RESERVED Channel Type
GAL
MPLS label stack
ACH header
Zero or more ACh TLVs
GACh message

## Slide 111: What can be carried in the GACh ?
Defined Channel Types (IANA registry) :
The GACh can thus be used for:
OAM (FM/PM) – using BFD, Y.1731, … (see next chapter)
status signaling for static (non-LDP) PWs
management traffic (e.g., when no IP forwarding plane)
control traffic (e.g., when no IP forwarding plane)
other uses ?
Value | Description | TLVs | Reference
0x0000 | Reserved |  | 
0x0001 | MCC | No | RFC5718
0x0002 | SCC | No | RFC5718
0x0007 | BFD w/o IP header | No | RFC5885
0x0021 | IPv4 packet | No | RFC4385
0x0057 | IPv6 packet | No | RFC4385
0x0058 | Fault OAM | No | RFC 6427
0x7FF8-0x7FFF | Experimental Use |  | RFC5586

## Slide 112: Which OAM ?
So what OAM do we put into the GACh ?
There are two possibilities:
Bidirectional Forwarding Detection
BFD is a “hello” protocol originally between routers
before TP IETF standardized it for IP, MPLS, and PWs (in VCCV)
  RFC 5880 (draft-ietf-bfd-base)
  RFC 5881 (draft-ietf-bfd-v4v6-1hop)
  RFC 5882 (draft-ietf-bfd-generic)
  RFC 5883 (draft-ietf-bfd-multihop)
  RFC 5884 (draft-ietf-bfd-mpls)
2. Y.1731 (802.1ag)
Y.1731 is an ITU/IEEE OAM protocol for Ethernet OAM
end-end OAM with FM and PM (ITU-only) capabilities
proposed as an alternative to LSP-ping and BFD in VCCV

## Slide 113: BFD - review
Originally developed by Juniper and Cisco
to detect failures in the bidirectional path between routers
faster than via routing protocol hellos
thus reducing routing processing load as hello rates can be reduced
Light-weight liveliness protocol
control packets sent in both directions at negotiated rate
rate specified in msec
optional echo mode for two-way failure detection
runs in data plane like OAM, but unlike router hellos,
simple fixed-field encoding to facilitate HW implementation no neighbor discovery (sessions triggered by routing protocol)
Since BFD can be the payload of any encapsulating protocol
so easily extended to new cases:
physical links, tunnels, LSPs, multihop routed paths, …

## Slide 114: BFD details
Modes
Async mode – each side periodically sends control packets
Demand mode – side does not send control packet unless polled
Echo mode – echo packet returned to sender
States
Down – just created or no connectivity
Init – during 3-way handshake (set-up or tear-down)
Up – connectivity
AdminDown – administratively down for indefinite period
does not imply lack of connectivity!

## Slide 115: BFD format
format of echo packet need not be defined
BFD control packet (without optional Authentication) :
Vers Diag Sta|P|F|C|A|D|M Detect Mult Length
My Discriminator
Your Discriminator
Desired Min TX Interval
Required Min RX Interval
Required Min Echo RX Interval

## Slide 116: BFD control packet – explanations
Vers : version = 1
Diag : diagnostic code specifying the reason for the last state change
0 -- No Diagnostic 1 -- Control Detection Time Expired
2 -- Echo Function Failed 3 -- Neighbor Signaled Session Down
4 -- Forwarding Plane Reset 5 -- Path Down
6 -- Concatenated Path Down 7 -- Administratively Down
8 -- Reverse Concatenated Path Down 9-31 -- Reserved
Sta: current BFD session state as seen by the transmitting system
0 – AdminDown 1 -- Down 2 -- Init 3 -- Up
P: Poll. Sender requests verification of connectivity or of parameter change, expects an “F” packet in reply
F: Final Sender is responding to a received poll.
C: Control plane independent - sender BFD in data plane, continues to function even if control plane fails
A: Authentication present
D: Demand – sender wishes to operate in Demand mode, asks remote not to send control packets
M: Multipoint - for p2mp applications
Detect Mult : Detection time multiplier (e.g., 3). Number of Tx intervals for detection in async mode
Length : length of packet in bytes
My Discriminator : unique nonzero value used to demux BFD sessions between the same endpoints
Your Discriminator : discriminator received from the remote or zero if unknown
Desired Min TX Interval : minimum interval (msec) that can send
Required Min RX Interval : minimal interval (msec) that can receive
0 means do not send periodic control packets.
Required Min Echo RX Interval : minimum supported interval (msec) between received echo packets
if zero, echo mode is not supported.

## Slide 117: Encapsulations
single hop IP
UDP dest port = 3784 for control packets, 3785 for echo packets
UDP source port from dynamic range
TTL=255 (for security)
multihop IP
UDP dest port = 4784 for control packets, echo mode forbidden
UDP source port from dynamic range
TTL does not provide security
PW
PW label + any of the 3 VCCV CC types but always with the CW
4 CV types – (fault only or fault+status) * (with/without UDP/IP headers) – indicated in CW
only async mode, discriminator=0, capabilities signaled in PWE control protocol
MPLS
label stack of FEC being monitored
MPLS TTL set to expire
BFD triggered by LSP ping
UDP/IP BFD control packet inside MPLS
async mode only
bootstrapped with LSP ping echo request/reply messages
containing discriminators in TLV type 15

## Slide 118: Y.1731 – brief review
Developed by the ITU and IEEE as 802.1ag (CFM)
and supported by the MEF
Designed as a full multi-level carrier-grade OAM solution
Introduced new concepts, such as MEPs, MIPS, …
Supports CC, CV, AIS, LB, LT, placket loss, delay, PDV, …
Unfortunately, Y.1731 is tightly coupled with Ethernet
    EtherType identifies Y.1731 packet
    DAs identifies entities such as MEPs and MIPS
    MEL identifies level
not easy to drop Y.1731 PDUs into other protocols

## Slide 119: Y.1731 format
after DA, SA, optionally VLANs, comes Ethertype (8902)
and the following PDU
if there are sequence numbers/timestamp(s), they are next
then come TLVs (after offset), the “end TLV”, followed by the FCS
TLVs have 1B type and 2B length fields
there may or not be a value field
the “end-TLV” has type = 0 and no length or value fields
MEL
(3b)
OPCODE
(1B)
VER
(5b)
FLAGS
(1B)
TLV-OFF
(1B)

## Slide 120: Y.1731 PDU types
opcode | OAM Type | DA
1 | CCM | M1 or U
3 | LBM | M1 or U
2 | LBR | U
5 | LTM | M2
4 | LTR | U
6-31 | RES IEEE | 
32-63 unused | RES ITU-T | 
33 | AIS | M1 or U
35 | LCK | M1or U
37 | TST | M1 or U
39 | Linear APS | M1or U
40 | Ring APS | M1or U
41 | MCC | M1 or U
43 | LMM | M1 or U
42 | LMR | U DA
45 | 1DM | M1 or U
47 | DMM | M1 or U
46 | DMR | UA
49 | EXM | 
48 | EXR | 
50 | VSR | 
51 | VSM | 
52 | CSF | M1 or U
54 | SLR | U
55 | SLM | U
56 | LLR | 
57 | LLM | 
64-255 | RES IEEE | 

## Slide 121: and the winner is …
So, for MPLS-TP there are two options
BFD +  The IETF chose this route
extensible to new encapsulations
not a full OAM protocol
already runs on LSRs
and deployed in MPLS core networks
extend BFD (and LSP-ping) to become a full FM OAM protocol
and invent new protocols as needed
Y.1731  The ITU-T chose this route
  full OAM protocol
  not easily extensible to MPLS
  already runs on switches
  and deployed in carrier Ethernet networks
  create a new encapsulation and reuse all functionality

## Slide 122: The IETF OAM - overview
All functionality runs over the GAL/GACh
RFC 6428 leverages BFD for CC, CV and RDI
RFC 6426 leverages LSP-ping for on demand CV
RFC 6435 new lock instruct and loopback protocol
RFC 6427 new fault (AIS, link-down) reporting protocol
RFC 6374 new PM protocol
RFC 6375 simplified subset of loss-delay protocol
Let’s see a few of these …

## Slide 123: The IETF CC and RDI message
from draft-ietf-mpls-tp-cc-cv-rdi
CC packet
RDI indicated in BFD control packet by
Diag=8 -- Reverse Concatenated Path Down
0001 VER 00000000 CC channel type
BFD control packet
GAL Label (13) TC S=1 TTL
GAL
GACh
BFD

## Slide 124: The IETF CV message
from draft-ietf-mpls-tp-cc-cv-rdi
CV packet
0001 VER 00000000 CV channel type
BFD control packet
GAL Label (13) TC S=1 TTL
GAL
GACh
BFD
MEP Source ID TLV
Type= 1)segment 2)LSP 3) PW Length
node identifier

## Slide 125: The IETF on-demand CV message
from draft-ietf-mpls-tp-on-demand-cv
on-demand CV packet (several encaps possible)
return path is in MPLS (no IP forwarding …)
three encapsulations
  LSP-ping UDP/IP packet in MPLS (RFC 4379 )
  LSP-ping packet in UDP/IP in GACh (channel type 0x21 or 0x57)
  “raw” LSP-ping packet in GACh (new channel type)
new TLVs are defined
0001 VER 00000000 channel type
RFC 4379 packet
GAL Label (13) TC S=1 TTL
GAL
GACh
LSP-ping

## Slide 126: The IETF fault message
from draft-ietf-mpls-tp-fault
fault management packet
L flag used for AIS R flag removes previous fault condition
TLVs indicate the nodes/interfaces and conditions
0001 VER 00000000 FM channel type
Vers RES Msg Type Flags Refresh Timer
GAL Label (13) TC S=1 TTL
GAL
GACh
FM
message
TLV Length
TLVs
L R

## Slide 127: The IETF loss and delay PM
RFC 6374 defines 4 new GACh types
the same packet format is used for query and response
a flag bit distinguishes between the two
direct mode = use of counters for accurate loss measurement
inferred mode = use of synthetic packets
for loss measurement counters are carried in the OAM packets
delay measurement timestamps may be
1588 format (default) or
NTP format
These messages are for MPLS in general
Profile for TP (where no ECMP, PHP, etc) is available
Value | Description | TLVs | Reference
0x000A | Direct Loss Measurement (DLM) | No | RFC6374
0x000B | Inferred Loss Measurement (ILM) | No | RFC6374
0x000C | Delay Measurement (DM) | No | RFC6374
0x000D | Inferred Loss and Delay Measurement (ILM+DM) | No | RFC6374

## Slide 128: The ITU-T Y.1731-based OAM
Defined in G.8113.1 and draft-bhh-mpls-tp-oam
Y.1731 PDUs are placed after GAL
ACh channel type (not allocated by IANA) identifies PDUs
MEL
OPCODE
VER
FLAGS
TLV-OFF
0001 VER 00000000 allocated channel type
Y.1731 PDU with (ICC-based or IP-based) MEG ID
GAL Label (13) TC S=1 TTL
GAL
GACh
Y.1731

## Slide 129: MPLS-TP resilience
Since it strives to be a carrier-grade transport network
TP has strong protection switching requirements
APS has been almost as contentious issue as OAM
and indeed the arguments are inter-related
RFC 6372 gives a general framework
and differentiates between
  linear
  shared-mesh and
  ring
protection

## Slide 130: Linear protection – IETF style
from RFC 6378
1+1, 1:1, 1:n and uni/bidi are supported
APS signaling protocol (for all modes except 1+1 uni)
is single-phase
and called the Protection State Coordination protocol
PSC messages are sent over the protection channel
APS messages are sent over the GACh with a single channel type
message functions identified by a request field
6 states: normal, protecting due to failure, admin protecting,
WTR, protection path unavailable, DNR
when revertive, a WTR timer is used

## Slide 131: PSC message format
Request : NR, SF, SD, manual switch, forced switch, lockout, WTR, DNR
PT = Protection Type : uni 1+1, bidi 1+1, bidi 1:1/1:n
R = Revertive
FPath = which path has fault Path = which data path is on protection channel
0001 VER 00000000 PSC channel type
Ver Request PT R Res FPath Path
GAL Label (13) TC S=1 TTL
GAL
GACh
PSC
TLV Length Res
Optional TLVs

## Slide 132: Linear protection – ITU style
from RFC 7347 (Pre-standard Linear Protection Switching)
Similar to previous, but uses Y.1731/G.8031 format
0001 VER 00000000 allocated channel type
GAL Label (13) TC S=1 TTL
GAL
GACh
G.8031
MEL
VER
OPCODE=39
FLAGS=0
OFFSET=4
req
state
prot
type
requested
sig
bridged
sig
reserved
END=0

## Slide 133: Ring protection
RFC 6974
Between any 2 LSRs can define a Sub-Path Maintenance Entity
So between 2 LSRs on a ring there are 2 SPMEs –
we define 1 as the working channel and 1 as the protection channel
Now we re-use the linear protection mechanisms, including the PSC protocol
draft-helvoort-mpls-tp-ring-protection-switching
Both counter-rotating rings carry working and protection traffic
The bandwidth on each ring is divided
X BW is dedicated to working traffic and Y dedicated to protection traffic
The protection bandwidth of one ring is used to protect the other ring
Each node should have information about the sequence of ring nodes
MPLS-TP Ring Protection Switching is G.8032-like, but forwards non-NR msgs

## Slide 134
Security

## Slide 135: MPLS security
RFC 5920 provides a security framework for MPLS networks
MPLS was designed for core networks
its security design is soft on the inside and hard on the outside
If an attacker gains physical access to an MPLS network node
(it is enough for there to be an open switch port)
he can inject fake MPLS packets with arbitrary labels
(there is high probability of guessing a valid label)
Once a packet is inside the network
there are no mechanisms to identify and block it
(no sanity checking, no header field to authenticate)
In addition there are issues with MPLS control protocols
At high rates this injection can overwhelm forwarding resources

## Slide 136: Source authentication
Ethernet and IP packets contain Source Addresses (SA)
but these can be readily forged
Message Authentication Codes (MACs)
can be used to authenticate a packet’s source
that is, to prove that the SA correctly indicates the source
Source authentication is used in IPsec and MACsec
along with integrity (anti-tampering)
and optionally confidentiality (encryption)
MPLS packets contain no source address
and thus there is no way to verify who sent them
This opens MPLS to injection and label swap attacks

## Slide 137: Control plane attacks
Some MPLS control protocols (e.g., RSVP-TE) are soft-state
and others (e.g., LDP) withdraw LSPs
when contact with a peer is lost
Intermittently deleting even a few consecutive keepalive packets
can thus cause a massive denial of service
More complex attacks can poison the LFIB
These attacks are not relevant for MPLS-TP w/o a control plane

## Slide 138
Pseudowires
PE
CE
CE
CE
PE
CE
CE
CE
ACs
ACs

## Slide 139: Communications services
There are many kinds of customer traffic
(voice, video, file-transfer, BE data, web browsing, etc.)
Historically, Service Providers built networks and sold services
optimized for a specific traffic type or types
Thus, we ended up with (too) many communications protocols
IPv4, IPv6, Ethernet, MPLS, ATM, frame relay,
CLNS, E1 , E3, T1, T3, SDH, OTN, CPRI, PPP,
fiber channel, Controller Area Network, Profinet, …
However, SPs with one type of network infrastructure
want to fully exploit it to carry all types of network traffic

## Slide 140: Interworking
As transport using different network protocols
are often sold as different services (although the customer shouldn’t care)
one frequently needs to connect networks using different protocols
This connection is called interworking
The protocol converter goes by various names :
  interworking function (IWF)
  gateway (GW)
  edge device (e.g., PE)
network
A
network
B

## Slide 141: Service Interworking
One way to connect two different networks
is by full conversion of the Native Service formats
This is called service interworking
The service interworking IWF fully terminates the native services
service
interworking
function
Native
Service
A
Native
Service
B
NS A header(s)
user data
NS B header(s)
user data

## Slide 142: Tunneling
Network interworking (tunneling) is a simpler alternative
that is applicable when both end-points sit on the same NS
For example, if we wish to interconnect two Ethernet LANs
using an MPLS infrastructure network
Note that the native service protocol is not terminated
native
service
network
native
service
network
SP
network
NS headers
user data
NS headers
user data
NS headers
user data
SP headers

## Slide 143: Emulation (wire service)
Since both ends of a tunnel are of the same native service
the tunnel seems to be transparent (a virtual wire)
In fact, the goal of network interworking (wire) service
is to emulate the native service
i.e., to be as transparent as possible
however, the emulation will not always be perfect !
customer
network
customer
network
leased line
customer
network
customer
network
provider
network
tunnel

## Slide 144: Emulation Edge to Edge
customer
network
customer
network
native service link or path
customer
network
customer
network
emulated link
provider
network
provider network edge
provider network edge
end to end service
edge to edge
NS link
NS link

## Slide 145: Pseudowire
a Packet Switched Network (PSN) is
  a network that forwards packets
  e.g., IPv4, IPv6, MPLS, Ethernet*
a pseudowire (PW) is a mechanism to tunnel through a PSN
PWs have been defined for :
MPLS
L2TPv3 over IP
TDM PWs have also been defined for :
Ethernet (only TDM PWs)
UDP/IP (only TDM PWs)
PWs enable exploitation of a single converged network
PWs are bidirectional (unlike MPLS LSPs)
PW architecture is an extension of VPN architecture

## Slide 146: Provider Network Architecture
a provider network is composed of:
Provider routers or switches (P routers)
Provider Edge routers or switches (PE routers)
Attachment
Circuit
PE
router
P router
P router
P router
PE
router
P router
Attachment
Circuit

## Slide 147: VPN architecture
customer 2 network
customer 1 network
C
C
C
C
C
C
C
C
C
CE
P
PE
P
P
CE
PE
P
P
CE
provider network
customer 2 network
customer 1 network
Key
C Customer router
CE Customer Edge router
P Provider router
PE Provider Edge router
C
CE
C
C

## Slide 148: Pseudowire Emulation Edge to Edge
Provider
Edge
(PE)
Customer
Edge
(CE)
Customer
Edge
(CE)
Customer
Edge
(CE)
native
service
AC
provider’s
PSN
Pseudowires (PWs)
Customer
Edge
(CE)
Customer
Edge
(CE)
Provider
Edge
(PE)
native
service
AC
PWE3

## Slide 149: Some PWE3 ideas
Edge-to-edge emulation and maintenance of PWs
  tunnel creation and placement out of scope
  PSN is responsible for differentiation between PWs
  e.g., in MPLS there is a PW label, in UDP/IP a PW port number
Network interworking, not service interworking
Native service emulation need not be perfect
e.g., timing of a recovered TDM PW may not be the same as the timing of a native TDM circuit
  imperfection documented in applicability statements
Must not exert controls on underlying PSN
  but diffserv, RSVP-TE can be used
Must not redefine native service functionalities
  use Native Service Processing functions
The PWE3 encapsulation consists of a 4-byte Control Word
  initially each native service encap defined a different CW
  RAD once had its own TDMoIP CW
  perhaps my most important contribution to PWE3 was the single CW format
Like MPLS packets, PW packets are not self-describing

## Slide 150: MPLS PWs
Basic idea behind MPLS PWs :
LSRs forward based on ToS label
LSR don’t look inside the packet (e.g., for an IP address)
So we can carry anything inside the MPLS packet – not only IP !
The IETF PWE3 WG focused on MPLS (and the L2TPext WG on L2TPv3)
Why ?
Emulated services often have QoS and TE requirements
  IP is basically a “best effort” service (RSVP extensions not prevalent)
  MPLS can provide TE guarantees (via RSVP-TE)
IP provides no standard “bundle” multiplexing method
  UDP/TCP ports provide application multiplexing
  RTP uses ports in a nonstandard way
  L2TP includes a multiplexing mechanism
  MPLS label stack provides natural multiplexing method
We won’t delve into L2TPv3 PWs in this mini-course

## Slide 151: Simplistic MPLS solution
Each customer network mapped to pair of (unidirectional) LSPs
Each native packet/frame encapsulated with MPLS label
Scaling problem:
requires huge number of LSPs in provider network
overburdening P-router LFIBs
P-routers need to be aware of customer network details
P
PE
PE
P
CE
CE
CE
CE
CE
CE
ACs
ACs

## Slide 152: (Martini) Pseudowires
Transport MPLS tunnel set up between PEs
Multiple PWs may be set up inside tunnel
PW label is always Bottom of Stack (S=1)
Native packet/frame encapsulated with 2 labels
P-routers are completely unaware of individual PWs
PW (inner) label
payload
MPLS (tunnel) label
transport tunnel
PE
CE
CE
CE
PE
CE
CE
CE
ACs
ACs
inner label outer label(s) MPLS-f
Translations: interworking label transport label(s) ITU-T
PW label tunnel label(s) IETF

## Slide 153: Martini PWs (cont.)
P routers use the tunnel label to forward the PW packet to the egress PE
The inner label is never used as an MPLS label
no forwarding decisions based on it
only used by PE to connect to the correct native service port
But this changes in MultiSegment PWs
native
service
AC
tunnel containing many PWs
native
service
AC
PE
router
P router
P router
P router
PE
router
P router

## Slide 154: Generic PWE packet format
PSN / multiplexing
optional RTP header
optional control word (CW)
higher layers
PW payload
We call everything above the PW payload - the encap

## Slide 155: Example formats
tunnel
label(s)
PW
label
control
word
Payload
MPLS PSN
IP header (5*4 B)
session ID (4 B)
optional cookie (4 or 8 B)
control word (4 B)
L2TPv3 PSN
Payload

## Slide 156: Standard PWE Control Word
0 0 0 x
  0000 for PW user traffic
  0001 for PW Associated Channel (ACh), e.g., for VCCV OAM
Flags (4 b)
  only a few native service encaps define flags
  used to transport native service fault indications
FRG
  some native service encaps use to indicate payload fragmentation
    00 = unfragmented 01 = 1st fragment
    10 = last fragment 11 = intermediate fragment
Length (6 b)
  used when packet may be padded by lower layers
Sequence Number (16 b)
  may be used to detect packet loss / misordering
0 0 0 x flags FRG Length Sequence Number

## Slide 157: The first nibble
Most native service encaps
  do not define CW flags
  do not use FRG or Length
  do not mandate use of the SN
So what is the CW for ?
The important part of the 4 bytes is the first nibble !
In RAD’s original CW, there was a PID here
In IPv4 over MPLS the first nibble after the BoS is 0100
In IPv6 over MPLS the first nibble after the BoS is 0110
In PW packets the first nibble after the BoS is 0000 or 0001
thus identifying the MPLS packet as carrying PW traffic (not IP)
ECMP mechanisms rudely recurse down the label stack
and peek at the first nibble to differentiate between IP and PW

## Slide 158
Some PW-specific mechanisms
T-PE
P
P
P
P
P
S-PE
P
P
P
P
P
T-PE

## Slide 159: Associated Channel and VCCV
PWs have an Associated Channel for OAM, etc.
Main use is for VC Connectivity Verification - VCCV
VC is an old name for PW
CV is an incorrect name for Continuity Check
VCCV runs inside PW (same PW label) so that it fate shares
Different Control Word format
Inside VCCV several different OAM mechanisms may be used:
  ICMP
  LSP ping (RFC 4379)
  BFD (one-way or echo)
The ACh has been extended for MPLS-TP (to become the GACh)
0 0 0 1 VER RES=0 Channel Type (0x07-raw 0x21-IPv4 0x57-IPv6)

## Slide 160: VCCV Channel Types
In RAD’s original proposal, there was an OAM PW (with a special label)
that monitored all PWs in the same tunnel
The PW ACh fate-shares with PW traffic
so how do we recognize a VCCV packet ?
RFC 5085 defines 4 Control Channel types
Type 1 in-band VCCV (only when there is a CW)
CW first nibble 0001
Type 2 out-of-band VCCV
MPLS Router Alert Label (label=1) above the PW label
Type 3 TTL expiry (TTL=1 at destination PE)
Type 4 new VCCV channel type
Generic ACh Label (label=13) under the PW label

## Slide 161: MS-PWs
Single-Segment PW (SS-PW) requires the PEs to see each other
With multiple PSN domains this may not be the case
MultiSegment PW (MS-PW)
Terminal-PEs interconnect via stitching-PE
PW label becomes a true MPLS label (switching, swapping)
When there is more than one S-PE
  need to ensure that the 2 LSPs traverse the same one
T-PE
P
P
P
P
P
S-PE
P
P
P
P
P
T-PE

## Slide 162: FAT PWs
IP ECMP functions by hashing specific key fields in the IP header
MPLS ECMP hashes on the label stack
but since the BoS is the closest to the individual flows
it gives the finest granularity
There is a proposal for allowing a special entropy label in MPLS
The Flow Aware Transport PW mechanism adds a flow label
below the PW label (NB the PW label is no longer BoS)
label random (high entropy) but not a reserved label
true flows must be consistently mapped to the same flow label
TTL=1 so that it is never accidentally used for label switching
Unlike RAD’s proposal for PW bonding
there is only a single PW
but standard MPLS ECMP causes load balancing

## Slide 163: PW redundancy
Since PWs are used by SPs for transport
Automatic Protection Switching may be needed
For SS-PWs, the MPLS network protects the tunnels (e.g., FRR)
But how do we protect against PE or AC failure ?
For MS-PWs how do we protect against S-PE failure ?
The basic idea is
dual homing a CE to >1 PE
and setting up primary and secondary PWs (control protocol extensions)
monitoring PWs using VCCV
triggering protection switch using (new bits in) PW status messages

## Slide 164
PWE Control Protocol

## Slide 165: PW set-up
PWs can be set up
statically
via the PWE3 control protocol (RFC 4447) based on LDP
via BGP (for L3VPN or L2VPN)
No matter how set up
need to place the PW into an MPLS tunnel
A PW is a bidirectional entity (two LSPs in opposite directions)
so we need to associate the two directions
PE
PE

## Slide 166: PWE3 (Martini) control protocol
PWE control protocol (RFC 4447) is used to set up / configure PWs
It is used only by PW end-points (PEs in standard model)
  intermediate nodes (e.g. P routers) don’t participate or see it
The PWE3 control protocol is based on LDP
  PWs do not support QoS
  targeted LDP is used to communicate with opposite end-point
  2 new FECs for PWs
  new TLVs added for PW-specific functionality
  associates two labels with PW
PE
PE
P
P
P
P
P

## Slide 167: LDP extensions
RFC 4447 does not define any new LDP messages
It defines 2 new FEC types (see next page)
PWid FEC (128)
Generalized ID FEC (129)
It defines 3 new TLVs
Notification PW Interface Parameters (in FEC element)
FEC PW Grouping ID (in FEC element)
PW Status (in Notification message)
  Status TLV contains more information than Label Withdraw message

## Slide 168: PW FEC types
A PW is a bidirectional entity (two LSPs in opposite directions)
so we need to associate the two directions
2 new LDP FEC types are defined
LDP previously defined 3 FEC types : wildcard(1) prefix(2) host address(3)
  PWid FEC (128)
  Generalized ID FEC (129)
FEC 128
  both end-points of PW must be provisioned with a unique (32b) value
  WARNING: no relationship between this value and label
  each PW end-point independently initiates LSP set up
  LSPs associated to form the PW
FEC 129
  used when autodiscovering PW end-points
  each end-point has Attachment Identifier (see next page)

## Slide 169: Generalized PW ID
Each forwarder (PW AC) has a PE-unique Attachment Identifier (AI)
  <PE, AI> must be globally unique
It is frequently useful to group a set of forwarders into a attachment group
  where PWs may only be set up among members of a group
then Attachment Identifier (AI) consists of
  Attachment Group Identifier (AGI) (which is basically a VPN-id)
  Attachment Individual Identifier (AII)
the LSPs making up the (two directions of the) PW are
  < PE1, (AGI, AII1), PE2, (AGI, AII2) > and
  < PE2, (AGI, AII2), PE1, (AGI, AII1) >
we also need to define
  Source Attachment Identifier (SAI = AGI+SAII)
  Target Attachment Identifier (TAI = AGI+TAII)
  receiving PE can map TAI uniquely to AC

## Slide 170: TDM PWs
headers
TDM payload

## Slide 171: What is TDM ?
By TDM we mean synchronous transport at
one of the PDH (G.702) rates
one of the SDH (G.707) rates
TDM networks can themselves carry
telephony traffic
data traffic
video
Native TDM networks
circuit switching ensures signal integrity
very high reliability (“five nines”)
low delay and no noticeable echo for telephony
timing information transported over the network
mature signaling protocols (over 3000 features)

## Slide 172: PDH rates
64 kbps
2.048 Mbps
1.544 Mbps
1.544 Mbps
6.312 Mbps
6.312 Mbps
8.448 Mbps
34.368 Mbps
139.264 Mbps
44.736 Mbps
32.064 Mbps
97.728 Mbps
274.176 Mbps
CEPT
N.A.
Japan
4
3
2
1
0
level
* 30
* 24
* 24
* 4
* 4
* 4
* 4
* 7
* 6
* 4
* 5
* 3
E1
E2
E3
E4
T1
T2
T3
T4
J1
J2
J3
J4

## Slide 173: TDM Structure
handling of TDM depends on its structure
unstructured TDM (TDM = arbitrary stream of bits)
structured TDM
…
SYNC
TS1
TS2
TS3
signaling
bits
…
…
TSn
(1 byte)
channelized (single byte timeslots)
S
Y
N
C
framed (8000 frames per second)
S
Y
N
C
S
Y
N
C
multiframed
frame
frame
frame
…
frame
multiframe

## Slide 174: TDM transport types
Structure-agnostic transport (SAToP – RFC4553)
for unstructured TDM
even if there is structure, we ignore it
simplest way of making payload
OK if network is well-engineered
Structure-aware transport (TDMoIP, CESoPSN)
take TDM structure into account
must decide which level of structure (frame, multiframe, …)
can overcome PSN impairments (PDV, packet loss, etc)
headers
TDM payload

## Slide 175: Structure aware encapsulations
Structure-locked encapsulation (CESoPSN)
Structure-indicated encapsulation (TDMoIP – AAL1 mode)
Structure-reassembled encapsulation (TDMoIP – AAL2 mode)
headers
TDM structure
TDM structure
TDM structure
TDM structure
headers
AAL1 subframe
AAL1 subframe
AAL1 subframe
AAL1 subframe
headers
AAL2 minicell
AAL2 minicell
AAL2 minicell
AAL2 minicell

## Slide 176: TDM PW layering structure
AAL1/CESoPSN used for preconfigured setup
AAL2 used for dynamic bandwidth
HDLC used for CCS signaling
higher layers
PSN / multiplexing
Optional RTP header
PWE3 Control Word
AAL1
AAL2
HDLC
SAToP
CESoPSN

## Slide 177: TDMoIP Control Word
0 0 0 0 / FORMID (4 b)
  was used to indicate TDMoIP mode (AAL1, AAL1 - CAS, AAL2, HDLC)
  ensures differentiation between IP and MPLS PSNs
Flags (4 b)
  L bit (Local failure)
  R bit (Remote failure)
  M field (2 b)
Length (6 b) used when packet may be padded by lower layer
Sequence Number (16 b) used to detect packet loss / misordering
0 0 0 0 flags 0 0 Length Sequence Number

## Slide 178: Optional explicit timing
VoIP uses RTP (Real-Time Protocol)
RTP can be used to transport timing across IP networks
It does this by providing:
a 16 bit sequence number
a 32 bit timestamp
at the expense of 12 additional overhead bytes per packet
Accurate timing is important in telephony
  and IP networks add packet delay variation (PDV)
For TDM PWs, only the timestamp is needed (SN is in CW)
  encodes time of sending using clock N*8kHz
  Note
    this is NOT the normal RTP clock (number of samples)
    rather with respect to a common clock

## Slide 179: CESoPSN mode
Can efficiently handle fractional T1/E1
FRG field in CW enables support of multiframe
CAS signaling uses a superframe (16/24 frames)
Superframe/multiframe integrity must be respected
Octet aligned mode for T1 (24 bytes plus one bit per frame)
PSN
T1/E1 frame
CW
T1/E1 frame
…

## Slide 180: TDMoIP AAL1 mode
Packet loss, misorder, PDV problems can be solved by:
adding a packet sequence number
adding a pointer to the next multi-frame boundary
only sending timeslots in use
allowing multiple frames per packet
for example
UDP/IP
T1/E1 frames (only timeslots in use)
seqnum
(with CRC)
ptr
TS1 TS2 TS5 TS7 TS1 TS2 TS5 TS7
7
@
Good idea! This is AAL1 !
using precisely AAL1 enabled service interworking with ATM networks

## Slide 181: TDMoIP AAL2 mode
Each minicell consists of a header and buffered data
Minicell header contains:
  CID (Channel IDentifier)
  LI (Length Indicator) = length-1
  UUI (User-User Indication) counter + payload type ID
using precisely AAL2 enabled service interworking with ATM networks
TDM frame
TDM frame
TDM frame
TDM frame
TDM frame
1
2
4
5
3
1
1
2
2
3
3
4
4
5
5
1
2
3
4
5
hdr
1
2
3
4
5
hdr
1
2
3
4
5
hdr
PSN hdrs
CW
TS1
TS2
TS3

## Slide 182: CEP
Circuit Emulation over Packet is an SONET/SDH PW
Encapsulate Synchronous Payload Envelope fragment
Structure Pointer in CW points to J1 byte in STM frame
PSN layers
Optional RTP header
CEP Control Word
CEP CW
E1 flags4 structure ptr13 Suppressable Sequence Number 14

## Slide 183: Ethernet PWs

## Slide 184: Traditional WAN architecture
Ethernet layer is terminated
  only higher layer (e.g., IP) is transported
  the traffic is no longer Ethernet at all
Ethernet header
removed at ingress, and
new header added at egress
This is not transparent Ethernet LAN interconnect
Ethernet LANs with many higher layer packet types
can’t be interconnected
raw L2 Ethernet frames can not be sent
Ethernet
Ethernet
not Ethernet
WAN

## Slide 185: Tunneling Ethernet frames
Users with multiple Ethernet sites may want to connect their LANs
  so that all locations appear to be on the same LAN
This requires tunneling of all Ethernet L2 frames (not only IP)
  between one LAN and another
The entire Ethernet frame needs to be preserved
  (except perhaps the FCS, which may be regenerated at egress)
Ethernet
Ethernet
Ethernet inside X
X

## Slide 186: Ethernet PW (RFC 4448)
While PWs were designed for legacy traffic
Ethernet PWs are now the most popular type
This is because native Ethernet transport is limited in range
RFC 4448 specifies:
Control word is optional
  even if control word is used, sequence number if optional
Standard mode – FCS is stripped and regenerated
  FCS retention mode (RFC 4720) allows retaining FCS
Can transport tagged or untagged Ethernet frames
  if tagged :
  encapsulation can be raw mode or tagged mode
  tagged mode processes (inserts/swaps/removes) service delimiting tags

## Slide 187: Ethernet Pseudowire packet
tunnel
label
PW
label
control
word
single Ethernet Frame
Ethernet Frame usually has FCS stripped
  SP tag may also be stripped
optional control word
  generation and processing of sequence number is optional
0000 reserved Sequence Number (16b)

## Slide 188: VPWS
Based on Ethernet PWs one can provide a
Virtual Private Wire Service or a
Virtual Private LAN Service (L2VPN)
VPWS emulates a wire supporting the Ethernet physical layer
set up MPLS tunnel between PEs
set up Ethernet PW inside tunnel
CEs appear to be connected by a single L2 circuit
(can also make VPWS for ATM, FR, etc.)
CE
CE
AC
AC
PE
PE
provider
network

## Slide 189: VPLS
VPLS emulates a LAN over an MPLS network
set up MPLS tunnel between every pair of PEs (full mesh)
set up Ethernet PW inside tunnels, for each VPN instance
CEs appear to be connected by a single LAN
What is the difference between this and a L3 VPN service ?
CE
CE
CE
for clarity only one VPN is shown
AC
AC
AC
PE
PE
PE

## Slide 190: L2VPN vs. L3VPN
in L2VPN CEs appear to be connected by single Ethernet network
  PEs are transparent to L3 routing protocols
  CEs are routing peers
in L3VPN CE routers appear to be connected by a single IP network
  CE is routing peer of PE, not remote CE
  PE maintains routing table for each VPN
CE
CE
CE
PE
PE
PE
?
L2VPN: MPLS network → giant switch
L3VPN: MPLS network → giant router

## Slide 191
Other PW types
PE
CE
CE
CE
PE
CE
CE
CE
ACs
ACs

## Slide 192: What else is there ?
For what native service types have PW encaps been defined ?
TDM (SONET/SDH, E1, T1, E3, T3)
Ethernet
ATM (port mode, cell mode, AAL5-specific modes)
Frame Relay
HDLC / PPP
IP PW (in 4447, never became a normative RFC)
Fiber channel
Generic packet PW

## Slide 193: ATM PWs (RFC 4717)
N:1 (Martini mode)
  control word optional
  remove HEC to form 52-byte cells
  pack 1 or more cells into MPLS packet (may mix VPI/VCI)
1:1 (ATM forum mode)
  special 3-byte control word required
  1-byte header for each cell
  pack 1 or more cells into MPLS packet
  may mix VCI for given VPI (but then need to insert VCI)
SDU (for AAL5 only)
  control word with 4 flags required (SN optional)
  payload is the complete SDU (no trailer)
PDU (for AAL5 only)
  special 3-byte control word required
  1-byte header after CW
  payload is N*48-byte PDU
port mode (RFC 4816) - format same as N:1

## Slide 194: Frame Relay PWs (RFC 4619)
2 encapsulations :
port mode (many-to-one mapping) 1 PW per all FR VCs
identical to HDLC PW encapsulation RFC4618
1:1 mode – one PW for each FR VC
Mandatory (for 1:1) CW contains 4 flags
F FECN (Forward Explicit Congestion Notification)
B BECN (Backward Explicit Congestion Notification)
D DE bit (Discard Eligibility)
C C/R (Command/Response)
SN optional and FRG extensively used

## Slide 195: Packet PW (RFC 6658)
Generic packet service to carry
any packets exchanged between adjacent LSRs, such as
IP packets (user, system)
Ethernet packets (e.g., IS-IS, LLDP, Ethernet OAM)
To mux different packet types we use raw Ethernet PW
although there is no real Ethernet interface
MAY use local MAC addresses
or MAY use (IANA allocated) MAC addresses PacketPWEthA / PacketPWEthB

## Slide 196: Fiber Channel PW (RFC 6307)
FC is a high-speed communications link used for SANs
Fibre Channel Over TCP/IP (FCIP) (RFC3821) needs TCP
to retransmit dropped frames and ensure order
MPLS networks may have very low loss and misorder rates
FC PW transparently transports FC traffic over MPLS
with simpler processing than FCIP
However, FC PWs have more complex NSP than other PWs

## Slide 197: DetNet PW
Recently, PWs have been proposed as a mechanism
for Deterministic Networking
For example, for high reliability MPLS-based DetNets
employ a replication and elimination function
that requires a sequence number per packet
This can be supplied by a PW-style control word
(Details still in being worked out)