## Slide 1: SDN / NFV vs. QoS-assured Networks
Presented by:
Yaakov (J) Stein
CTO

## Slide 2: 2012 DA14
On Friday, Feb. 15 2013, an asteroid named 2012DA14
about 30 meters across
weighing about 40,000 metric tons)
traveling at about 28,000 km/h
came within 27,700 km of earth
Yet astronomers classified this Near Earth Object as
white (nonhazardous) on the Torino scale !
geostationary satellites - 35,786 km
mean lunar distance 384,400 km

## Slide 3: Torino scale
The Torino scale gauges NEO importance
based on (very roughly) :
how close the object is
how big* the object is
* the energy also depends on how fast the NEO is moving
Of course, this is geocentric point of view
From the NEO’s point of view the question is
whether the earth is getting in the way of its progress potentially endangering its continued existence

## Slide 4: Impact of SDN/NFV on SP networks
The potential impact of SDN/NFV on Service Provider networks is similar
It depends on :
how close SDN/NFV is to what SP’s want
how big* a change SDN/NFV can bring
* it also depends how rapidly SDN/NFV is maturing
Of course, this is the Service Provider’s point of view
From the SDN community point of view the question is
whether the SP network requirements get in their way
potentially killing SDN entirely (at least in the SP space)
In order to understand the potential impact of SDN/NFV on SP networks
we need to first define SP networks, SDN, and NFV
The focus here is on SP networks
but much of what we say is true
for campus and enterprise networks
We will not discuss the advantages of SDN
for research in academic networks
nor certain special security applications

## Slide 5: What is a Service Provider network ?
A network that :
provides a communications service to a customer
  the customer may be an end-user or yet another SP
provides QoS assurances (always availability, often performance)
  since vanilla service is mostly free
provides 1. and 2. profitably
  all SPs that still exist agree on this point …
If SDN can truly fulfill these, this would be close !
Note that the following are not part of this definition :
use of specific routing protocols and packet formats (Ethernet, MPLS, IP)
  this is just a means of attaining 1. supra
use of Traffic Engineering, FM, PM, protection switching, …
  these are just means of attaining 2. supra
use of special purpose hardware rather than merchant silicon
  this is just a means of attaining 3. supra

## Slide 6: SDN/NFV motivation
Today’s communications world contains many different Network Elements (NEs)
sensors, smartphones, notebooks, laptops, desk computers, servers,
DSL modems, Fiber transceivers,
SONET/SDH ADMs, OTN switches, ROADMs,
Ethernet switches, IP routers, MPLS LSRs, BRAS, SGSN/GGSN,
NATs, Firewalls, IDS, CDN, WAN aceleration, DPI,
VoIP gateways, IP-PBXes, video streamers,
performance monitoring probes , performance enhancement middleboxes,
etc., etc., etc.
New and ever more complex NEs are being invented all the time,
and RAD and other equipment vendors like it that way
while Service Providers find it hard to shelve and power them all !
In addition, while service innovation is accelerating
the increasing sophistication of new services
the requirement for backward compatibility
and the increasing number of different SDOs, consortia, and industry groups
which means that
it has become very hard to experiment with new networking ideas
NEs are taking longer to standardize, design, acquire, and learn how to operate
NEs are becoming more complex and expensive to maintain

## Slide 7: Two complementary solutions
Network Functions Virtualization (NFV)
This approach advocates replacing hardware NEs
with software running on COTS computers
that may be housed in POPs and/or datacenters
Advantages:
COTS server price and availability scales well
Functionality can be placed where-ever most effective or inexpensive
Functionality may be speedily deployed, relocated, and upgraded
Software Defined Networks (SDN)
This approach advocates replacing standardized networking protocols
with centralized software applications
that may configure all the NEs in the network
Advantages:
Easy to experiment with new ideas
Software development is usually much faster than protocol standardization
Centralized control simplifies management of complex systems
Functionality may be speedily deployed, relocated, and upgraded
Note: Some people call NFV Service Provider SDN !
Note: Some people call this SDN Software Driven Networking
and call NFV Software Defined Networking !

## Slide 8: What do SDN proponents say ?
There are as many definitions of SDN as proponents and detractors
We’ll concentrate on the definition of SDN as a network that :
utilizes general purpose computational resources (pure NFV)
  forwarding elements need to be flexibly reprogrammable (SDN and NFV)
considers packet forwarding to be a computational problem (SDN and NFV)
  usually implies centralized server having complete knowledge of network state
replaces fundamental principles of communications theory with those of computation and software design (modularity, abstractions, …)
  which SDN proponents believe are completely different principles (pure SDN)
If SDN truly changes a fundamental principle, this would be big !
Open Source does not seem to be a indispensable requirement of SDN today !
SDN does not have to be out in the open daylight
Note that simply using a protocol such as OpenFlow as a means to configure
standard routers/switches does not fall under this definition
(not obeying any of the above)

## Slide 9: What are the fundamental principles ?
First, let’s examine the truly fundamental principles of communications theory
to see if with which ones computation theory disagrees
The four most fundamental principles are:
Shannon’s (source/channel) separation theorem
Virtual Connections and Virtual Private Networks
Separation of data, control, and management planes
Client/server and peer-peer layering
Note that they are all about …
breaking the problem into parts, or
joining parts to make a whole

## Slide 10: 1. Shannon’s Separation theorem
Historically the separation theorem led to digital communications
It states that the optimal communications system has precisely 4 parts
Any further partitioning reduces optimality
In particular, the celebrated 7-layer OSI (X.200) model
is in direct contradiction to the separation theorem
and indeed leads to gross inefficiencies
It was put in place to facilitate implementation
and should not be considered a fundamental principle
So, if SDN discards this layering model
it violates tradition, but actually returns to fundamental communications principles
However, SDN theorists regard ISO layering as an important communications principle !
source
encoder
channel
encoder
channel
decoder
source
decoder
information source
information sink
degrading
channel
bits
bits
analog
signal
analog
signal
digital channel
known capacity
nothing allowed here
nothing allowed here
application
layer
application
layer
physical layer

## Slide 11: Shannon’s Separation theorem (cont.)
Whether SDN proponents support or oppose OSI layering
has no relevance to fundamental principle 1
This principle derives from physics
and computation theory has nothing to add or detract from it
* SDN proponents can not disagree with principle 1

## Slide 12: 2. Virtual Connections and VPNs
The separation theorem speaks about communications links
and early telegraph and telephone connections were indeed links
However, it is impossible (or at least very inefficient)
to directly connect every 2 points that need to communicate
Instead, one can
create a connected graph of arbitrary topology (a network)
find a path connecting any two points (a virtual connection)
Furthermore, one can logically create a fully connected graph,
sub-graphs of which are are virtual private networks
In order to implement this scheme, one must
associate an address (which becomes part of the Shannon information) to each point
implement a scheme to forward information through the original graph
This type of virtualization is used in computation all the time !
* SDN proponents will agree with principle 2 (if they know about it …)

## Slide 13: 3. Data, control, and management planes
In order to facilitate forwarding
it is worthwhile to distinguish between :
forwarding
routing (i.e., learning how to forward)
administration (setting policy, service commissioning, monitoring, billing, …)
This leads to defining three planes – data (or user), control, and management
Traditionally the distinction between control and management was that :
management had a human in the loop
while the control plane was automatic
With the introduction of more sophisticated software
the human could often be removed from the loop
The difference that remains is that
the management plane is slow and centralized
the control plane is fast and distributed
We will see that these characteristics are important!
data plane
control plane
management plane

## Slide 14: Data, control, and management planes (cont.)
Many SDN proponents claim
that separation of the data and control planes is a defining attribute of SDN rather than a time-honored fundamental characteristic of networks
This belief apparently arises from these proponents
being familiar with the Linux router
which does not clearly separate forwarding from routing
However, the Linux router was written by programmers
not by networking experts
* SDN proponents actively promote
fundamental principle 3
data plane
control plane
management plane

## Slide 15: 4. Client/server layering
In the same way that we virtualized the idea of a link (first virtualization)
we can virtualize the idea of a (virtual) network (second virtualization)
So, we needn’t require a single end-user to create a link
and we needn’t require a single SP to create the entire (virtual) network
Rather we can combine (virtual) networks to provide the end-end service
There are two ways to connect two networks (G.805)
client/server interworking (layering, OTT)
peer to peer interworking (stitching)
Unlike OSI layering
there are very good (business) reasons for these:
maintaining a generic interface
modularity
effect isolation
information hiding
In other words, precisely the principles of modern software design !
* Computation theorists agree in principle with fundamental principle 4

## Slide 16: Consequences of layer violations
Client/server layering enables Service Providers
to serve a higher-layer SP
to be served by a lower-layer SP
Layer violations may lead to security breaches, such as :
billing avoidance
misrouting or loss of information
information highjacking
information tampering
Layer respect is often automatically enforced by network element functionality
A fully programmable forwarding element may create layer violations, due to :
programming bugs or
being taken over by malicious entities
If fully programmable elements (SDN switches) become widely deployed
Service Providers will need to deploy additional security mechanisms
It may prove impossible to protect against certain SDN security breaches
So, while computation theory agrees with principle 4
SDN practice’s disrespect of it may lead to serious security risks

## Slide 17: Robustness
Our conclusion so far - computation theory supports
all four fundamental principles of communications theory
But SDN proponents complain about
the brittleness / fragility of communications protocols
As opposed to the robustness their approach can bring
To investigate this claim, we need to understand what robustness means
We say that a system is robust to X
when it can continue functioning even when X happens
For example,
A communications network is robust to failures
if it continues functioning even when links or network elements fail
A communications network is robust to capacity increase
if it continues functioning when the capacity it is required to handle increases
Note that it is meaningless to say that a system is robust without saying to what !

## Slide 18: Robustness (cont.)
Unfortunately, robustness to X may contradict robustness to Y
For example,
In order to achieve robustness to failures
the network is designed with redundancy (e.g., 1+1)
In order to achieve robustness to capacity increase
the network is designed for efficiency, i.e., with no redundancy
Thus networks can not be designed to be robust to everything
Instead, networks are designed to profitably provide services
The X that seems to be most on the minds of SDN proponents is
creation of new types of services
In the past, new service type creation was infrequent
so networks were not required to be robust to it
This is indeed an area where there is potential
for SDN/NFV to make a big difference !

## Slide 19: The CAP Theorem
Since we haven’t found any fundamental principles of communications theory that are alien to computation theory
Let’s look at a theorem from computation theory
There are three desirable characteristics of a distributed computational system
Consistency (get the same answer no matter which computational element responds)
Availability (get an answer without unnecessary delay)
Partition tolerance (get an answer even if there a malfunctions in the system)
The CAP (Brewer’s) theorem states that you can have any 2 of these, but not all 3 !
SDN teaches us that routing/forwarding packets is a computational problem
so a network is a distributed computational system
So networks can have at most 2 of these characteristics
Which characteristics do we need, and which can we forgo ?

## Slide 20: CAP: the SP Network Choice
SPs pay dearly for lack of service
not only in lost revenues, but in SLA violation penalties
SP networks are designed for1 :
high availability (five nines) and
high partition tolerance (50 millisecond restoration times)
So, consistency must suffer
black-holed packets (compensated by TTL fields, CV testing, etc.)
eventual consistency (but steady state may never be reached)
This is a conscious decision on the part of the SP
The precise trade-off is maintained by a judicious combination
of centralized management and distributed control planes
1 This applies to services that have already been configured.
When commissioning a new service Availability is sacrificed instead
which is why service set-up is often a lengthy process.
CAP
X

## Slide 21: CAP: the SDN Choice
SDN has emphasized consistency (perhaps natural for software proponents)
So such SDNs must forgo either availability or partition tolerance (or both)
Either alternative may rule out use of SDN in SP networks
Relying solely on a single1 centralized controller
(which in communications parlance is a pure management system)
may lead to more efficient bandwidth utilization
but means giving up partition tolerance
However, there are no specific mechanisms to attain availability either !
Automatic protection switching needs to be performed quickly
which can not be handled by a remote controller alone2
1 Using multiple collocated controllers does not protect against connectivity failures.
Using multiple non-collocated controllers requires synchronization, which can lead to low availability.
2 There are solutions, such as triggering preconfigured back-up paths,
but present SDN protocols do not support conditional forwarding very well.
CAP
X

## Slide 22: Is NFV reasonable ?
There have been many PoCs showing that NFV is just around the corner
The reasoning given is
general purpose CPUs can not economically perform
the required network function right now
but, because of Moore’s law they will be able to do so soon
Does this make sense ?
Moore’s law is being interpreted to state
computation power is doubling per unit price about every two years
However, this reasoning neglects Butters’ Law that states
optical transmission speeds are doubling every nine months
So, if we can’t economically perform the function in NFV now
we won’t be able to perform it at the required data-rates next year
Note that driving bandwidth can increase faster than Moore’s law
because of increasing number of devices and applications

## Slide 23: So, how small and far is SDN/NFV ?
Despite to claims to the contrary, SDN/NFV
do not repudiate any principles of communications theory
do not propose any revolutionary new principles
Thus they have no impact on basic communications theory
New SDN management protocols (e.g., OpenFlow)
that may lead to more efficient bandwidth utilization
or faster new service deployment
or more sophisticated security mechanisms
will be adopted alongside existing protocols
These will have only minimal impact on SP networks
(As SDN proponents remind us, we have so many protocols already …)
NFV will never take over high-rate network functions
due to Butter’s law trumping Moore’s law

## Slide 24: So, how big and close is SDN/NFV ?
NFV will spread to access networks and management functions
in order to increase robustness of networks to creation of new service types
SDN opts for a different CAP theorem trade-off
preferring consistency to availability and partition-tolerance
This means that it is far off-course for present-day SP networks
and will require rethinking of its applicability
New security threats from misbehaving SDN/NFV network elements
may present difficult security challenges to Service Providers
strongly negatively impacting their operations

## Slide 25
Follow us at
raddata.blogspot.com