## Slide 1: Automotive networks and the world of SOME/IP
Yaakov (J) Stein

## Slide 2: ECUs
An Electronic Control Unit (ECU) is exactly what you would imagine
an electronic unit for controlling a (mechanical/electrical) system
The term is mostly used in automotive systems
where it can be confused with a specific ECU - the Engine Control Unit
What exactly does an ECU do?
input one or more (sensor) indications from the controlled system
perform some calculation (all modern ECUs contain a CPU!)
output one or more signals (actuations)
  to alter the operation of the controlled system
ECU
sensor
actuator
controlled system

## Slide 3: What’s an ECU made of?
Modern ECUs are SoCs (Systems on Chip) usually containing:
CPU (8/16/32-bit, 10-100 MHz)
flash memory for the software (≤ 1 MB)
RAM for data (not always)
signal conditioners, A/Ds, D/As, relays, etc.
I/O ports (e.g., for diagnostics)
communications interfaces (most of this talk!)
Most ECUs today are specific to the car manufacturer and even to a model

## Slide 4: For example?
Modern cars can have between 10 and 100 ECUs, for example:
Engine Control Unit (ECU) (fuel injection, air/fuel ratio, ignition timing, temp. correction, …)
Transmission Control Unit* (automatic gear)
Power Steering Controller
Battery Management System
Windshield Wiper Controller
Speed Control Unit (cruise control)
Brake Control Unit (ABS, anti-skidding)
Turn Signal Control Module (blinkers)
Air bags
Tire pressure
Light Control Module (headlights, rear lights, cabin lights)
Body Control Unit(s) (A/C, immobilizer, door/window/mirror control/…)
Advanced Driver Assistance System
Multimedia system
Parking video camera
…
* WARNING: TCU also used for Telematics Control Unit

## Slide 5: Newer ECUs
As cars become more sophisticated there are more ECUs
keyless entry
remote start
all-passenger personal infotainment
Automatic Vehicle Location (telelocation)
radar/lidar distance measurement
lane assist
360 degree parking assist
traffic sign recognition
pedestrian detection
V2X (V2V, V2I, V2P, …) including over 5G

## Slide 6: And more futuristic!
Augmented Reality dashboards / steering wheels
  distance and identification overlaid over objects on the road
  dangers highlighted
platooning V2V
fully self-driving (autonomous) delivery vehicles
photoelectric recharging of electric vehicles

## Slide 7: Why not a single CPU?
Why are there so many ECUs instead of a single Central Processing Unit?
History
automotive technology has developed over time
  so it was natural to add an independent local ECU for each new feature
Real time
there may be tight delay constraints between sensing and actuation
using separate ECUs eliminates most process queuing delays
Reliability
When there are critical reliability requirements, modularization -
  avoids single point of system-wide failure
  makes it simpler to develop bug-free code and prove correctness

## Slide 8: Communications
Because it is composed of many ECUs
the automobile itself is essentially
a distributed multiprocessor (parallel) computation system
Some of these ECUs are, and should remain, completely independent
For example, it’s a really bad idea to allow the multimedia controller
to access the steering or braking systems!
( see https://www.youtube.com/watch?v=MK0SrxBC1xs )
But many ECU do need to exchange information, for example:
Engine Control Unit and Transmission Control Unit (many interactions!)
reverse/parking controller needs TCU trigger
Body Control Unit needs to lock doors upon attaining some speed
diagnostics and dashboard instrumentation need data from almost all systems

## Slide 9: The original solution
With the proliferation of ECUs and their communications requirements
automotive manufacturers started connecting them up
using dedicated point-to-point links (some analog some digital)
each with its own proprietary protocol
This solution does have several advantages
only ECUs truly requiring communications are interconnected
  (compartmentalization is good for security!)
single purpose protocols may be simpler to design (at least the 1st time!)
but resulted in numerous problems
tremendous number of cables ( O(N2) )
difficult to aggregate information for instrumentation and diagnosis
R&D and maintenance complexity

## Slide 10: The cost of networking ECUs
Over time the complexity, cost, and weight of wiring harnesses
has significantly increased to the point where they are non-negligible
Old cars have under 100 wires, reaching about 50 meters in length
while modern cars can have over 1000 wires exceeding 1 km in length
In fact
wiring up can comprise 50% of the manufacturing labor cost
copper wiring can add 25 kg to car’s weight
There is thus a strong drive for upgrading conventional communications
with modern more efficient networking solutions
It has been estimated that cost reduction may be up to 75%

## Slide 11: Automotive network standards
Vendors, automotive industry groups, and standards organizations
have come up with networking standards for ECU interconnection
Controller Area Network bus (CAN bus) [ISO 11898-1 … 11898-6]
Local Interconnect Network (LIN bus)
FlexRay [ISO 17458-1 … 17458-5]
Media Oriented Systems Transport (MOST bus)
Time-Triggered Ethernet (TTTech) [SAE AS6802]
Scalable service-Oriented Middleware over IP (SOME/IP)
application specific
e.g., K-line diagnostics, OBD-II diagnostics and emissions monitoring
We’ll discuss some of the most important of these

## Slide 12: CAN bus
Right now CAN bus is the dominant automotive ECU networking protocol
nearly every automobile sold today has a CAN bus!
Like many current ECU networking protocols
the physical layer of CAN bus is a multi-master serial bus
all ECUs are connected in parallel and all messages are broadcast
the physical bus is balanced 2-wire (with termination resistors at bus ends)
with differential voltage across these wires and NRZ encoding
any ECU can transmit at any time
all ECUs receive all messages, but only act on particular message IDs
CAN nodes don’t have L2 addresses (since topology is considered unimportant)
but higher layers over CAN may support addressing

## Slide 13: CAN bus history
1983 Bosch (German manufacturer) started development of CAN bus
1987 Intel produced the first CAN controller chips
1991 Mercedes Benz produced the first vehicle with CAN bus
1993 ISO released ISO 11898 for CAN bus, later divided into
  11898-1 for layer 2
  11898-2 for layer 1 at 1 Mbps
  11898-3 for layer 1 at speeds up to 125 kbps
  15765-2 for layers 3 and 4
1994 CAN bus became the de-facto L1/L2 standard in all US cars
2001 CAN bus became the de-facto L1/L2 standard for European cars

## Slide 14: CAN speeds
CAN buses are typically rated based on their speed
Class A rating carries less than 10 Kbps
for power windows, mirrors, seats, door locks, trunk releases, lights
Class B rating from 10 Kbps up to 125 Kbps (SAE J1850 or ISO 9141-2)
for instrumentation, transmission, security systems, climate control
Class C speeds up to 1 megabits per second (many at 500 Kbps)
for powertrain, ABS, stability control
Class D is a proposal for speeds over 1 Mbps
for onboard entertainment systems, video streaming
Some vendors define proprietary classes based on 2 buses – low and high speed
  GMLAN: low speed 33.33 Kbps and high speed 500 Kbps
  Mercedes: low speed 83 kbps and high speed 500 Kbps

## Slide 15: CAN Multiple access method
ECUs on a CAN bus may want to transmit at any time
and so some Multiple Access mechanism must be provided
CAN bus uses bit-wise deterministic collision avoidance
the message with highest priority (lowest message ID) gains access
and all other transmitters must stop and wait
Note that the message ID is the first field in the message
minimizing the arbitration time
Strict priority based arbitration results in
highest priority messages always transmitted with no delay
lower priority messages preempted but transmitted afterwards
straightforward analysis of latency for all messages

## Slide 16: How are messages transmitted in CAN bus ?
All CAN messages are broadcast to every ECU on the bus
Every message starts with a single Start of Frame bit (0)
and ends with End of Frame field (seven 1 bits)
between messages there is a frame gap (at least three 1 bits)
Bit stuffing is used if 7 consecutive 1s happened to appear in a message
Messages contain:
message type identifier (also used as priority indicator)
  all receivers observe and consume relevant messages
  message ID meanings are proprietary to manufacturers
control bits and up to eight data bytes
15-bit CRC field for error detection (all single bit errors detected)

## Slide 17: CAN frame types
There are 4 kinds of CAN bus messages (frames)
Data – ECU broadcasts message to all other ECUs
Remote – sent to request data from a specific node
Error – transmitted by node detecting a bus error
Overload – (OBSOLETE) request more delay between data/remote frames
Examples
blinker ECU sends data frame with data indicating its state in order to
  turn on blinker lights
  turn on clicker sound and indicator on dashboard
  suppress lane departure warning
central locking controller needs to know if the car is in park
  it sends a remote frame to TCU requesting park status
  TCU responds with data frame containing park status

## Slide 18: Data frames (CAN 2.0 format)
Just for concreteness, let’s describe a CAN data frame (classic format)
Start of Frame (1 bit) equals 0
Message ID (11 bits in base CAN, 29 bits in extended CAN)
  standard and extended frames may coexist, standard having higher priority
Remote Transmission Request (1 bit) 0 in data frames, 1 in remote frames
Reserved (2 bits) set to 0
Data Length Code (4 bits) number of data bytes 0…8)
Data (0…8 bytes) serialized information, MSB sent first
Cyclic Redundancy Check (15 bits)
ACK (2 bits including Ack delimiter) indicates previous message passed CRC
End of Frame (7 bits) all 1s

## Slide 19: CAN serialization
In serial protocols
serialization is the process of formatting data into a sequence of bits
deserialization is the recovery of data structures from the bit stream
The CAN specification details its serialization functions, such as
MSB is always transmitted first
big-endian / little-endian for multibyte data is manufacturer dependent
fields need not start on byte boundaries
bit stuffing
  a maximum of 5 consecutive 0 or 1 bits is allowed
  if the data has >5 identical bits an additional opposite bit is inserted

## Slide 20: CAN diagnostics
CAN bus scanners are used by technicians to diagnose problems
A CAN connector is located under the hood and/or under the dashboard
The scanner receives and logs all CAN messages
Another use is emissions conformance testing
during annual test or when requested by authorities
All modern cars have OnBoard Diagnosis II usually based on CAN

## Slide 21: Higher layers
CAN defines L1 and L2, but leaves higher layers to other protocols, e.g. :
These protocols standardize message identifiers, set-up procedures, etc.
ARINC | DeviceNet | Modbus
CanKingdom | EnergyBus | NMEA 2000
CANopen | ISO 11783 (ISOBUS) | OSEK/VDX
CANopen Lift | J1939 | SDS
CCP/XCP | MilCAN | UAVCAN

## Slide 22: CANOpen
As an example let’s look a bit at CANOpen from CAN in Automation
Every CANopen device implements CAN for L1 and L2
but for many message types the 11-bit CAN id is divided into
4-bit function code
7-bit CANopen NodeID (DA)
Starting/resetting a device is controlled via a state machine with states :
Initialization
Pre-operational
Operational
Stopped
Transitions between states are made by sending a
Network ManagemenT object to the device

## Slide 23: CANOpen device components
Every CANOpen device must implement
an object dictionary (with standardized format)
an application part
a communication unit
CANOpen uses variables for configuration and for measurement data
variables are stored in the device’s object dictionary (vector w/ 16 or 16+8 bit index)
CANOpen functions are implemented in each device’s application part
and only operate when the device is in operational state
The communication unit implements CAN
and at least the IDs in this table
PDO: Input and output values (voltage, frequency, etc.)
SDO: Configuration settings (node ID, baud rate, offset, etc.)
Communication object | Communication object ID (hex)
NMT (node control) | 0
Global failsafe command | 1
Sync protocol | 80
Emergency (error detected) | 080 + NodeID
TimeStamp | 100
Process Data Object | 180/200/280/300/380/400/480/500 + NodeID
Service Data Object | 580/600 + NodeID
heartbeat | 700 + NodeID
LSS | 7E4, 7E5

## Slide 24: CANOpen operation
Variables in an object dictionary are void, Boolean, (un)signed integer, float or char
Every node implements a server that handles read/write from/to its object dictionary
via CANOpen SDO messages
CANOpen defines addresses / ranges in the dictionary for specific variables
For example
the master might write true to a variable to start a measurement
and afterwards acquire the result by reading a float variable
Process data (data that changes over time) is also stored in the object dictionary
but the overhead of polling and receiving single responses would be excessive
So data in the PDO segment of the object dictionary can be sent without being polled (event/time driven) via PDO messages
In addition the CANopen master can get a system snapshot
by sending a SYNC message to which multiple nodes respond

## Slide 25: CANOpen modes in modern terms
CANOpen implements a confusing mixture of operational modes
NMT operates in master/slave mode
where the master issues state machine change commands
SDO operates in client/server pull mode
in which the client queries the server that replies with data
PDO operates in push mode
where an ECU sends information without polling
Heartbeat protocol also operates in push mode
to monitor verify nodes in the network are still alive
Node guarding operates in a mixture of master/slave and pull mode
monitoring the NMT state of a device

## Slide 26: LIN bus
LIN bus is a very different ECU bus protocol
designed to be cheaper than CAN bus
uses a single wire instead of 2-wire
lower reliability (but guaranteed latency)
limited to 40 m of cabling
very low data rates (19.2 kbps or 20 kbps, depending on variant)
master-slave operation (single master node and up to 16 slaves)
no node synchronization to save on expensive crystal oscillators
LIN arrived after CAN (about 1998), and
was developed by the LIN consortium (Audi, Volvo, VW, BMW, Mercedes)
along with Volcano (Mentor Graphics) and Motorola (Freescale, NXP)
LIN is commonly used today as a sub-bus for CAN and Flexray

## Slide 27: LIN multiple access method
LIN slave nodes have 7-bit addresses (NADs)
composed of supplier ID + function ID + variant ID
and NADs can be automatically assigned
using Slave Node Position Detection
All communication is initiated by the master sending to a single slave
thus no collision avoidance is needed
The LIN master node decides what is transmitted
by maintaining a schedule table
A slave only transmits after being invited to do so by the master
however all nodes can read any data transmitted on the bus
The master invites itself to transmit when it needs to broadcast data

## Slide 28: LIN frames
A LIN bus frame consist of
Synchronization break (≥ 13 bits) Frame Alignment Sequence alternations
Synchronization (1 byte) 0x55 (LSB sent first)
Identifier byte (1 byte) message type = 6 ID bits + 2 parity check bits
Data bytes (2, 4, or 8 bytes)
Checksum byte
The master transmits a header that consists of a break signal
followed by synchronization and identifier fields.
Slaves respond with a data frame
that include 2, 4 or 8 data bytes plus 3 bytes of control information

## Slide 29: LIN frames
LIN defines multiple frame types
since the ID is 6 bits, there can be only 64 frame types in a system
Unconditional (ID=0…59) frames carry data and are sent to all nodes
Sporadic (unconditional message triggered by value change, not periodic)
Event-triggered – like sporadic, but several slaves can respond with same ID
Master request diagnostic (ID=60)
Slave response diagnostic (ID=61)
User-defined (ID=62)
Reserved (ID=63)

## Slide 30: FlexRay
FlexRay was developed by the FlexRay Consortium
(initially Freescale, Bosch, NXP, BMW, VW, Daimler, GM)
At the end of 2009, the consortium disbanded
but the FlexRay standard is now maintained by ISO
FlexRay was designed to be better than CAN bus
faster (10 Mbps)
more deterministic (when needed)
more fault tolerant
but also much more expensive (aimed at luxury cars)
The first FlexRay capable car was from BMW at the end of 2006
followed by Audi, Bentley, Mercedes, Lamborghini, Rolls-Royce, Volvo
Many believe that FlexRay will be completely replaced by Ethernet

## Slide 31: FlexRay wiring
FlexRay networks may be single channel (2 wire)
but are almost always dual channel (4 wire) for fault tolerance
In addition to these 1 or 2 pairs of Unshielded Twisted Pair
there are further ground and power wires
FlexRay networks can either be buses (like CAN or LIN)
or star topologies
or hybrids (star(s) hanging off the bus)
depending on requirements and cost

## Slide 32: FlexRay multiple access method
FlexRay enables Time Division Multiple Access for enhanced determinism
similar to WiFi, Passive Optical Networks, and some 2G cellular systems
All FlexRay nodes are synchronized to the same clock to within 10 μsec
and nodes only transmit during their allotted timeslots
The cycle is constant for a given network
and typically chosen between 1 and 5 millisecond
This cycle is divided into 4 segments:
Static Segment for time-triggered messages
Dynamic Segment for event-triggered messages (CAN-like)
Symbol Window for network startup and maintenance signaling
Idle Time used to maintain sync between nodes
SS
DS
SW
IT

## Slide 33: MOST
MOST is an automotive shared bus network for multimedia
There are variants at rates of 25, 50, 100, and 150 Mbps
and it can run over multi-wire copper (MOST50, MOST150)
or plastic optical fiber (MOST25, MOST100)
The lowest rate (MOST25) already supports 15 channels of
uncompressed CD-quality audio or compressed MP1 video+audio
MOST was created by OASIS Silicon (acquired by SMSC)
maintained since 1998 by the MOST Cooperation
The first MOST capable vehicle was released in 2001
and today it is supported by many automotive manufacturers
including almost all European ones (Audi, BMW, Mercedes-Benz, Volkswagen, Volvo, …)
as well as GM, Honda, Toyota and Hyundai

## Slide 34: MOST transport
MOST defines all layers of the protocol stack
At layer 1 MOST networks are
synchronous (like TDM and SDH/SONET)
differential Manchester coded
logical ring (≤ 64 node) topology
ring is actually N-1 point-to-point links with idle regeneration or add/drop at each node
At layer 2
MOST25 has 64 byte frames MOST50 has 128 byte frames
MOST100 has 256 byte frames MOST150 has 384 byte frames
and each frame contains (in addition to preamble and header)
control channel (2/4 bytes) for commands e.g., stop playing
synchronous channel for real-time streaming data (video or audio)
packet data channel for bulk/bursty data

## Slide 35: MOST network operation
Every MOST network has a timing master
that periodically generates frames
All are other nodes are timing slaves that:
receive the frame
synchronize with the preamble using a PLL
parse the frame and decides if it needs to process it
if no need to process: then the frame is forwarded as-is
if processing needed: process control and/or data information
add information in empty fields of the frame
transmit the frame to the next node on the ring
At the end the frame returns to the timing master

## Slide 36: Higher layers
MOST frames are aggregated into blocks
MOST High Protocol maps to layers 3 and 4
MOST Async Medium Access Control adaptation layer
can translate between MOST layer 2 and Ethernet
and between MHP and TCP/IP
At the application layer MOST devices are composed of function blocks
which define the API for controlling the device (e.g., radio or MP3 player)
and for network management (NetBlock - mandatory)
Each function block has an XML descriptor
The programming structure of MOST devices is also well defined
but describing it would take us too far astray

## Slide 37: Comparison so far
LIN
CAN-B
CAN-C
FlexRay
MOST100
speed
relative cost
20 kbps
125 kbps
CAN-A
10 kbps
1 Mbps
10 Mbps
100 Mbps
MOST150
MOST50
MOST25

## Slide 38: Limitations
There are already so many ECU networking protocols
why would anyone need something new?
Current protocols are limited in
speed – good enough for traditional uses
capabilities – hard to implement new paradigms
such as a computational resource ECU
interfaces – basically each higher layer is locked to a L1 and L2
resulting in many different networks in each vehicle
interoperability – most protocols have significant
manufacturer proprietary parts
This has led people to consider the modern universal standards
Ethernet for L1/L2 and the IP suite for L3+

## Slide 39: Why not Ethernet ?
However, Ethernet has many drawbacks that may make it inapplicable
Ethernet L1 was not designed for harsh environments (vibrations, acceleration, temperature)
standard RJ45 connectors do not tolerate vibration, gold contacts corrode, etc.
Ethernet copper L1 does not work well in noisy vehicle environments
and may itself produce excessive EMI/RFI
Ethernet cabling (e.g., CAT5 – 4 twisted pairs) is far too expensive
Ethernet does not have native reliability guarantees
Ethernet is asynchronous while many applications require synchronous operation
Ethernet does not natively distribute synchronization
Ethernet L2 can not guarantee latency in low μsec (for steering, ECU, TCU)
Ethernet flow bandwidth allocation is BE and not guaranteed
Ethernet’s popularity has resulted in multiple security issues
Bus Ethernet is no longer supported (see next slide)

## Slide 40: Bus vs. switched Ethernet
Ethernet originated as a peer-peer bus, similar to automotive networks
with coaxial cable as the physical medium
and CSMA/CD as the multiple access mechanism
But the bus physical topology was abandoned long ago
(unavailable after 10 Mbps rate)
in favor of switched Ethernet with a star topology
Switched Ethernet employs dedicated point-to-point links
from the switch to every node, and 2 nodes communicate via the switch
This already adds several disadvantages
it requires much more wiring and lengthens link lengths
it adds an expensive switch to the network
the switch is a single point of failure and a traffic bottleneck
switch
switch may be incorporated into 1 of the ECUs

## Slide 41: TCP/IP/Eth may never completely replace CAN
So there is the elephant in the room!
CAN bus frames contain between 0 and 8 bytes (0-64 bits) of data
to which base CAN adds 47 bits (extended CAN 67 bits)
But TCP/IP/ETH adds 656 bits of overhead! (20B L1, 22B L2, 20B L3, 20B L4)*
So the bandwidth ratio
With a 2 byte payload TCP/IP/Eth consumes > 10 times the bandwidth of base CAN!
So TCP/IP/Eth should only be used for ECUs with large payloads
and CAN is frequently still used for traditional ECUs
Of course, since we are talking about switched Ethernet this bandwidth is not shared like in CAN bus
but one could connect CAN devices point-to-point, but that is never done to save wiring!
*Note: with IPv6 the header size is 20 bytes longer - 816 bits
data(bytes) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TCP/IPv4 vs base | 13.96 | 12.07 | 10.67 | 9.58 | 8.71 | 8.00 | 7.41 | 6.91 | 6.49
TCP/IPv4 vs ext | 9.79 | 8.85 | 8.10 | 7.47 | 6.95 | 6.50 | 6.12 | 5.79 | 5.50

## Slide 42: What to do about it?
As mentioned, many modern systems retain CAN (or similar)
for services with short messages
reserving the IP/Ethernet network for services with long messages
SOME/IP has a built-in mechanism to concatenate messages
into a single IP UDP/IP or TCP/IP packet at the cost of some added delay
AUTOSAR’s Socket Adapter (between the IP stack and the application)
also has its own mechanism to concatenate messages
TCP’s Nagle algorithm combines small packets, but is disabled in SOME/IP
The IP suite has standardized header compression mechanisms
that reduce the TCP/IP headers to 3-4 bytes
but these are not used in automotive systems

## Slide 43: Ethernet-CAN gateways
It may be desirable to access CAN devices from Ethernet, for example:
accelerate firmware flashing of CAN devices
access CAN logging/diagnostics from a PC
enable communications between CAN and Ethernet ECUs
enable remote (cellular) monitoring/actuation of CAN devices
For this reason CAN-Ethernet gateways are presently available
switch
GW
CAN
Ethernet
OBD

## Slide 44: Industrial Ethernet
Ethernet is such a popular technology that many of its disadvantages
have been addressed in other contexts
In particular, Industrial Ethernet provides :
reliability – HSR and PRP redundancy mechanisms
harsh environments – M8 and M12 rugged watertight connectors, extended temperature range switch standards
low latency – EtherCAT (IEC 6158) MAC reduces latency,
          AVB/TSN can give latency bounds
But Industrial Ethernet is much more expensive than plain Ethernet
which is already much more expensive than CAN

## Slide 45: Broad-R Reach
Broadcom created a new Ethernet 100 Mbps L1 called BroadR-Reach
specifically for automotive networking
uses a single UTP cable, maximum length of 15 m
is full duplex over this single pair using echo cancellation DSP
uses PAM3 code pairs to achieve 3 bits per symbol to reduce analog BW and thus reduces crosstalk and can meet automotive EMI/RFI specs
uses a highly optimized scrambler to better de-correlate signals
IEEE has standardized this as 100BASE-T1 (802.3bw, 802.3-2015 Clause 96)
(the “1” stands for 1 pair, and this was followed by 1000Base-T1 802.3bp)
In 2011 the OPEN (One-Pair EtherNet) Alliance was formed
and Broadcom RAND licenses to all OPEN Alliance members
(currently > 300 members)

## Slide 46: What about timing and reliability?
Ethernet has completely replaced all previous networking technologies
(token ring, token bus, ATM, frame relay, …)
in many applications
but was never adopted for the most demanding environments
such as industrial control systems, vehicle control, video distribution
In particular, Ethernet could not meet ISO 26262 requirements
for mission-critical vehicle systems like braking or steering
This is because Ethernet is a asynchronous, Best Effort, technology
Recently special flavors of Ethernet have been developed
providing low delay high reliability
to help Ethernet conquer these applications as well

## Slide 47: TTTech
Another proprietary solution is Time Triggered Ethernet (TTE) from TTTech
TTE extends standard Ethernet for reliable time-critical applications
In 2011 TTE was adopted by Society of Automotive Engineers as AS6802
and later adopted by NASA and ESA for some space communications
TTE switches are Ethernet switches with
accurate synchronization
time-triggered flow control and traffic scheduling
bandwidth partitioning
Most of TTEs functionalities are now available
in 802.1 standard Audio Video Bridging and Time Sensitive Networking

## Slide 48: AVB
During 2005-2012 the IEEE Audio Video Bridging Task Group
addressed time-sensitive Ethernet, mostly for the home AV market
AVB extends switched Ethernet to
provide synchronization (timing over Ethernet frames)
low-latency
reliability
The following standards were developed by the AVB TG
802.1BA Audio Video Bridging (AVB) Systems
802.1AS Timing and Synchronization for Time-Sensitive Applications
802.1Qav Forwarding and Queuing for Time-Sensitive Streams
802.1Qat Stream Reservation Protocol
(Qav and Qat were absorbed into 802.1Q-2011)

## Slide 49: TSN
In 2012 the AVB TG was renamed TSN to handle additional use cases
industrial, infrastructure, vehicular/transportation, fronthaul, etc.
TSN fundamental principles:
highly accurate synchronization of Ethernet switches (better than 1 μsec)
protocol for reservation of resources (buffers, BW on links)
achieve bounded latency for time sensitive streams, using
  new time-based buffering/queuing mechanisms
  new frame preemption mechanism
achieve very high availability and very low PLR
  zero congestion loss
  1+1 replication + elimination mechanism
co-existence of BE and TSN traffic (up to 75%)

## Slide 50: Example TSN mechanism – preemption
802.1Qbu frame preemption was adopted in 2016 and absorbed into 802.1Q
When express frame(s) arrives and a normal frame is being transmitted
the packet transmission of the normal frame is temporarily suspended
the neighboring switch buffers the content received
the express frame(s) are sent and forwarded
the transmission of the normal frame is continued
the neighboring switch reassembles the outgoing packet and forwards
Optimal bandwidth utilization of background traffic for time aware shaping
and low-latency communication in non-scheduled networks

## Slide 51: Example TSN mechanism - Qbv Scheduler
T |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 |  | O | C | O | O | C | O | O | O
1 |  | C | O | O | O | O | O | C | C
2 |  | O | C | C | C | C | O | O | O
3 |  | O | O | O | O | C | C | C | O
N | repeat |  |  |  |  |  |  |  | 
selector
Gate Schedule
0
1
2
3
4
5
6
7
gates
CoS queues
PCP
In 802.1Qbv Ethernet’s 8 CoS queues are cyclically gated
like TDM timeslots and FlexRay’s slots
All switches are synchronized, so all gate at exactly the same time
Schedules are specified with granularity up to 1 ns (but implementations may be less precise)

## Slide 52: Simple use of 802.1Qbv - Cycling Queuing
Optimal use of time sensitive gating doesn’t scale
Cyclic queuing provides a (non-optimal) guaranteed delay upper bound

## Slide 53: 802.1AS (and IEEE 1588)
For some AVB/TSN mechanisms to work we need to distribute Time of Day
throughout the network
802.1AS is a simplified profile of IEEE 1588-2008 (Packet Time Protocol)
a protocol for distributing time over packet (Ethernet or IP) networks
802.1AS is plug and play
and can deliver time accurate to within ± 0.5 μsec
At any moment 802.1AS requires a single master clock in the network
but if there are more than one the best is automatically selected
If the master fails a backup master can take over within < 1 second
The master can obtain precise time from GPS
which is already present in every modern vehicle

## Slide 54: PTP operation
How does PTP (1588) work ?
PTP is a master-slave protocol (not client/server like NTP)
The basic idea is that the master
periodically sends packets with the precise time to all its slaves
Unfortunately the time in the packet received is stale
since it takes some unknown time
for the packet to travel from master to slave
So every now and then a ranging measurement is performed
and the stale timestamp can be corrected to yield the correct time

## Slide 55: How is ranging performed ?
The basic idea behind ranging is simple
master sends a packet to slave at time T1
packet is received by slave at time T2
slave replies to master at time T3
master receives reply time T4
We can not compare T1 and T4 with T2 and T3
since the clocks are not yet synchronized
but
T4 –T1 = round trip propagation time + slave processing time
T3 – T2 = slave processing time
so
T = (T4 –T1) – (T3 – T2 ) = round trip propagation time
Assuming symmetry (d12 = d34) ½ T is the required one-way propagation time
master
slave
T1
T2
T3
T4
t
t
sync
delay req
delay response

## Slide 56: Why is 802.1AS enough?
We said that 802.1AS is a simplified version of PTP
why is a simplified version sufficient for such a critical application?
PTP was designed for complex networks and ultra-high accuracy (sub-ns)
link lengths of 10s of kilometers
paths contain many hops
switches/routers may become congested
links/switches may fail
The maximum cable length of Broad-R Reach is 15m
which in copper wire translates to about 75 nanoseconds
(remember our goal is 500 ns accuracy!)
If the 802.1AS is incorporated into the Ethernet switch
then this is the entire time offset!
Even if not, we need to take into account only a single switch

## Slide 57: IEEE 1722
Another IEEE protocol you may encounter is 1722 - AVB Transport Protocol
used for multimedia and video cameras
IEEE 1722 enables interoperable streaming by defining:
media formats and encapsulations
raw and compressed audio/video formats
media stream synchronization mechanisms
latency normalization and optimization
multicast address assignment
IEEE 1722 packets sit over Ethernet with EtherType 88B5
but contain an addition header with control and identifier information
1722 can be used instead of MOST for high-rate video

## Slide 58: Security
One of the arguments against Ethernet is its (lack of) security
There is nothing inherently less secure about Ethernet (and TCP/IP)
but in practice there are more hackers knowledgeable in these
In both, there need to be at least mechanisms to
authenticate ECUs and handle malicious messages
block DoS attacks or at least limit rate
CAN is actually worse since its messages do not contain source addresses
and thus there is no way to source authenticate them
But the security issues become most serious
when connecting to external services
which is only envisioned for IP/Ethernet

## Slide 59: The IP suite
I assume that the IP suite (defined by > 10,000 RFCs) needs no introduction
IP itself (IPv4 and IPv6) defines layer 3 – the network layer
While not the transport protocol of the Internet (that’s MPLS …)
IP has become the world’s standard packet interface
The IP suite also includes protocols at other layers
4 transport (layer 4) protocols:
  UDP – unreliable and no congestion control
  TCP – reliable and congestion control
  SCTP – highly reliable and congestion control
  DCCP – highly reliable and congestion control
protocols under layer 3 (but not physical layer)
although IP is often transported over L2 Ethernet
protocols above layer 4 (IPSec, TLS, NTP, FTP, DNS, SMTP, …)

## Slide 60: SOME/IP
We finally arrive at SOME/IP, which as its name suggests, sits above IP
Some/IP was designed by BMW in 2011
Scalable service-Oriented MiddlewarE over IP
is a service-oriented middleware control messaging regime
for in-vehicle communication
Its design principles include:
support event notifications (like CAN, LIN or FlexRay)
support Remote Procedure Calls (request/response similar to MOST)
rely on UDP/IP and TCP/IP sockets for peer-to-peer communication
carry AUTOSAR packets
interface with GENIVI (Linux based automobile infotainment),
Android Automotive, and OSEK-OS

## Slide 61: Middleware ?
Software professionals define middleware
as a layer between the OS and applications
that simplifies development/delivery of applications
so that developers can focus on their application logic
The term is most frequently used
when linking new apps to legacy systems
when simplifying communications in distributed applications
Android, sitting between Linux and an app is actually middleware according to this definition
Networking professionals define middleware
as services above the transport (TCP) layer
but below the application environment (below application-level APIs)
HTTP, sitting between TCP and a browser is actually middleware according to this definition
SOME/IP is middleware according to both definitions
The term middleware was first used in a 1968
NATO Software Engineering Conference

## Slide 62: RPC
Remote Procedure Calls facilitate distributed computing
by enabling a program running on one processor
to call a procedure that executes on another processor
but coding the call as if it were a normal (local) procedure
RPCs are thus a form of inter-process communication (IPC)
in which the software doesn’t explicitly detail the communications
In modern systems such as SOME/IP
set and get operations are implemented using RPCs
event notifications are implemented using callbacks
Note that remote calls can fail because of network problems
so RPC calls may deal with not knowing whether the call succeeded
or wait (hang) for acknowledgement
Bruce Jay Nelson is credited with coining the term RPC in 1981

## Slide 63: Why another RPC protocol?
In the IP world there are already a number of RPC protocols
such as gRPC, Java’s RMI, XML-RPC, JSON-RPC, Microsoft RPC, SOAP, CORBA, … *
Why do we need a special one for automotive applications?
embedded applications in general
and mission-critical embedded in particular
are significantly different from the web or cloud-based applications
for which most RPC mechanisms were optimized
need to operate on small, computationally challenged, platforms
wire efficiency may be critical
need to match the CAN-like mindset of automotive developers
MOST function blocks contain methods that are similar to RPCs

## Slide 64: Basic SOME/IP stack
From a pure networking point of view
SOME/IP sits above TCP/IP (or UDP/IP)
providing services to the application layer
It is thus comparable to http
(and SOAP, websockets, gRPC, CORBA, Python’s urllib, .NET, etc.)
In many cases other layers may surround it
(e.g., in AUTOSAR it sits above the SoAD, which itself sits above TCP,
in GENIVI vsomeip and vsomeip-sd are shared libraries)
SOME/IP does not replace standard IP protocols
(e.g., DHCP, ICMP, ARP)
SOME/IP is mostly for control
not transport of large amounts of data (e.g., video)
So it will generally sit in parallel to AVB for that
Broad-R Reach
802.1Q
IPv4 / IPv6
TCP or UDP
SOME/IP
application

## Slide 65: A bit more complex stack with SOME/IP
In this example (which could be made much more complex)
SOME/IP is used for (e.g., windows, doors, reverse video, lane alert, etc.)
CAN (or LIN or FlexRay) is still used for traditional uses (Engine Control Unit, TCU, steering, etc.)
AVB Ethernet (1AS+1722) is used for audio/video (no need for SOME/IP!)
Broad-R Reach
802.1Q
ARP
TCP or UDP
SOME/IP
application
media player
IPv4
ICMP
DHCP
CAN
CANOpen
ECU, TCU
IEEE
1AS
1588
IEEE
1722

## Slide 66: SOME/IP basics
SOME/IP RPC is based on a client-server (provider/consumer) model
To emphasize this model SOME/IP uses the term service
rather than function, procedure, or method
In each transaction one ECU provides a service (function/method)
and another consumes that service (invokes function/method)
Different interaction types are supported:
request/response (RPC)
  invoke method without response (fire & forget)
  get/set (read/write field on remote ECU)
publication/subscribe (pub/sub) to receive event notification
SOME/IP has an optional service discovery mechanism

## Slide 67: Methods and fields
A method is a procedure, function or method run on a server ECU
A set method (AKA setter) is a method that writes a field
A get method (AKA getter) is a method that reads a field
An event method sends out event messages containing field values
A field is a variable on a server which has get, set and/or event methods
A field may be a status, a configuration parameter, a measurement, etc.
Note:
SOME/IP uses modern object oriented language
(method, getter/setter, callback)
but ECUs are still frequently programmed using old fashioned C

## Slide 68: Packet format
SOME/IP uses UDP and TCP (recommended to use UDP as much as possible)
Details of IP addresses and ports are given in an interface specification
Packet format:
Request ID (32 b)
Ethernet header
IP header
TCP or UDP header
Message ID (32 b)
Length (32 b)
Protocol ver (8b)
Interface ver (8b)
Message type (8b)
Return code (8b)
Payload (up to 1400 Bytes)
Ethernet trailer (FCS)
Note: SOME/IP packets are not IP fragmented

## Slide 69: SOME/IP port numbers
SOME/IP request response uses the standard port mechanism
response source port = request destination port
response destination port = request source port
Port 30490 is used for SD and never for anything else
Ports representing services are 30501, 30502, …
the precise mapping given in the Interface Specification
Note – 30490, 30501, etc. are in the IANA registered port range (1024-49,151)
but are NOT assigned to SOME/IP by IANA! (30401-30831 are unassigned)
If a client needs a temporary port number, it uses 30500
If any ECU needs a dynamic port number
it is selected from the ephemeral port range 49152-65535

## Slide 70: Transport Protocol
SOME/IP supports both UDP and TCP at L4 (SCTP is not supported)
the Interface Specification dictates which is used for each message type
UDP is used when there are hard latency requirements (<100ms)
TCP is used for large payloads (> 1400 Bytes)
w/o hard latency requirements (however, Nagling is disabled to reduce delay!)
exploiting TCP reliability mechanisms
(retransmission, reordering, but not segmentation)
For large payloads with hard latency requirements
a special UDP-only mode called SOME/IP-TP is defined
which uses a non-standard fragmentation mechanism

## Slide 71: Message ID
The 32 bit field contains an identifier
which identifies the nature of the RPC call or event
It is roughly similar to a CAN ID
and must be unique within the vehicle
The 32 bit field is divided into subfields identifying
the service
and a particular function of that service (which may be an event)
Service ID - 16 MSBs
Reserved - 1 bit
Method ID - 15 LSBs

## Slide 72: Request ID
The 32 bit Request ID is a message sequence number
and must be temporarily unique for a given client-server association
(it eventually wraps around …)
When a server responds to a client’s request
it copies the request ID from the request’s Request ID field
into the response’s Request ID field
In this way the client unambiguously knows
to which request this response
even if there are multiple outstanding unanswered requests
Request IDs must not be reused by a client
until the response arrives or the response has timed out

## Slide 73: Request ID (cont.)
In some implementations (e.g., AUTOSAR)
the 32-bit Request ID field is subdivided into subfields
Client ID (16 bits) : unique in the vehicle
Session ID (16 bits) : unique for the client
incremented mod 216 for each new session
Client ID is unique identifier for the calling client
This structure facilitates a logger to identify the client of each message
and allows a client to differentiate between multiple sessions
calling the same function

## Slide 74: Message types
The message type byte is used to differentiate between operational modes
The latest* definitions are (we’ll discuss their usage later)
0x00 REQUEST (request a response)
0x01 REQUEST_NO_RETURN (fire & forget request)
0x02 NOTIFICATION (event callback – no response expected)
0x80 RESPONSE
0x81 ERROR (response with error)
The 3rd MSB (xxTx-xxxx) of the message type is the TP bit
which is set to 1 when using TP mode (e.g., TP_REQUEST is 0x20)
*Note – some older message types have been obsoleted because of lack of use:
REQUEST_ACK, REQUEST_NO_RETURN_ACK, NOTIFICATION_ACK, RESPONSE_ACK and ERROR_ACK

## Slide 75: Return code
The final header byte is the 1-byte return code
which is used by RESPONSE and ERROR type messages
to indicate whether a request was successfully processed
For all other messages types the Return code is set to zero
The following Return codes are currently defined :
0x00 no error (can not be sent in ERROR messages)
0x01 unspecified error
0x02 unknown service
0x03 unknown method
0x04 not ready (server not yet running)
0x05 unreachable
0x06 timeout
0x07 incorrect protocol version
0x08 incorrect interface version
0x09 malformed message (transformer deserialization error)
0x0A wrong message type

## Slide 76: SOME/IP transformer
The SOME/IP transformer
transforms data structures into and from on-wire representation
performing a function similar to CAN’s serializer/deserializer
However, unlike CAN’s simple static-sized fields
the Transformer can handle dynamic lengths and structures
The serialization is big-endian and network byte order (RFC 791)
The Interface Specification may dictate message field alignments

## Slide 77: Transformer data types
The following basic data types are defined
boolean
uint8, uint16, uint32, [uint64], sint8, sint16, sint32, [sint64]
float32, float64
More complex types can be built based on these using
(multidimensional) arrays
C-like structures
Strings are built using Unicode arrays terminating in 0
(although their length is always determined by the message length)

## Slide 78: Operational modes
SOME/IP services use 4 messaging modes
Request/Response
(basic RPC)
Field interactions
  (special case of request response)
Fire & forget
(like procedure or void function)
Event notification
(similar to fire & forget but from server to client)
Server
Response
Event
Event
Event
Request
Client
Response
Get/Set
Event
Request

## Slide 79: Request/Response
When a client desires to invoke a method on a server
and to receive a response
(pass/fail, status, result of calculation, measurement, etc.)
it sends a request message with message type 0x00 REQUEST
Once it is completed running
the server sends back to the client a response message
with message type 0x80 RESPONSE
providing the results of the method (its returned value)
in the payload
It further sets the Return Code (if all OK - 0x00 no error)

## Slide 80: Fire & forget
When a client desires to invoke a method on a server
and doesn’t require a response (procedure, void function)
it sends a request message
with message type 0x01 REQUEST_NO_RETURN
This is called fire & forget (for obvious reasons)
No SOME/IP response is sent by the server
if the message is over TCP
the client knows that the RPC message was received
if the message is over UDP
the client never knows …

## Slide 81: Set/Get
Setters and Getters are simply special cases of methods
with the single purpose of accessing a field
Set and get messages are thus identical to request/response messages
but usage and encoding in the server ECU software differ
Getters can be used for polling a value when needed by the client
instead of having the server periodically send field events
Note that delay critical processes prefer to store the last received value
rather than requesting an update
Setters need not be used for triggering processes (as they are in CAN)
since methods can be directly invoked using request or fire & forget
Setters are often used for configuration and configuration changes

## Slide 82: Event Groups
In SOME/IP events are aggregated into event groups
to which an ECU can subscribe
Note that you can’t subscribe to an individual event, only to its group
For example, a tire air pressure warning system might have:
Event group 1 – pressure monitoring
  Event 1.1 front left tire pressure changed
  Event 1.2 front right tire pressure changed
  Event 1.3 rear left tire pressure changed
  Event 1.4 rear right tire pressure changed
Event group 2 – pressure warnings
  Event 2.1 front left tire pressure under threshold
  Event 2.2 front right tire pressure under threshold
  Event 2.3 rear left tire pressure under threshold
  Event 2.4 rear right tire pressure under threshold

## Slide 83: Event messaging
A server ECU wishing to announce an event
(usually periodically, upon change, or upon threshold passing)
sends a message with message type 0x02 NOTIFICATION
to all subscribed clients
The method ID subfield of the Message ID is the Event ID
Subscription may be made via SD, or may be configured
Events do not have lifetimes (although service discovery does)
A special case of event messaging is for status fields
field events send out an initial value event
if Explicit Initial Data Control is supported (all modern implementations)

## Slide 84: Interface Specification
The SOME/IP standards (and other frameworks use along with SOME/IP)
can not, and does not attempt to,
completely specify everything needed to run an actual system
each manufacturer has its own system design
new features and ECU types are being added all the time
Hence every SOME/IP system has an Interface Specification specifying
the ECUs in the system and their interconnectivity (addresses, clusters, etc.)
services supported by each ECU (with their port number and Service ID)
events, event groups, fields for each ECU (with message alignments)
whether to use TCP, UDP, TP for each message type
The Interface Specification is typically encoded in XML, e.g., in
FIBEX (Field Bus Exchange Format) used for CAN, FlexRay, MOST, and SOME/IP
AUTOSAR XML (ARXML)

## Slide 85: FIBEX
FIBEX specifies UML and XML formats
for configuring multiprotocol automotive networks
completely specifying all needed elements and databases
It was developed by the German-incorporated ASAM consortium
Association for Standardization of Automation and Measuring Systems
as ASAM MCD-2 NET (presently in version 4.1.x)
FIBEX is used in design, configuration, monitoring and simulation
and supports auto-generation of ECU software and testing tools
FIBEX defines
services provided and consumed for each ECU
network topologies (ECUs, network ports, gateways, connectors)
signals allowed to be sent and received for each ECU, triggers, timing, etc.
technology-specific description of each port

## Slide 86: ARXML
ARXML is an XML schema (actually arxml is the file extension)
for describing AUTOSAR-based systems
It is derived from the AUTOSAR metamodel
and used to generate other files (Run Time Environment, Basic SoftWare)
The ARXML file contains the Application Interfaces table, which includes
Compositions (body, powertrain, occupant safety, multimedia, telematics, HMI, … )
Components
Ports
Port interfaces
Data types
Units
Instances of component types
AUTOSAR is a complete universe
that can’t be covered here

## Slide 87: SOME/IP Service Discovery
In classic automotive systems the services are all preconfigured
there is simply no need to add anything to the system
(who ever heard of adding a new engine while driving?)
In modern systems
new services may be added to existing systems
  new gadgets or smartphones
servers may appear and disappear
  driver may turn devices on/off
there may be multiple providers of the same service
  for redundancy or for load balancing
services may be external to the vehicle
  infrastructure road closure alert system
  emergency lane change services of nearby cars
Hence service discovery is available, but optional, in SOME/IP
  when not used, configuration is in the Interface Specification

## Slide 88: SOME/IP Service Discovery details
SOME/IP SD enables
locating services by type
monitoring service instance availability (running)
subscribing to a service’s events
SD commands
Service: Find, Offer, and StopOffer
Event groups: Subscribe, StopSubscribe, SubscribeAck, and SubscribeNack
SD runs over UDP/IP multicast (unicast) with port number 30490
Services have TTL (typically 2 seconds)
so that services timeout unless refreshed by a periodic service offer
This prevents a client from hanging upon network problems
or if the server dies without sending StopOffer

## Slide 89: Example messaging flow with SD
Server
Offer Service
Subscribe
Subscribe ACK
Event
Event
Event
Find Service
Client

## Slide 90: SD packet format (omitting lower layers)
SD packets use the standard SOME/IP header with:
Service ID 0xFFFF
Method ID 0x8100
Client ID 0x0000
Session ID increments as usual
Message type 0x02 NOTIFICATION
Return code 0x00 No error
Request ID (32 bit)
Protocol ver (8b)
Interface ver (8b)
Message type (8b)
Return code (8b)
Flags (8b)
Reserved (24b)
Length of Entries (32 bit)
Entries array
Length of Options (32 bit)
Options array
Length (32 bit)
Message ID (32 bit)
Client ID 0000
Method ID 8100
Session ID
Service ID FFFF
2
0
1
1

## Slide 91: SD flags
3 flags are currently defined, of which only 1 is important :
Reboot flag (MSB) equals 1 after reboot until Session-ID wraps around
thereafter set to 0
note that reboot is detected in steady state by this flag changing
Unicast Flag (historical) set to 1
Explicit Initial Data Control Flag (legacy)
set to 1 if the server ECU sends an initial value for field events

## Slide 92: Entries array
The entry array is used to detail
the services (format 1) and
the event groups (format 2)
Type values
0 – Find
1 – Offer, StopOffer
2 – Subscribe, StopSubscribe
3 – SubscribeAck,
StopSubscribeNack
Type
index 1st options
index 2nd options
#
1st options
#
2nd options
TTL
Service ID
Instance ID
Major
version
Minor version
counter
Event group ID
reserved

## Slide 93: Options array
Options define
IPv4 or IPv6 addresses
unicast/multicast
L4 transport protocol
port numbers
load balancing
configuration strings
human-readable name
and name=value pairs
Example formats:
Length
Type 1
Configuration string
reserved
Length
Type 4
reserved
reserved
IPv4 address (32 bit)
L4 proto
port number
Length
Type 6
reserved
reserved
IPv6 address (128 bit)
L4 proto
port number

## Slide 94: SOME/IP start-up time
Vehicle networks are expected to start-up in sub-second times, including
powering up ECUs
software boot time
network auto-configuration
service discovery (for mission-critical services)
SOME/IP networks require many more steps than CAN networks
Ethernet – flooding and MAC table population
IP – optional DHCP address acquisition
TCP – 3-way handshakes
SOME/IP SD – service advertisement, (find), offer, subscribe
network is considered functional
when all clients have found all required services
SOME/IP – first requests
but due to higher rates, each step is much faster
Vacuum-tube based televisions would take tens of seconds to warm-up
Modern entertainment systems take about the same amount of time
due to software initialization times
In practice, SOME/IP often boots in less than 10 ms !

## Slide 95: SOME/IP example
An ADAS system client needs to receive warnings
from a video object recognition system server (service 1111)
Event group 2222 of service 1111 contains events such as
lane crossing
zebra crossing
pedestrian in street
obstruction ahead
How does SOME/IP handle this?
Assume that the Interface Specification defines
Server has IPv4 address 10.1.1.100 | Client has IPv4 address 10.1.1.200
SD multicast address 239.1.1.100 | Service ID 1111, Event group=2222

## Slide 96: SOME/IP example message flow
Client sends FIND SD message
SA=10.1.1.200, DA=239.1.1.100 (multicast), UDP DA_port=30490
Type=0, Service_ID=1111 (no options)
Server sends OfferService
SA=10.1.1.100, DA=10.1.1.200, UDP DA_port=30490
Type=1, Service_ID=1111 options : IPv4, unicast, UDP, port=30502
Client sends SD Subscribe message
SA=10.1.1.200, DA=10.1.1.100, UDP DA_port=30502
Type=2, Service_ID=1111, Eventgroup=2222 options : port=49200
Server sends SD SubscribeAck
SA=10.1.1.100, DA=10.1.1.200, UDP SA_port=49200 DA_port=30490
Type=3, Service_ID=1111 (no options)
Server sends SOME/IP Event message
SA=10.1.1.100, DA=10.1.1.200, UDP SA_port=30502, DA_port=49200
Type=2, Return_code=0, serialized data of the event
Client 10.1.1.200
Server 10.1.1.100
SD Find
SD Offer
SD subscribe
Event
Subscribe ACK

## Slide 97: SOME/IP (lack of) security
Use of Ethernet and the IP suite enlarges the attack surface
as compared to simpler automotive networks
Unfortunately, the rapid development of the field
the re-use of existing insecure IoT software
the lack of security experience of automotive engineers
false belief in security via obscurity
have greatly worsened the situation
SOME/IP’s RPC mechanism has no built-in security mechanisms!
SOME/IP has the arsenal of Ethernet and IP suite security tools available
but in practice these are not currently used
The situation parallels that of 3G cellular systems
where R&D teams were clueless regarding security

## Slide 98: A few points
In order to help debugging and diagnostics
SOME/IP SD includes human readable (text) service names
in addition to the unique identifiers
This is a extremely hacker-friendly feature!
There is one security feature in the standard!
SOME/IP service find and offer messages are usually multicast
but may be unicast instead
This idea is to prevent unexpected ECUs from subscribing to a service
at the cost of knowing a priori which clients need to subscribe
and thus obviating the need for the service offer!

## Slide 99: Some possible attack vectors
Attacks are usually distinguished according to
requiring physical access to the Ethernet network
requiring only remote access (exploiting V2X communications)
but the line is blurry because of gateways
Current remote attacks typically
enter via the cellular or WiFi networks
pwn the entertainment system (Ethernet, FlexRay or MOST)
usually via standard spoofed ID, over-runs, malformed packets, etc.
jump via a gateway to other networks (including CAN)
Fortunately, anomaly detection may be simpler in vehicular systems
One company with solutions in this field is Argus Cyber Security

## Slide 100: A MitM attack on SOME/IP SD
A malicious ECU (either surreptitiously connected or a legitimate ECU that has been pwned)
listens for service offers
Upon receiving one it subscribes to the service
and commences sending service offers for the same service
If timed correctly it can cause client ECUs
to subscribe to its service
instead of the legitimate one
It then performs standard Man in the Middle tactics
either passively extracting information
or actively modifying information
ECU Alice (server)
ECU Bob (client)
ECU Eve
SD Offer
SD Offer
SD subscribe
SD subscribe
Event
Event

## Slide 101: THE END Thanks for your attention
Yaakov (J) Stein