## Slide 1: vAccess Technology Backgrounder
Yaakov (J) Stein
CTO

## Slide 2: Virtualization and NFV
In the field of computation, there has been a major trend towards virtualization
Virtualization means the creation of a virtual machine (VM)
that simulates an independent physical computer
A VM is software that emulates hardware (e.g., an x86 CPU)
over which one can run software as if it is running on a physical computer
CPUs are not the only hardware device that can be virtualized
Network Function Virtualization means
running network functions as software on a CPU or VM
The virtualized function is called a VNF

## Slide 3: Virtualization and NFV
NFV enables
using standard COTS hardware (whitebox servers)
  reducing CAPEX and OPEX
fully implementing functionality in software
  reducing development and deployment cycle times, opening up the R&D market
consolidating equipment types
  reducing power consumption
optionally concentrating network functions in datacenters or POPs
  obtaining further economies of scale, enabling rapid scale-up and scale-down
DO NOT be confused!
White box switch means an SDN (e.g., OpenFlow) switch
most frequently an inexpensive configurable hardware switch
possibly a configurable software switch (e.g., Open vSwitch)
White box server means a COTS computation platform
most frequently an x86-based CPU or VM capable of running VNFs
possibly combined with networking functionality

## Slide 4: Distributed NFV
RAD developed the idea of optimally relocating VNFs in the network
from the edge (CPE) through aggregation through PoPs and HQs to datacenters
This is called Distributed-NFV (DNFV)
Optimal location of a functionality needs to take into consideration:
resource availability (computational power, storage, bandwidth)
real-estate availability and costs
energy and cooling
management and maintenance
other economies of scale
security and privacy
regulatory issues
For example, consider moving a DPI engine from where it is needed
this requires sending the packets to be inspected to a remote DPI engine
If bandwidth is unavailable or expensive or excessive delay is added
then DPI must not be relocated
even if computational resources are less expensive elsewhere!

## Slide 5: Edge NFV
A natural place for some network functionalities, for example:
  end-to-end encryption
  end-to-end performance monitoring
  delay sensitive preprocessing
is the Customer Premises Equipment
The combination of DNFV and CPE is called vCPE
Note that some people use the following terminology:
vCPE – virtualizing of CPE functionality and relocating in the cloud
uCPE – providing hosting capabilities in the CPE and relocating to it
While initially ridiculed,
vCPE is now considered a sweet spot for NFV deployment

## Slide 6: Two problems
There are two problems with using pure whitebox servers as CPEs
whiteboxes often lack required interfaces (e.g., T1/E1)
some functions (e.g., encryption) may be too compute-intensive
for pure software to handle
Network
CPE
Customer Site
Customer
Network
Hypervisor
VNF
VNF
NFV
orchestrator

## Slide 7: Two solutions
There are two ways to combine vCPE and hardware interfaces/acceleration
Gray box / Whitebox+ (e.g., ETX-2iB with DNFV module)
  start with a physical CPE
  augment it with a (possibly pluggable) server
  where physical CPE has the required interfaces and hardware processing
Whitebox with pluggable acceleration
  start with a pure server platform
  plug into it hardware modules (SFP, GPU, M.2, etc.)
    where these modules provide two basic functions:
    needed physical interfaces
    needed computation power

## Slide 8: What is vAccess ?
A service provider wants to use a basic whitebox with SFP cage interfaces
The traffic is IP based (IPv4 or IPv6)
which for most locations is delivered over Ethernet
but some locations are only served by TDM (E1/T1, n*E1/n*T1, ...)
RAD’s solution is to provide TDM interfaces by MiToP (renamed MiRIC-ML)
plugged into SFP cages
If there are multiple TDM links, they are bonded together using MLPPP
where the MLPPP processing is performed by a VNF in the whitebox
A rough diagram of this solution is as follows:
whitebox server
MiRIC-MLs
SFP cages
MiRIC driver
vAccess
VNF
N TDM links
(N = 1 ... 4)
customer premises
IP over MLPPP over HDLC over T1/E1
internal
TDM PW

## Slide 9: Formats along the way ...
whitebox server
framed unchannelized TDM
HDLC
MLPPP
IP (no Ethernet)
Ethernet’
IP packet
Ethernet
IP packet
Ethernet terminated!
Ethernet terminated!
Ethernet
IP
UDP
TDM PW (CW)
MLPPP
IP packet
Note: an internal TDM PW is required
since the SFP interface transports Ethernet
TDM PW → TDM
IP → MLPPP VNF

## Slide 10: So – what do we have to learn?
In order to understand how vAccess works, we will need to understand:
IP and Ethernet (won’t delve deeply here)
Packets in TDM (HDLC)
PPP
MLPPP
TDM PWs
For these, we will need to cover the following standards
ISO 3309 HDLC
RFC 1661 PPP (ex 1548)
RFC 1662 PPP in HDLC framing (ex 1549)
RFC 1990 ML-PPP (ex 1717)
RFC 1994 PPP CHAP (ex 1334)
G.702, G.703 unstructured and structured TDM
RFC 4553, 5086 TDM PWs

## Slide 11: Data over TDM

## Slide 12: TDM
Time Domain Multiplexing is the base technology
for the digital Public Switched Telephone Network
TDM is used today to mean any Constant Bit Rate signal
with one of the data rates listed in G.702
if framed – with 8000 frames per second (since analog audio was 4 kHz)
The data-rates are arranged in a hierarchy (DS0, DS1, DS2, ...)
but are different in different parts of the world
Notes:
TDM signals need not be framed
Even if framed, TDM need not be divided into channels (timeslots)
if framed, higher data rates mean longer frames (unlike OTN)
Whether channelized or not
  TDM need not carry voice
  but can be used to transport arbitrary data (e.g., IP packets)

## Slide 13: G.702 rates
64 kbps
2.048 Mbps
1.544 Mbps
1.544 Mbps
6.312 Mbps
6.312 Mbps
8.448 Mbps
34.368 Mbps
139.264 Mbps
44.736 Mbps
32.064 Mbps
97.728 Mbps
274.176 Mbps
CEPT
North America
Japan
DS4
DS3
DS2
DS1
DS0
* 30
* 24
* 24
* 4
* 4
* 4
* 4
* 7
* 6
* 4
* 5
* 3
E1
E2
E3
E4
T1
T2
T3
T4
J1
J2
J3
J4

## Slide 14: TDM Structure
unstructured TDM (TDM = arbitrary stream of bits)
structured TDM
…
SYNC
TS1
TS2
TS3
signaling
bits
…
…
TSn
(1 byte)
channelized (single byte timeslots)
S
Y
N
C
framed (8000 frames per second)
S
Y
N
C
S
Y
N
C
multiframed
frame
frame
frame
…
frame
multiframe

## Slide 15: Packet to bit stream
There is a problem when transporting IP or Ethernet over TDM:
IP and Ethernet consist of packets
TDM signals consist of continuous bit streams
There are two ways to carry frame packets into a bit stream
  by sending an idle codes on the TDM when there is no traffic (HDLC)
  by sending frames all the time, but idle frames when no traffic (GFP)
packet 1
packet 2
packet 3
packet 4
packet 1
packet 2
packet 3
packet 4
packet 1
packet 2
packet 3
packet 4
idle
idle
idle codes

## Slide 16: HDLC
ISO developed High-Level Data Link Control based on IBM’s SDLC
HDLC uses a flag (hex 7E = 01111110)
as an idle code when there is nothing to send
to separate packets (at least one flag must appear between packets)
So when there is no traffic
the TDM looks like this ...0111111001111110011111100...
Notes:
some implementations use flags as delineators (beginning and end)
and so require 2 flags between packets
some old implementations use all ones as idle and flags as delineators
some implementations allow “zero sharing”
  so that 2 consecutive flags look like this 011111101111110
7E
7E
7E

## Slide 17: HDLC flags
But the flag (7Es – exactly 6 consecutive ones)
must never appear in valid data inside a packet!
otherwise it will be misinterpreted as a delineator
If we have access to the physical layer we can mark these (“violations”)
Otherwise (we only access bits) we must disallow the idle code
There are two methods of disallowing flags
bit stuffing (zero insertion)
byte (octet) stuffing

## Slide 18: Bit stuffing / zero insertion
ECMA-40
Whenever the encoder sees 5 successive 1s it appends a 0
  thus there are never 6 successive 1s in the data
When the decoder sees 5 successive 1s :
If the next bit is a 0 it is deleted
If the next bit is a 1 then this is the closing flag
Notes:
bit stream length is no longer necessarily divisible by 8
bit stream length is not a priori predictable
worst case expansion is 20%
encoding/decoding is easy in hardware, hard in software

## Slide 19: Byte (octet) stuffing
RFC1549
Whenever the encoder sees hex 7E
  It replaces it with 7D 5E
Whenever the encoder sees hex 7D
  It replaces it with 7D 5D
Optionally other codes (e.g. some under hex 20) can be “escaped”
  Second byte is original with 6th bit complemented (xor with hex 20)
  e.g. ^Q = hex 11→ 7D 31 ^S = hex 13 → 7D 33
When the decoder sees 7D xx
  It replaces it with the original byte (complementing 6th bit)
Notes:
bit stream remains byte oriented
length expansion is typically about 1%, but can range from 0 to 100% !
(there is also a consistent overhead byte stuffing algorithm (≈0.4%) – but it is not in use)
encoding/decoding is easy in software!

## Slide 20: HDLC framing
HDLC frame is bounded by flags, and has a particular structure
Many variants (SDLC, ISO, LAPB, LAPD, LAPF, LAPS, SS7, PPP-HDLC, Cisco-HDLC, etc)
Address:
There may be no address (e.g., SS7 HDLC)
SDLC always had 8 bit addresses
ISO 3309 HDLC has structured multibyte addressing
  Service Access Point Identifier (MSB of SAPI =1 may indicate broadcast/multicast)
  EA=1 means 8 bit, EA=0 means extended address
  C/R=1 for commands, C/R=0 for responses
The single byte hex FF is recognized as the broadcast address
flag (8)
flag (8)
address (0/8/16)
ctrl (8/16)
data
FCS (16/32)
EA
C/R
SAPI
EA

## Slide 21: HDLC control
HDLC networks can be configured to be:
Balanced – all stations have equal responsibility
Unbalanced – primary and one or more secondary stations
and HDLC can operate :
Best effort (datagram)
  uses Un-numbered (U) frames
Reliable (Asynchronous Balanced Mode)
  uses frames with sequence numbers in control field
    Information (I) frames (data + acknowledgement)
    Supervisory (S) frames (only acknowledgement)
The various frame types are indicated by the control field
  which varies widely between different protocols

## Slide 22: HDLC FCS
HDLC uses a Frame Check Sequence to detect errors
Frames with incorrect FCS are typically discarded
Link Quality can be monitored due to the FCS
Packet Loss Ratio can be calculated by counting packets with bad FCS
Bit Error Rate can also be estimated
The FCS is implemented as a shift-register (CRC)
CRC-16 X16 + X12 + X5 + 1
CRC-32 X32 + X26 + X23 + X22 + X16 + X12 + X11 + X10 + X8
+ X7 + X5 + X4 + X2 + X + 1
Some HDLC-based protocols require 32 bit FCS
Some mandate 16 bit FCS
Some allow 16 bit but recommend 32 bit FCS

## Slide 23: GFP
Defined in ITU-T G.7041 (also numbered Y.1303)
Unlike HDLC, GFP continuously transmits frames (no idle codes)
any idle time between GFP frames is filled with GFP idle frames
GFP handles various client and server networks
Client may be PDU-oriented (Ethernet MAC, IP)
  or block-oriented (GbE, fiber channel)
GFP frames
  are octet aligned
  contain at most 65,535 bytes
  consist of a header + payload area
Ethernet
IP
other
GFP – client specific part
GFP – common part
SDH
OTN
other
HDLC
PDH

## Slide 24: GFP frame structure
Every GFP frame has a 4-byte core header
  2 byte Payload Length Indicator
  PLI = 01,2,3 are for control frames
  2 byte core Header Error Control
  X16 + X12 + X5 + 1
  entire core header is XOR’ed with B6AB31E0
  so idle frames are B6AB31E0 (Barker-like codes)
Idle GFP frames
  have PLI=0
  have no payload area
Non-idle GFP frames
  have ≥ 4 bytes in payload area
  the payload has its own header
  2 payload modes : GFP-F and GFP-T
  optionally protect payload with CRC-32
  payload is scrambled like PoS
PLI (2B)
cHEC (2B)
payload header
(4-64B)
payload
optional payload
FCS (4B)
core
header
payload
area

## Slide 25: GFP payload header
GFP payload header has
  type (2B)
  type HEC (CRC-16)
  extension header (0-60B)
    either null or linear extension (payload type muxing)
  extension HEC (CRC-16)
type consists of
  Payload Type Identifier (3b)
    PTI=000 for client data
    PTI=100 for client management (OAM dLOS, dLOF)
  Payload FCS Indicator (1b)
    PFI=1 means there is a payload FCS
  Extension Header ID (4b)
  User Payload Identifier (8b)
    values for Ethernet, IP, PPP, FC, RPR, MPLS, etc.
type (2B)
tHEC (2B)
extension header
(0-58B)
eHEC (2B)
UPI (8b)
PTI (3b)
EXI (4b)
PFI

## Slide 26: PPP

## Slide 27: Point to Point Protocol (RFC 1661)
PPP is a method for transporting datagrams between 2 peers
over full-duplex, point-to-point data links
  for example: short lines, leased lines, dial-up modems
PPP was originally designed for dial-up modems
but may be used to connect hosts to routers, and routers to routers
instead of Ethernet
PPP has 3 components:
the PPP encapsulation method for (multiprotocol) datagrams
the Link Control Protocol for establishing, configuring,
and testing data-link connections
Network Control Protocols for establishing/configuring higher protocols, e.g.:
  IPCP RFC 3241 (ex 1332, ex 1172) for protocol 8021 – IPv4
  RFC 1377 for protocol 8023 – OSI including IS-IS
  RFC 5072 for protocol 8057 – IPv6

## Slide 28: Lifetime of a PPP link
Link Dead
Link Establishment Phase
configuration negotiation based on LCP
Authentication Phase (optional)
one-way authentication using PAP/CHAP/EAP
Network-Layer Protocol Phase
configuration of higher-layer protocol using NCP
Link Termination Phase
tearing down the connection due to
  failed authentication
  excessive checksum errors
  link failure
  user termination
Link Dead
Note: full state diagram in RFC 1661

## Slide 29: Basic PPP encapsulation (RFC 1661)
Encapsulation enables demuxing of different network-layer protocols
Only 1 field needs to be examined for protocol determination
Protocol field (similar to EtherType) obeys ISO 3309 rules:
  protocol value must be odd (for EA=1)
  if 16-bit, then the LSB of first byte must be zero (for EA=0)
Protocol values managed by IANA (http://www.iana.org/assignments/ppp-numbers)
0xxx...3xxx are higher layer protocols being transported
  0021 is IPv4 0057 is IPv6
  003D is MLPPP
  0281 is MPLS unicast 0282 is MPLS multicast
8xxx...Bxxx are NCPs
Cxxx...Fxxx are control protocols
  C021 is LCP
  C025 is link quality report
  C023 is PAP C223 is CHAP C227 is EAP
Padding may be used (e.g. to cause header to fall on 32-bit boundary)
protocol (8/16)
information
padding

## Slide 30: PPP using HDLC framing (RFC 1662)
When using PPP over synchronous links we use HDLC framing
Basic PPP encapsulation is extended by 8 bytes
Synchronous Link may be bit-oriented or byte-oriented
Bit stuffing or byte stuffing allowed
Escape mechanism
  allows transparent transfer of control data (e.g. ^S/^Q)
  enables removal of spurious control data (inserted by intermediate boxes)
1 byte Broadcast address is used by default (users may define alternative address)
FF means “broadcast”
1 byte control field is always 03
Unnumbered Information Poll/Final (P/F) bit set to zero
flag
7E
address
FF
ctrl
03
information
FCS
(16/32b)
protocol
(8/16b)
padding
(optional)
flag
7E
HDLC
PPP
PPP
HDLC

## Slide 31: RFC 1662 vs. X.85/X.86
Alternatives to RFC1662 are
ITU-T X.85 (IP over LAPS)
ITU-T X.86 (Ethernet over LAPS)
Cisco HDLC
Their encapsulations are similar to RFC1662 (but can’t co-exist with it)
For example, instead of protocol ID, X.85 has a SAPI =21 for IPv4 =57 for IPv6
The FCS MUST be 32 bits and no padding is used
No special escaping is defined
flag
7E
address
04
ctrl
03
IP Packet
FCS
(32b)
SAPI
(16b)
flag
7E
flag
7E
address
FF
ctrl
03
information
FCS
(16/32b)
protocol
(8/16b)
padding
(optional)
flag
7E
1662
X.85
PPP frame
Cisco HDLC uses:
address = 0 for unicast 8F for multicast
ctrl = 0
protocol = 0800 for IPv4 EtherType

## Slide 32: PPP control
RFC 1661 defines Link Control Protocol packets
configuration packets to establish and configure a link
termination packets to terminate a link
maintenance packets used to manage and debug a link
All LCP packets look like this:
where codes can be:
1 Configure-Request 5 Terminate-Request 9 Echo-Request
2 Configure-Ack 6 Terminate-Ack 10 Echo-Reply
3 Configure-Nak 7 Code-Reject 11 Discard-Request
4 Configure-Reject 8 Protocol-Reject
and ID is used to match replies to requests
code
1 B
ID
1 B
length
2 B
data
N B
flag
7E
address
FF
ctrl
03
protocol
C021
flag
7E
Note: length includes code, ID, length, and data fields

## Slide 33: LCP configuration
LCP configuration packets consist of TLVs describing options
The following options are defined:
1 Maximum Receive Unit (default 1500B)
3 Authentication Protocol (none or PAP/CHAP/EAP)
4 Quality Protocol (used to monitor packet loss)
5 Magic Number (random 4B number used in loopbacks)
7 Protocol Field Compression (1B instead of 2B)
8 Address and Control Field Compression
(omit constant address and control for data packets)
(we will see more later)

## Slide 34: PPP Authentication
After LCP has configured a point-to-point link
PPP provides an optional authentication mechanism
The authentication can be in either or both directions
Password Authentication Protocol was a primitive 2-way handshake
a password was sent in the clear until acknowledged
PAP was obsoleted by RFC 1994
PPP Challenge Handshake Authentication Protocol is somewhat better
authenticator sends a "challenge" message to peer
peer responds with the (MD5) hash of ID+shared-secret+challenge
authenticator checks the response
if correct then authentication is acknowledged else connection terminated
4. if no response a new challenge is sent
CHAP protects against replay attacks, but
requires shared secret to be open at both ends
doesn’t scale well to authenticate many clients
RFC 2284 (obsoleted by 3748) defined PPP Extensible Authentication Protocol

## Slide 35: PPPoX
PPP can run over server layers other than HDLC over TDM
RFC 2516 describes PPP over Ethernet
(uses EtherType 8863 for discovery phase and 8864 for session)
PPPoE was widely used for point-to-point connections
over an Ethernet in the First Mile link (e.g., DSL modem)
but has since between mostly replaced by newer protocols, such as L2TP
RFC 2364 describes PPP over ATM (actually PPP in AAL5 in ATM)
PPPoA was widely used for point-to-point connections
over ATM-based DSL modems (ATM transport)
but has been phased out with adoption of Ethernet transport in DSL (PTM)

## Slide 36: MLPPP

## Slide 37: Multiplexing terminology
There are mechanisms to efficiently utilize links in a network
Duplexing (half/full duplex)
sending information in both directions on same link
examples: FDD, TDD
Multiplexing
sending multiple flows of information on same link
examples: FDM, TDM
Inverse multiplexing
sending a single flow of information on multiple links
examples: LAG, link bonding, ECMP, VCAT
Multiple Access
multiplexing uncoordinated users
examples, FDMA, TDMA, CDMA

## Slide 38: Inverse Mux types
How do we distribute packets over N links?
The simplest way would be to send them round robin
and forward them as received at the other side
but this would result in excessive misordering
There are two philosophies to fix this problem:
1. consistent mapping (ECMP, LAG)
map flows consistently onto the same link
(usually by hashing the header)
2. differential delay compensation (VCAT, EFM bonding, MLPPP)
optionally fragment
add a sequence number (SN)
send over any link (round robin, queuing, etc.)
forward at the other side according to sequence number

## Slide 39: MLPPP
Based on ISO 7776 (X.25 LAPB data link procedures)
RFC 1990 defines an inverse MUX mechanism for PPP that:
aggregates multiple PPP links (possibly of different rates/technologies)
presents to applications a single virtual PPP link with higher data-rate
optionally fragments/reassembles packets
the sender MUST fragment packets with size exceeding some maximum
adds a special MLPPP header
  based on PPP over HDLC header
  contains a 12b or 24b sequence number for in-order forwarding
  marks Beginning and End of fragment (B and E fields)
  an unfragmented packet has both B and E set
distributes the packets/fragments over the links
the receiver MUST buffer packets/fragments and forward them in-order
aggregate PPP link
individual PPPoHDLC links

## Slide 40: Fragmentation
Before fragmentation, packets are PPP encapsulated according to basic PPP
not PPP in HDLC and so does not contain address (FF) or ctrl (03) fields
consists of protocol field for packet (e.g., 0021 for IPv4)
Then the MLPPP header is added to each fragment
Finally the PPP in HDLC header is added
with address=FF, ctrl=03, protocol=003D for MLPPP
Note that the beginning fragment (or full packet) has multiple headers
PPP in HDLC for the link (no address or ctrl, protocol = 003D)
MLPPP header for fragment in link
PPP header for packet with true protocol number (e.g., 0021)

## Slide 41: MLPPP formats
FCS
address FF
control 03
protocol 003D
B
E
RESERVED
SN Byte 1
SN Bytes 2 and 3
fragment data
PPP header
MLPPP
header
PPP FCS
FCS
address FF
control 03
protocol 003D
B
E
RES
SN (12b)
fragment data
long (24b) sequence number format
short (12b) sequence number format
Note: RESERVED fields must be set to 0
if B=1 protocol (e.g., 0021)
if B=1 protocol (e.g., 0021)

## Slide 42: MLPPP sending procedures
Sequence numbers are incremented for every packet/fragment
It is permissible to distribute over links using simple round-robin
but this taxes the delay compensation mechanism
If all links have the same nominal data rate
it is advisable to fragment packets into fragments of equal sizes
If links have different data rates
it is advisable to use fragment sizes proportional to relative rate
alternatively, the sender may use equal-size fragments
but send a number of fragments per link proportional to relative rate
A sender may use any other distribution mechanism, such as:
place packet/fragment in least occupied queue
place packet fragment in queue that it best fits
1
2
3
4
5

## Slide 43: MLPPP receiving procedures
The receiver
buffers received packets
tracks the sequence numbers
tracks B and E fragments
Misordered full packets are reordered (or discarded) before forwarding
If fragmented, a packet is forwarded to the PSN only after receiving the E frame
If a fragment is lost (E or following B received, but not all SNs in packet)
all fragments are discarded
1
2
3
4
5
1
2
Ethernet
3
4
5
MLPPP over TDM

## Slide 44: MLPPP LCP extensions
The MLPPP endpoints perform PPP negotiation for each link in the multilink
Note that links may be added/removed to a multilink on-the-fly at any time
and do not disrupt the sequencing
MLPPP requires additional LCP configuration options:
17 Multilink Maximum Received Reconstructed Unit
18 Multilink Short Sequence Number Header Format
19 Endpoint Discriminator (to identify component links of aggregate)
The MRRU (default 1500) is the maximum size of the reassembled packet
and may be longer than the MRU on the individual links
Endpoint Discriminator identifies the MLPPP endpoint
and is the same for all links making up the multilink
If a new endpoint discriminator is announced
a new multilink must be opened

## Slide 45: TDM Pseudowires

## Slide 46: Pseudowires
A pseudowire (PW) is a mechanism to tunnel native service traffic
through a Packet Switched Network (IPv4, IPv6, MPLS, Ethernet)
PWs are usually bidirectional (unlike MPLS LSPs)
PW architecture is an extension of VPN architecture
The PWE3 Working Group in the IETF defined the following native services:
ATM (port mode, cell mode, AAL5-specific modes) RFC 4717, 4816
Frame Relay RFC 4619
HDLC/PPP RFC 4618
TDM (E1, T1, E3, T3) RFC 4553, 5086, 5087
SONET/SDH (CEP) RFC 4842
Fiber channel RFC 6307
Generic packet service RFC 6658
Ethernet (raw, VLAN-aware) RFC 4448
Note that most of these are legacy services
but the most interesting one today is Ethernet (for VPLS)

## Slide 47: Pseudowire Emulation Edge to Edge PWE3
Provider
Edge
(PE)
Customer
Edge
(CE)
Customer
Edge
(CE)
Customer
Edge
(CE)
native
service
AC
provider’s
PSN
Pseudowires (PWs)
Customer
Edge
(CE)
Customer
Edge
(CE)
Provider
Edge
(PE)
native
service
AC

## Slide 48: TDM PW Protocol Processing
Steps in TDM PW processing
The synchronous bit stream is segmented (either by framing or number of bytes)
The TDM segments may be adapted
PWE3 control word is prepended
PSN headers are prepended (encapsulation)
Packets are transported over PSN to destination
PSN headers are utilized and stripped
Control word is checked, utilized and stripped
TDM stream is reconstituted (using adaptation) and played out
Note that adequate synchronization must be guaranteed
but that would require another talk to explain
TDM
TDM
PSN Packets
PSN
PSN Packets

## Slide 49: Flags in the CW
The PWE control word has 2 flags: L and R
and a 2-bit field: M
They are used in the following way :
L is set to indicate a forward defect (AIS)
R may be set to indicate a reverse defect (RDI)
M can modify the meaning of the FDI
0 0 0 0 flags FRG Length Sequence Number
L R M(2b)

## Slide 50: TDM transport types
Structure-agnostic transport (SAToP – RFC4553)
for unstructured TDM
even if there is structure, we ignore it
simplest way of making payload
OK if network is well-engineered
Structure-aware transport (CESoPSN – RFC 5086, TDMoIP – RFC 5087)
take TDM structure into account
must decide which level of structure (frame, multiframe, …)
can overcome PSN impairments (PDV, packet loss, etc)
The Frame Alignment Signal (FAS) is maintained at PSN egress
Overhead bits may be transported

## Slide 51: Structure Agnostic Transport
SAToP encapsulates N bytes of TDM in each packet
There is no TDM frame alignment !
N must be constant and preconfigured
If packets are lost, the egress knows how many TDM bytes to fill in
Default values for N :
E1 – 256 B
T1 – 192 B
E3 and T3 – 1024 B
For T1 there is an optional special mode called octet aligned mode
that adds 7 bits of padding to every 193 consecutive bits (to make 25 B)

## Slide 52: Structure aware encapsulations
Structure-locked encapsulation (CESoPSN)
Structure-indicated encapsulation (TDMoIP – AAL1 mode)
Structure-reassembled encapsulation (TDMoIP – AAL2 mode)
headers
TDM structure
TDM structure
TDM structure
TDM structure
headers
AAL1 subframe
AAL1 subframe
AAL1 subframe
AAL1 subframe
headers
AAL2 minicell
AAL2 minicell
AAL2 minicell
AAL2 minicell

## Slide 53
Presenter Name
Title
E-mail