## Slide 1
Correlation

## Slide 2: Signal similarity
We often need to know how similar two signals x and y are
for example, to detect the appearance of a single in noise
In radar we transmit a known signal
the signal propagates in space until it is reflected by a target
it then travels back and is received by the radar receiver
By accurately detecting the exact time that the signal is received
and subtracting the exact time it was transmitted
we can deduce the distance to the target
However, due to
the 1/r2 propagation loss
the minute amount of energy reflected
the signal received is very weak
while the noise may be large
We need a very sensitive way to detect the known signal in noise

## Slide 3: Signal similarity
To compare two signals
we can compute the difference signal δ = x – y
and define similarity as its energy Eδ being small
But that doesn’t work if (with respect to x)
y has some gain
y is shifted in time
For example, if y = g x then the difference is δ = (1-g) x
which is only small if g≈1
We can derive something better from the energy Eδ
Eδ = - )2
= 2 – 2 + 2
= Ex – 2 Cxy + Ey
Cxy is called the (cross)correlation between x and y

## Slide 4: Correlation
Eδ = Ex – 2 Cxy + Ey
where Ex and Ey are the (constant) energies of the 2 signals
Note that when Eδ is minimal, Cxy is maximal
so we say the signals are correlated when Cxy is large
Cxy is still large even if y has arbitrary gain with respect to x
since the gain is captured in the energy component
For example, if y = g x (and thus Ey = g2 Ex)
then Cxy = = g = g Ex
What do we mean by large?
If y = g x we can also write Cxy = g =
so, a simple way to gauge the size of cross-correlation
is to compare it with (it won’t be exactly equal because of noise!)
However, Cxy will not indicate similarity if y is shifted in time

## Slide 5: Correlation and anticorrelation
If Cxy is positive and large
then x and y are correlated (similar)
If Cxy is negative and large
then x and y are anticorrelated
If Cxy is zero (or very small)
then x and y are uncorrelated (different)

## Slide 6: Correlation with lags
To take care of time shifts with define (m is called the correlation lag)
Cxy(m) =
(m is called the correlation lag)
We now look for its maximum value (its peak)
This peak corresponds to the optimal time shift
if there the correlation is significant (using the same criterion as before)
then we have found our similar signal
Note the difference between correlation and convolution
in correlation both indexes increase
in convolution one increases one decreases

## Slide 7: Autocorrelation
We can define the autocorrelation Cxx(m) =
which tells us how similar the signal is to itself
Of course a signal is always similar to itself!
But we use autocorrelation to see how similar a signal is
to a time shifted version of itself
A periodic signal has peaks at lags that are multiples of its period!
Since |cxx(m)| ≤ Ex it is useful to define the normalized autocorrelation
cxx(m) = Cxx(m) / Ex
where |cxx| ≤ 1
Why can autocorrelation be more accurate than using the FFT?

## Slide 8: Wiener filter
Pulse radars transmit a short (and thus low energy) distinctive pulse
and receive a delayed, weak, noisy copy after time t = 2 R / c
The Wiener filter finds t by building an MA filter
with coefficients equal to the time reversed signal
The MA’s convolution actually performs a correlation
t

## Slide 9: Prediction
Wiener’s famous paper was named
Interpolation, extrapolation and smoothing of stationary time series
Where in modern terminology:
smoothing = low-pass filtering
interpolation = resampling (sampling at different time instants)
extrapolation = prediction
We previously saw how Yule predicted sun-spots via an AR process
* = where s* is the estimate of s
Let’s directly derive the coefficient b for the simplest case (M=1)
We want to minimize the energy of the error signal e = y*-y
2 = = (1+2)Es – 2Cs(1)
Differentiating and setting equal to zero we find = Cs(1) / Es = cs(1)
So, there is a connection between prediction and autocorrelation!
More generally, the coefficients are given by Yule Walker equations!

## Slide 10: Yule Walker with correlations
Start with the Yule Walker equations (e.g., for M=4)
=
Multiply both sides by and sum over n (note ∑sn+m sn = ∑sn-m sn)
=

## Slide 11
Adaptation

## Slide 12: Adaptive filters
We often would like to remove noise from a noisy signal
Sometimes we can access a signal that is highly correlated to the noise
For example, assume 2 microphones
1. air conditioner noise qn
2. speech xn + filtered air conditioner noise q’
In the simplest case
the filtering is a single-tap MA filter which adds a qn-m
so yn = xn + a qn-m where a and m are unknown
The idea is to find a and m by adapting our estimates of them
so this is called an adaptive filter
If a and q change over time
or even when we simply alter our estimates of them
then this is not a filter since it is not time invariant
q
x
y = x+q’

## Slide 13: Adaptation
We can assume that
the desired signal x and
the noise
are uncorrelated
By finding the maximum cross-correlation
between q and y=x+q’ (which only looks for q!)
we can determine m and thus qn-m
But how do we find a ?
Estimate x*n = yn - c qn-m = xn + (a-c) qn-m
x
q
-
a
x*
c

## Slide 14: The energy parabola
x*n = xn + (a-c) qn-m
So Ex* = < x*2 > = < x2 > + (a-c)2 < q2 > + 2 (a-c) <x q>
Since x and q are uncorrelated the last term is zero
The energy is parabolic in c with a single minimum
Ex*
c
a

## Slide 15: Adaptation
Starting from x*n = xn + (a-c) qn-m
The global minimum is for c=a and there x*n = xn
To find c we need to minimize the energy of x*n as a function of c
This minimization is typically done via gradient descent (AKA steepest descent)
What if we receive the noise and echoes of it? yn = xn + Σm am qn-m
The same thing can be done for a M-tap filter
using M-dimensional gradient descent
Ex*
c
a

## Slide 16: Gradient descent
E
c
In gradient descent we choose a step size λ
at each step we estimate the gradient (derivative of E) d
and correct c at each step by c ← c - λ d
The gradient points in the direction that E increases
so we move in the opposite direction (minus sign)
The larger the gradient the further we move
for more complex problems
the energy is not parabolic
and may contain local minima
choosing the step size
can be important!

## Slide 17: Echo cancellation
Another common use of adaptive filters is echo cancellation
Acoustic Echo Cancellation
e.g., for car hands-free units
Line Echo Cancellation
hybrid
hybrid

## Slide 18: Echo suppressors
Telephony hybrids are not perfect
leaking some amount of echo is sent back to the speaker
If the echo delay is < 20 ms then this is not noticed
but round-trip delay for US coast-to-coast is > 50 ms
and for satellite conversations the delay is > ½ second
Before the advent of DSPs echo was removed by echo suppressors
that chose the louder direction and blocked the opposite direction
effectively making telephone conversations half-duplex
(this still sometimes happens with simple office phones)
For non-speech (fax, modems) echo suppressors are turned off
by sending a 2100 Hz tone
Echo suppression is a waste of full-duplex infrastructure
conversation is unnatural
hard to break in
speaker hears dead line (so telephones artificially add sidetone)
LEC was one of the first applications of DSPs

## Slide 19: Echo cancellers
In a simplistic model of LEC the near end simply estimates the echo
and subtracts it to send clean (echo-less) speech to the far end
(of course, the far end does the same)
Real LECs have additional elements, including
double-talk detectors (Geigel algorithm)
to freeze adaptation when both sides are speaking
nonlinear processing (center clipping) to remove residual echo
near end
far end
-
clean speech
echo path
speech
+
echo

## Slide 20: Realistic LEC

## Slide 21: LEC in action
The LEC mechanism
places samples received from the far-end into the X buffer
convolves them with the current filter (called the H register)
obtaining the echo estimate
subtracts the echo estimate from the near-end samples
How is the filter adaptation done?
Assume that only the far-end subscriber is talking
then the signal at the input to the subtracter is unwanted echo generated by the near-end hybrid and telephone
The adaptation mechanism varies the filter coefficients
minimizing the energy at the output of the subtracter
If the far-end is quiet or double-talk is detected
the adaptation algorithm automatically stops updating

## Slide 22: Equalization
A problem that arises in data communications
We can model the channel distortion as
filtering i.e.,
adding noise
Recovering the original signal
requires applying the inverse of the channel filter (equalization)
i.e.,
For this we need to
find the channel filter coefficients
invert the filter
Equalizers are also used in stereo audio systems. Why ?
transmitter
receiver
distorting
channel

## Slide 23: Multipath
What happens when a signal is received over a primary (shortest) path
and also over delayed paths (e.g. reflections off buildings) ?
The composite signal contains echoes
and is thus an MA filtered version of the original
primary path
delayed paths
+
min
delay
max delay

## Slide 24: Finding the equalizer
If we start the transmission with a known signal
then finding the channel filter is a system identification problem
In particular, if we assume that the channel filter
is MA then we need to solve Wiener-Hopf equations
and the inverse filter will be AR why?
is AR then we need to solve Yule-Walker equations
and the inverse filter will be MA why?
Sometimes we can’t transmit a special known sequence - why?
for example, receiver may turn on at any time
then we need blind equalization
And even if we can, what if the channel changes over time? why?
for example, a mobile receiver
Then we need to adapt the equalizer over time
if we can derive a measure of received SNR
we can use gradient descent

## Slide 25: Using the equalizer
There are two ways to apply equalization G to compensate for H
at the receiver x = G y = G H x = H-1 H x
at the transmitter (Tomlinson precoding) : transmit x’ = G x
and receiver automatically sees y = H G x = H H-1 x
If the channel filter is not AR then the second way is better – why?
Because at frequencies where the filter has zeros
the channel frequency response is not invertible
That is, if at ω0 we have H(ω0)=0
then no G(ω0) can obey G(ω0) H(ω0) = 1
and so information there is lost
Even if H(ω0) is not exactly zero, but very small H(ω0) ≈ 0
G(ω0) will have to be very large
and will lead to noise amplification
(we have been neglecting the additive noise until now ...)
However, Tomlinson requires a back-channel!