## Slide 1: Real-time
1-input 1-output DSP systems
Hard real-time: ALWAYS finish computing output before next input
Soft real-time: enough to finish on average
N-input N-output DSP systems
No need to process all N inputs between the Nth and the N+1th
by using double/cyclic buffer
enough to process N inputs before the next N arrive
Real-time demands algorithms that are O(N)
since otherwise, no matter how fast the CPU,
for large enough N we won’t finish processing in time
double buffer
cyclic
buffer

## Slide 2: DFT complexity
DFT: Xk = Sn=0N-1 xn WNnk
We need to compute N values (k = 0 … N-1)
each of which contains with N products (n = 0 … N-1)
Thus, the straightforward DFT takes N2 products
DFT is O(N2)
but the Fast Fourier Transform reduces it to O(N log N)
This is not low enough to guarantee real-time for all N
but is sufficiently low to enable even extremely large Ns
(processors are rated by how large an FFT they can perform in real-time)

## Slide 3: Warm-up problem 1
Find minimum and maximum of N numbers x0 x1 x2 x3 ... xN-2 xN-1
minimum alone takes N comparisons
maximum alone takes N comparisons
minimum and maximum takes 1½ N comparisons
x0 x1 x2 x3 ... xN-2 xN-1
run over at pairs, separating into larger and smaller
– this takes ½ N comparisons
the maximum must be in the smaller list
– find it in ½ N comparisons
the minimum must be in the larger list
– find it in ½ N comparisons
Altogether 3/2 N comparisons – 25% savings
use decimation
can be performed in-place

## Slide 4: Warm-up problem 2
Multiply two N digit numbers (w.o.l.g. N binary digits)
Long multiplication takes N2 1-digit multiplications
Partitioning factors reduces to 3/4 N2
Can recursively continue to reduce to O( N log2 3)  O( N1.585)
3 multiplications, each N/2 bits
32 multiplications, each N/4 bits
3 log2(N) multiplications, each 1 bit

## Slide 5: Decimation and Partition
Decimation (LSB sort)
x0 x2 x4 x6 EVEN
x1 x3 x5 x7 ODD
Partition (MSB sort)
x0 x1 x2 x3 LEFT
x4 x5 x6 x7 RIGHT
x0 x1 x2 x3 x4 x5 x6 x7
Decimation in Time  Partition in Frequency
Partition in Time  Decimation in Frequency

## Slide 6: DIT FFT
separate sum in DFT
by decimation of x values
we recognize the DFT of the even and odd sub-sequences
we have thus made one big DFT into 2 little ones
If DFT is O(N2) then DFT of half-length signal takes only 1/4 the time
thus two half sequences take half the time
Can we combine 2 half-DFTs into one big DFT ?

## Slide 7: DIT is PIF
comparing frequency values in 2 partitions
Note that same products
just different signs
+ - + - + - + -
We get further savings by exploiting DIT = PIF
All the odd terms all have - sign !
combining we get the "butterfly"

## Slide 8: What does this mean ?
We have divided the DFT of length N into
2 DFTs of length
a butterfly for each pair of outputs
This can be used for a recursive FFT implementation
DFT N/2
EVEN
Xk
Xk
DFT N
LEFT
DFT N
RIGHT
WN
k
DFT N/2
ODD
k
k
k = 0 ... N/2 -1

## Slide 9: DIT all the way
We have already saved
but we needn't stop after splitting the original sequence in two !
Each half-length sub-sequence can be decimated too
Assuming that N is a power of 2, we continue decimating until we get to the basic N=2 butterfly
multiplications

## Slide 10: DIT N=8 - step 0

## Slide 11: DIT N=8 - step 1

## Slide 12: DIT N=8 - step 2

## Slide 13: Full DIT for N=8
W41 = W82
W20 = 1
= 1
= 1
= 1
don’t worry about the order – yet!

## Slide 14: Complexity
We assume that all the Ws are precomputed
An FFT of length N has
log2(N) layers of butterflies
½N butterflies per layer, each with
  1 complex multiply
  2 complex adds (1 add and 1 subtract)
So there are :
½ N log2(N) complex multiplies
N log2(N) complex adds
Actually, a lot of these are trivial!
the last layer has 1 trivial multiplication
the next to last layer has 2 trivial multiplications
...
the first layer has no non-trivial multiplications

## Slide 15: Real complexity
Each complex add is 2 real adds
Each complex multiply is either:
4 real multiplies and 2 real adds
(a + i b) (c + i d) = (a*c – b*d) + i (a*d + b*c)
or 3 real multiplies and 5 real adds
M1 = a*c M2 = b*d M3 = (a+b)*(c+d)
(a + i b) (c + i d) = (M1 – M2) + i (M3 – M2 – M1)
So N log2(N) complex adds = 2N log2(N) real adds
½ N log2(N) complex multiplies =
2N log2(N) real multiplies
and another N log2(N) real adds (altogether 3N log2(N) )
or 3/2 N log2(N) real multiplies
and another 5/2 N log2(N) real adds (altogether 9/2 N log2(N) )

## Slide 16: Bit reversal
the input seems to be in a strange order !
So abcd  bcda  cdba  dcba
The bits of the index have been reversed !
  (DSP processors have a special addressing mode for this)

## Slide 17: DIT N=8 with bit reversal

## Slide 18: DIF N=8
DIF butterfly
we can derive this from the DIT graph using the transposition theorem!