## Slide 1: Systems
A signal processing system has signals as inputs and outputs
The most common type of system has a single input and output
A system is called causal
  if yn depends on xn-m for m 0 but not on xn+m
A system is called linear (note - does not mean yn = axn + b !)
if x1  y1 and x2  y2 then (ax1+ bx2) (ay1+ by2)
A system is called time invariant
if x  y then zn x  zn y
A system that is both linear and time invariant is called a filter
0 or more signals as inputs
1 or more signals as outputs
1 signal as input
1 signal as output

## Slide 2: What is/isn’t a system?
answers

## Slide 3: Example systems
Identity system yn = xn
Amplifier (gain) yn = g xn
Saturator yn = sign( xn )
What does this do to a sinusoid ?
How is it related to the amplifier ?
Why is DSP better than electronics ? (see next slide)
Time by time functions yn = f(xn)
These are not interesting since they don’t involve time
Delay y = x (i.e., yn = xn-1 )
First time difference y = x (i.e., yn = xn - xn-1 )
Smoother yn = xn-1 + xn + xn+1 (not causal!)
How can we make it causal?

## Slide 4: DSP is better than electronics
Analog electronic amplifiers have
maximum output voltage (power supply voltage)
cut-in voltage
nonlinearities
In DSP we can multiply exactly
(we’ll see later why overflow/underflow won’t concern us)
x
cut-in
y
maximum
nonlinearities

## Slide 5: Filters
Filters have an important property
Y() = H() X() Yk = Hk Xk
In particular, if the input has no energy at frequency f
  then the output also has no energy at frequency f
  (what you get out of it depends on what you put into it)
This is the reason to call it a filter
  just like a colored light filter (or a coffee filter …)
Filters are used for many purposes, for example
filtering out noise or narrowband interference
separating two signals
integrating and differentiating
emphasizing or de-emphasizing frequency ranges
The simplest filters are amplification and delay

## Slide 6: How does the filter law work?
ω
X(ω)
ω
H(ω)
ω
Y(ω)
1
ω
X(ω)
ω
H(ω)
ω
Y(ω)
1
ω
X(ω)
ω
H(ω)
ω
Y(ω)
1
H(ω) is called the frequency response

## Slide 7: Frequency response
In general H(ω) is a complex number
The absolute value is the gain
how much the sinusoid is amplified or attenuated
The phase is the phase shift
how much the sinusoid is delayed
H(ω) is a function of ω
a filter need not do the same thing to all frequencies!
Many time we use filters that are low-pass, high-pass, etc.
but not all filters are like that
low pass
f
high pass
f
band pass
f
band stop
f
notch
f
x
y
x
y
| H(f) |
| H(f) |
| H(f) |
| H(f) |
| H(f) |

## Slide 8: Types of filters
low pass
f
high pass
f
band pass
f
band stop
f
notch
f
multiband
f
realizable LP
When designing filters, we can specify :
transition frequencies
transition widths
ripple in pass and stop bands
linear phase (yes/no/approximate)
computational complexity
memory restrictions
What kind of analog filter is an anti-aliasing filter ?

## Slide 9: Nonfilters
If a system is not linear it does not obey the filter law !
For example, yn = xn + ϵ xn2
if xn = sin(ωn) then yn = sin(ω n) + ϵ/2 - ϵ/2 cos(2ω n)
So the input spectrum has 1 component
and the output spectrum has 3!
If a system is not time invariant it is not a filter!
For example, y(t) = ei Ω t x(t)
if x(t) = ei ω t then y(t) = ei Ω t ei ω t = ei (Ω + ω) t
Why did we use complex exponentials here ?
What happens to a more general spectrum ?
sin2(ϕ) = ½ - ½ cos(2 ϕ)
ω
ω
2ω
0
original line
harmonic
DC
ω
ω
Ω+ω
0
original line
shifted line
Ω
ω
original spectrum

## Slide 10: Question 1
To understand our first kind of filter we’ll look at an example
We know that a signal is DC (a constant sn = k)
but only see a noisy version xn = sn + vn
where the noise signal vn is DC-free (zero average)
How do we discover k (recover sn) ?
We average over as much time as we can
k = < xn > = < sn + vn > = < sn > + < vn > = < sn > + 0
In practice, we take N samples
k =

## Slide 11: Question 2
We know that a signal sn changes very slowly
(has only low frequencies in its spectrum)
but only see a noisy version xn = sn + vn
where the noise signal vn is DC-free (zero average)
How do we recover sn ?
We average over a window
long enough for the noise to average out
but not so long as to destroy the signal
And then we move on to the next window
This is called Moving Average
yn = ( if L is odd then 1/(L+1) )

## Slide 12: Question 3
The same, but signal sn doesn’t change so slowly
(there are higher frequencies in its spectrum)
How do we recover sn ?
We perform a (generalized) Moving Average but with non-equal coefficients
yn = where = 1
For example the smoother yn = xn-1 + xn + xn+1
What coefficients return us to the original MA ?
Why do we often use triangular coefficients ?
0
- L/2
L/2

## Slide 13: Question 4
What if the signal sn has a spectrum with all frequencies ?
We can still perform Moving Average
but need to find the coefficients based on the frequency domain such that we allow the signal to pass
but block as much noise as possible
This will only work if MA is a filter!
v

## Slide 14: MA is always a filter
Let’s check that Moving Average is a filter (linear and time invariant)
LINEARITY
If we multiply the input by a gain g
yn’ = = g = g yn
If we add two inputs u and v which give outputs x and y
= xn + yn
TIME INVARIANCE
If we shift the input signal by m times (m positive or negative)
and the coefficients don’t change!
yn’ = = yn+m
Note that sometimes it is useful to have coefficients
that change slowly over time (to adapt to changing circumstances)
In which case we almost have a filter …

## Slide 15: How to design a digital filter
20 years ago a large part of every DSP course was devoted to
how to design digital filters, i.e., given S(ω) how to find
It is not enough to take the function S(ω) and perform an iFT
since in practice we would do this in the digital domain Sk
and we would have no control over what happens
between the discrete frequency points
Here is the algorithm I recommend today 
Google digital filter design software free download
Download and install
We’ll learn later about the different filter types
for now pick MA (also called FIR) filter
Enter or draw the desired frequency characteristics
Press compute coefficients
View the spectrum
Try it out

## Slide 16: Convolution
We saw that to filter out noise we used the signal processing system
yn =
This is not causal, a similar causal filter is
yn =
These forms of computation are called (finite) convolution
Note that convolution is the sum of products
with one index going up and the other index going down
in this way the sum of the 2 indexes stays the same (n) We could have made both indexes go in the same direction
which is called correlation (used to compare 2 signals x and y)
Cx,y(m) =
Note that here the indexes both go up together!

## Slide 17: Picturing Convolution
We chose the coefficients so that the indexes of a and x
go in opposite directions
Note that the sum of the input indexes equals the output’s index !
x0
x1
x2
x3
x4
x5
a2
a1
a0
*
*
y0
*
a2
a1
*
a0
*
*
y0
*
*
y1
*
a2
*
a1
*
*
y0
a0
*
*
*
y1
*
*
y2
*
a2
*
a1
*
*
y2
a0
*
*
*
y3
*
*
y4
*
y0
y1
a2
*
a1
*
*
y1
a0
*
*
*
y2
*
*
y3
*
y0
a2
*
a1
*
*
y3
a0
*
*
*
y4
*
*
y5
*
y0
y1
y2
+

## Slide 18: Convolution
You know all about convolution !
LONG MULTIPLICATION B3 B2 B1 B0
* A3 A2 A1 A0
-----------------------------------------------
A0B3 A0B2 A0B1 A0B0
A1B3 A1B2 A1B1 A1B0
A2B3 A2B2 A2B1 A2B0
A3B3 A3B2 A3B1 A3B0
------------------------------------------------------------------------------------
POLYNOMIAL MULTIPLICATION
(a3 x3 +a2 x2 + a1 x + a0) (b3 x3 +b2 x2 + b1 x + b0) =
a3 b3 x6 + … + (a3 b0 + a2 b1 + a1 b2 + a0 b3 ) x3 + … + a0 b0

## Slide 19: Multiply and Accumulate (MAC)
How do we compute a convolution? (or a correlation?)
We iterate on a basic operation
y  y + ai * xj
Since this Multiplies a times x and then ACcumulates the answers
  it is called a MAC
The MAC is the most basic computational block in DSP
Even computing energy can be done using (degenerate) MACs
E  E + xi * xi
The MAC is the most basic computational block in DSP
It is so important that a processor optimized to compute MACs
  is called a DSP processor

## Slide 20: In the frequency domain
Remember that in DSP
we are interested in time and frequency domains
We know what an MA filter does in the time domain – convolution!
What does it do in the frequency domain?
What does an MA filter do to a sinusoid of arbitrary frequency ω ?
Here it is much easier to use complex exponentials than sines
So we ask, what does an MA filter do to xn = eiωn for arbitrary ω
We haven’t proven it yet (don’t worry – we will later)
but we said that for all filters Y(ω) = H(ω) X(ω)
That means that sinusoids are eigensignals of filters
MA-filter( eiωn ) = H(ω) eiωn
H(ω) is called the MA frequency response (0 ≤ ω ≤ π)
Why do we look at H(ω) for all ω instead of Hk ?
Why don’t we look at H(ω) for negative ω ?
H(ω)
ω
0
π

## Slide 21: Simple MA Frequency response
Let’s start with a simple noncausal 3-point MA
yn = (xn-1 + xn + xn+1)
First let’s ask what this filter does to DC
remembering that for DC we can take xn = 1 (for all n)
yn = (1+1+1) = 1 (for all n) so y is also DC (of course - it had to be!)
and H(DC) = yn / xn = 1
Next let’s ask what it does to Nyquist frequency (ω=π)
remembering that for Nyquist we take xn = … -1 +1 -1 +1 …
For even n: yn = (-1+1-1)= - and for odd n: yn = (+1-1+1)=
So yn is … + - + - … which is also a Nyquist signal (it had to be!)
and H(ω) = yn / xn = -
We’ll only care about |H(ω)| for now, and |H(Nyquist)| =

## Slide 22: Simple MA Frequency response (cont)
We have already found 2 points on the |H(ω)| plot
Now let’s find the rest!
We substitute xn = eiωn for arbitrary ω (0 ≤ ω ≤ π)
So yn is a constant times eiωn (of course - it had to be!)
and H(ω) = yn / xn = ( 1 + 2cos(ω) )
Why isn’t this a nice enough low-pass filter?
|H(ω)|
ω
0
π
1
|H(ω)|
ω
0
π
1

## Slide 23: What about averaging more?
The frequency response of the more general averaging filter
is
The more we average the more low-pass the filter becomes!
Why?

## Slide 24: Frequency response 2
As another example let’s look at the simple smoother filter
yn = xn-1 + xn + xn+1
For DC yn = + + = 1 (for all n) so H(DC) = yn / xn = 1
For Nyquist (even n) yn = (-1) + + (-1)= 0 so H(Nyquist) = 0
For general frequency we substitute xn = eiωn
y is a sinusoid of the same frequency (of course – it has to be!)
and |H(ω)| = ½ ( 1 + 2cos(ω) ) Why is this better?
|H(ω)|
ω
0
π
1

## Slide 25: The first finite difference
Last example - the first finite difference in the frequency domain
y = x (i.e., yn = xn - xn-1 )
H(ω) eiωn = eiωn – eiω(n-1) so H(ω) = 1- e-iω
This is a high-pass filter!
Why must it be high-pass?
Why is this complex (i.e., why does it have a phase shift)?

## Slide 26: Differentiation and Integration
What does the analog derivative look like in the frequency domain?
Here is it easy enough to use sines
The derivative of x(t) = sin(ωt) is y(t) = = ω cos(ωt)
so | H(ω) | = ω and there is a 90 degree phase shift
What about the analog integral?
The integral of x(t) = sin(ωt) is y(t) = = – (1/ω) cos(ωt)
so | H(ω) | = 1/ω and there is a 90 degree phase shift
|H(ω)|
ω
0
|H(ω)|
ω
0

## Slide 27: Convolution and multiplication
We already saw 2 connections between convolution
multiplying numbers and polynomials are convolutions
But we now understand a deeper connection
The filter law means that a convolution in the time domain
yn =
corresponds to a multiplication in the frequency domain Yk = Hk Xk
So, instead of convolving a and x in the time domain
we can move to the frequency domain and multiply
x0
x1
x2
x3
x4
x5
a2
*
a1
*
*
y1
a0
*
*
*
y2
*
*
y3
*
y0
X0
X1
X2
X3
X4
X5
A1
*
A2
*
*
Y1
A3
*
*
*
Y2
*
*
Y3
*
Y0
A0
A4
A5
Y4
Y5
*
*
*
a4
a3
*
*
6*6 multiplications!
y5
y4
many people even write y = a*x
a5
*
6 multiplications
Why 6*6 and not 1+2+3+4+5+6 = 21 ?

## Slide 28: The complexity of convolution
In DSP we use either the time domain or the frequency domain
whichever is better for the task at hand
To perform convolutions over N elements in the time domain
yn = for n = 0 … N-1
requires N times N multiplications (and another N*(N-1) additions)
and so the complexity is O(N2)
To perform the same thing in the frequency domain Yk = Hk Xk
requires only N multiplications
But if we are working in the time domain
we need to first convert a and x into frequency domain A and X
and at the end convert Y back into time domain y
To do that we need to perform 2 DFTs Xk =
and 1 iDFT yn = each of which is O(N2) !
What we really need is a lower complexity DFT algorithm!

## Slide 29: AR
Computation of convolution is iteration
In CS there is a more general form of 'loop' - recursion
Example: let's average values of input signal up to present time
  y0 = x0 = x0
  y1 = (x0 + x1) / 2 = 1/2 x1 + 1/2 y0
  y2 = (x0 + x1 + x2) / 3 = 1/3 x2 + 2/3 y1
  y3 = (x0 + x1 + x2 + x3) / 4 = 1/4 x3 + 3/4 y2
  yn = 1/(n+1) xn + n/(n+1) yn-1 = (1-b) xn + b yn-1
So the present output
  depends on the present input and previous outputs
In DSP recursion is called AutoRegression (term invented by Udny Yule)
Note: to be time-invariant, b must be non-time-dependent (not like here!)

## Slide 30: Unraveling the recursion
Given an AR form we can swap the recursion for an infinite iteration
For example, the simplest AR filter is yn = xn + b yn-1
In general AR filters can be written as infinite convolutions
yn =
Try this for the AR with 2 time delays
(we’ll leave out the input gain for now)

## Slide 31: AR is a filter
The recursive AR form is an AR (autoregressive) filter
LINEARITY
Start from the infinite convolution form
the proof is the same as for the MA filter
TIME INVARIANCE
Start from the infinite convolution form
the proof is the same as for the MA filter
as long as the coefficients are not time dependent

## Slide 32: Frequency response of an AR filter
Let’s try our simple AR example yn = (1- b) xn + b yn-1
What happens for DC?
We know that for all n xn=1 and yn = H0
so H0 = (1- b) + b H0 or H0 (1 – b) = (1- b) so H0 = 1
What happens for Nyquist ?
We know that xn=… -1 +1 -1 +1 … and yn = … -Hπ +Hπ -Hπ +Hπ …
so Hπ = (1- b) - b Hπ or H π (1+b) = (1- b) so Hπ = (1- b) / (1+b)
For general frequency ω : xn = eiωn and yn = H(ω)eiωn
so H(ω)eiωn = (1- b)eiωn + bH(ω)eiω(n-1) so H(ω) = (1- b) + bH(ω) e-iω
so H(ω) = (1- b) / (1 - b e-iω) Why is this complex (i.e., has a phase shift)?
and |H(ω)|2 = 1 / (1 - 2bcos(ω) + b2 )
we purposely put the input gain back in!

## Slide 33: The AR frequency response
b = 0.5
b = 0.95
b = 0.6
b = 0.7
b = 0.8
b = 0.9
yn = (1- b) xn + b yn-1
For small b yn ≈ xn so H(ω) ≈ 1
For large b yn can’t keep up with x
so H(ω) is very low-pass

## Slide 34: The harder way
But we cheated! We haven’t yet proven the filter law
We can find the frequency response of the AR filter
from the unraveled form, but without using the filter law
(we used the formula for the sum of an infinite series
with q = )

## Slide 35: The accumulator
We once defined the accumulator y = x
by
(the inverse of the first finite difference - = 1)
We can write the accumulator as an AR filter
If we input DC this explodes! (AR filters can be unstable)
What is the frequency response?
Thus
So |H(ω)| is very similar to the FR of the true integrator!

## Slide 36: MA, AR and ARMA
The general causal system looks like this:
yn = f ( xn , xn-1 … xn-l ; yn-1 , yn-2 , …yn-m ; n )
But the general causal filter has to be
a linear combination of the inputs and outputs
This is called ARMA (it would be hard to say MAAR)
  if bm=0 then it is MA
  if a0=0 and al >0=0 but bm≠0 then it is AR
Why doesn’t the ARMA filter depend explicitly on n ?
Why does the sum only include previous inputs and outputs?
Why must the function be a linear combination of them ?
Why does m start at 1 and not 0 ?

## Slide 37: Symmetric form of writing ARMA
We can write the ARMA equation in symmetric form
by terms moving from side to side
This form is a called a difference equation
since it can be rewritten as
What is the connection between the coefficients?

## Slide 38: 3 ways of writing the ARMA filter
So far we can write the causal ARMA filter in 3 ways
ARMA form
Symmetric form
(difference equation)
Infinite convolution
What happens when the filter is MA? AR?
How can we translate between representations?
it looks nicer with L

## Slide 39: System identification
Up to now we have discussed
what a known ARMA system does to a given input
Now let’s consider the converse problem
We are given an unknown system with one input and one output
think of the system as inside a black box which can’t be opened
What is known are the input and output to the black box
Can we figure out what is inside the box ?
This is called the system identification problem
x
y
unknown
system

## Slide 40: Identification?
What do we mean by identifying the system ?
You are given the unknown system for some amount of time
You need to be able to predict the output for any given input
For ARMA systems, it is enough to know any of these:
ARMA form – L a coefficients and M b coefficients
symmetric form (difference equation) L α coefficients, M β coefficients
infinite convolution form all
the frequency response all Hk
since from any of these we can calculate the output y for all times
x
y
unknown
system

## Slide 41: Two flavors
There are two different ways this game can be played
Easy system identification problem
we are allowed to input any x we want and observe the output y
what input should we use?
Hard system identification problem
the system is already "hooked up"
we can only observe the input x and output y
The hard problem is indeed harder than the easy problem
for example - what happens if the input is always 0?
unknown
system
x
y
unknown
system

## Slide 42: Filter identification
Is the system identification problem always solvable ?
Not if the system characteristics can change over time
Since you can't predict what it will do next
So only solvable if system is time invariant
Not if system can have a hidden trigger signal
So only solvable if system is linear
Since for linear systems
any signal is the sum of the trigger plus the difference
small changes in input lead to bounded changes in output
So only solvable if system is a filter !

## Slide 43: Easy problem Impulse Response (IR)
To solve the easy problem (where we can input any signal(s) we want)
we need to decide which input signal x to use
One common choice is the unit impulse
the signal that is zero everywhere except at time zero n=0
The response of the filter to an impulse at time zero (UI)
  is called the impulse response IR (not a surprising name !)
  תגובה להלם
The impulse response of a filter is universally called hn
What can we say about the impulse response for a causal system?
0
0
hn

## Slide 44: Some impulse responses
What is the impulse response for an MA filter?
hn = =
So the MA coefficients are exactly the impulse response
What is the impulse response for an ARMA filter ?
Use the infinite convolution form!
hn = =
which is why we called these coefficients h in the first place!
The IR of an MA filter is nonzero for a finite number (L) of times
and so MA filters are called Finite Impulse Response filters
The IR of AR or general ARMA filters
is nonzero for an infinite number of times (due to the recursion!)
and so they are called Infinite Impulse Response filters

## Slide 45: IR for MA filter
a2
a1
*
a0
*
*
*
*
0
*
*
a2
a1
*
a0
*
*
*
*
a0
*
*
0
a2
a1
*
a0
*
*
*
*
a1
*
*
a0
0
a2
a1
a0
*
a2
*
*
a1
a0
0
0
0
0
0
0
1
0
a2
a1
*
a0
*
*
*
*
0
*
*
a2
a1
a0
0
You see why we chose this direction?
convolution, not correlation!
We can see why MA filters are FIR
by the following graphical construction

## Slide 46: IR solves the easy SI problem!
It is enough to input one simple signal to know the system !
if we know the response of a filter to the UI
we know its response to any SUI
because of time invariance (just shift the impulse!)
if we know the response of a filter to all SUIs
we know its response to any weighted combination of SUIs
because of linearity (add the weighted outputs!)
any input signal x
  can be written as the weighted combination of SUIs
since SUIs are a basis
0
hn
0
m
hn
m

## Slide 47: Easy problem Frequency Response (FR)
We have found one solution to the easy SI problem
Another common choice of input are the sinusoids
xn = sin ( k n )
But we need to enter all possible sinusoids (k=0, 1, …)
However, from the filter law we know that
sinusoids are eigensignals of filters
  the response to a sinusoid of frequency w : sin ( w n )
  is a sinusoid of frequency w (or zero output)
  yn = Aw sin ( w n + fw )
So we input all possible sinusoids
but record only the frequency response FR
the gain Ak
the phase shift fk
k
Ak
fk
0
1
2

## Slide 48: FR solves the easy SI problem!
It is enough to input these sinusoids to know the system !
if we know the response of a filter to xn = sin ( k n )
we know its response to xn = sin ( k n + f )
because of time invariance
if we know the response of a filter to arbitrary sinusoids
we know its response to weighted combination of them
because of linearity (add the weighted outputs!)
any input signal x
  can be written as the weighted combination of sinusoids
since they are the Fourier basis

## Slide 49: Does this make sense?
In the first solution we only needed one trial
we entered one input the UI
and recorded the impulse response hn
In the second solution we had to enter many inputs – all the sinusoids!
Does this make sense?
For the impulse response we needed to record many time values
for the frequency response
we only needed one complex number for each input
For example, assume a signal with N values (in time/frequency domain)
and an MA with N coefficients
for hn we need to record N values
for Hk we need to record N coefficients : 1 for each frequency
Why do you think we call the IR h and the FR H ?

## Slide 50: The easiest hard problem
The hard problem is so hard
that we will start with a simple case
Assume an MA filter with 3 coefficients
yn = = a0 xn + a1 xn-1 + a2 xn-2
We further assume that the input was zero until time n=0
(we can always take the time the signal starts to be n=0 …)
so xn<0 = 0
We need to find 3 unknowns – a0, a1, and a2
so we will need three equations to solve

## Slide 51: The easiest hard problem (cont.)
First let’s write the equation for n=0
y0 = a0 x0 + a1 x-1 + a2 x-2 = a0 x0
Since x0 ≠ 0 we can divide to find a0 = y0 / x0
Next we write the equation for n=1
y1 = a0 x1 + a1 x0 + a2 x-1 = a0 x1 + a1 x0
What do we already know?
y1 = a0 x1 + a1 x0 so a1 = (y1 - a0 x1) / x0
which is OK since x0 ≠ 0
Finally we write the equation for n=2
y2 = a0 x2 + a1 x1 + a2 x0
so a2 = (y2 - a0 x2 - a1 x1 ) / x0 which is OK since x0 ≠ 0

## Slide 52: The easiest hard problem – matrix form
First can rewrite the three equations
y0 = a0 x0
y1 = a0 x1 + a1 x0
y2 = a0 x2 + a1 x1 + a2 x0
in matrix format (with the coefficient as the vector)
which can be solved by inverting the matrix

## Slide 53: The easiest hard problem – some more
The matrix to invert is lower triangular
which is why it was so easy to solve
In fact, our solution was the straightforward inversion!
But this matrix has another characteristic
it has Toeplitz (T form
– the same value along diagonals
Otto Toeplitz

## Slide 54: A slightly harder problem
Assume an MA filter with 3 coefficients
yn = = a0 xn + a1 xn-1 + a2 xn-2
but the input does not start nonzero
We still need to find the 3 unknowns – a0, a1, and a2
so we will need three equations to solve
So pick any n (there is nothing special about any time)
and write three consecutive equations
yn = a0 xn + a1 xn-1 + a2 xn-2
yn+1 = a0 xn+1 + a1 xn + a2 xn-1
yn+2 = a0 xn+2 + a1 xn+1 + a2 xn
Note that we need to observe 5 consecutive times
n-2 xn-2 n-1 xn-1 n xn and yn
n+1 xn+1 and yn+1 n+2 xn+2 and yn+1

## Slide 55: Solving the slightly harder problem
Let’s jump directly to the matrix form
So, here is yet another connection
between convolution and (matrix) multiplication
The solution is once again to invert the matrix
but this time it is not lower triangular
but it is still Toeplitz
Inverting a general matrix is O(N3) and may be unstable
(well actually O(nlog2(7)) = O(n2.807) or even less)
but inverting a Toeplitz matrix takes only O(N2)
and is always stable (Levinson Durbin algorithm)

## Slide 56: BTW – another connection
We wanted to solve for the coefficients
and thus put them into a vector
In other circumstances we may want to rewrite the equations
yn = a0 xn + a1 xn-1 + a2 xn-2
yn+1 = a0 xn+1 + a1 xn + a2 xn-1
yn+2 = a0 xn+2 + a1 xn+1 + a2 xn
in another form
Here the matrix is Toeplitz but not square!
This is yet another connection between convolution
and multiplication by a Toeplitz matrix!

## Slide 57: Wiener-Hopf equations
The equations we found
are called the Wiener-Hopf equations
However, you will never see them written in this simple way!
That is because of noise!
If we solve them twice for different n
we won’t get exactly the same answer
So you might solve many times and average the solutions
but that would require many matrix inversions
and is not even the right thing to do!
Norbert Wiener

## Slide 58: What’s the right way?
Let’s go back to the original MA equation
yn =
Multiple both sides by xn+j and sum over all n
Remember that we mentioned the correlation of x and y ?
So the Wiener-Hopf equations can be written:
This has the same form, but need be solved only once!
we can reverse the summation order!

## Slide 59: What about AR filters?
Now let’s assume that the unknown system
is an AR filter with 3 coefficients
yn = xn + = xn + b1 yn-1 + b2 yn-2 + b3 yn-3
Once again we have three coefficients to find
so we need to write 3 equations
Note that we need to observe 6 times - 6 ys and 3 xs

## Slide 60: Yule-Walker equations
Let’s write the equations in matrix form
so
These are called the Yule Walker equations
The matrix has Toeplitz form
and so is solved by Levinson-Durbin
Your cellphone solves YW equations
thousands of times per second !
Udny Yule
Sir Gilbert Walker
vector
matrix

## Slide 61: What is the right way?
However, you will never see the Yule Walker equations
written in this simple way because of noise
Instead take the original AR equation (without the x)
yn =
Multiply both sides by yn+j and sum over all n
which can be written
we can reverse the summation order!

## Slide 62: What about ARMA filters
We can repeat the entire exercise for general ARMA filters
We have L+M variables and so have to write L+M equations
But the matrix will not turn out to be Toeplitz
and thus the equations will be difficult to solve!
So, in DSP we try to make every system identification problem
either MA or AR !

## Slide 63: Another way to solve
So far we have worked in the time domain
Why can’t we use the filter law directly?
Since Yk = Hk Xk we can divide to find Hk = Yk / Xk
and knowing Hk determines the filter!
The problem is that Xk can be zero!
So, instead we will use the z transform
and at last prove the filter law!
We will start with
the infinite convolution form of the ARMA filter

## Slide 64: Using z transform
the same tricks we’ve done before!

## Slide 65: H(z) is a rational function
B(z) Y(z) = A(z) X(z)
Y(z) = A(z) / B(z) X(z)
but Y(z) = H(z) X(z)
so H(z) = A(z) / B(z)
the ratio of two polynomials is called a rational function
roots of the numerator are called zeros of H(z)
roots of the denominator are called poles of H(z)

## Slide 66: Poles and zeros
From the fundamental theory of algebra we know that
every polynomial of degree n has n roots over the complex numbers
Hence we can write
where we see the zeros and poles of the transfer function
An important theorem in complex functions states
that the zeros and poles determine a rational function
to within a multiplicative constant
So the poles and zeros of the transfer function determine the filter
to within an overall gain
In diagrams zeros are shown as ● and poles as x

## Slide 67: Special cases
If the ARMA form is actually an MA filter
then there are α coefficients
but all the β are zero except β0 = 1
So H(z) = A(z) / B(z) = A(z) has zeros but no poles!
If the ARMA form is actually an AR filter
then there are β coefficients
but all the α are zero except α0 = 1
So H(z) = A(z) / B(z) = 1/B(z) has poles but no zeros
If the ARMA filter is general (not MA or AR)
then it has both poles and zeros

## Slide 68: Summary of filter names
FIR | MA | all zeros
IIR | AR | all poles
 | ARMA | zeros and poles

## Slide 69: What do zeros/poles mean?
Since Y(z) = H(z) X(z), if the input is xn = zn the output is yn = H(z) zn
A zero at z means that if the input is xn = zn the output is zero!
  A zero on the unit circle
means an input sinusoid xn = sin(ωn)
for which the output is zero
A pole means that if the input is that signal
the output explodes!
  A pole on the unit circle
means an input sinusoid xn = sin(ωn)
for which the output explodes
Why do zeros and poles not on the real axis come in pairs?
Why don’t we allow poles on or outside the unit circle
while zeros can be anywhere?
DC
Nyquist
ω>0
ω<0
z

## Slide 70: Are zeros important?
The filter law Y(ω) = H(ω) X(ω) tells us that
no new frequencies are created
but frequencies can disappear (when H(ω)=0) !
We call a frequency that disappears a zero of the filter
and more generally a signal zn that disappears
We already saw examples of MA filters with zeros!
yn = xn – xn-1 (first finite difference) has a zero at DC
yn = xn + xn-1 has a zero at Nyquist
yn = xn + xn-2 has a zero at half Nyquist (ω = π/2)
Bandstop and notch filters are used because of their zeros
band stop
f
notch
f
H(ω)
H(ω)

## Slide 71: Are poles important?
The filter law in the z plane Y(z) = H(z) X(z) tells us that
no new zn signals are created
but these signals can explode (when H(ω)=∞) !
We call a zn signal that explodes a pole of the filter
We already saw examples of AR filters with poles!
yn = xn + yn-1 (accumulator) has a pole at DC
yn = xn – yn-1 has a pole at Nyquist
yn = xn – yn-2 has a pole at half Nyquist (ω = π/2)
we don’t want poles on the unit circle (for sinusoids!)
but sinusoids that are amplified
require nearby poles
low-pass
high-pass

## Slide 72: Designing filters by poles and zeros
DSP experts sometimes design filters directly using poles and zeros!
What do the following pole/zero diagrams mean?

## Slide 73: How to find the transfer function?
If you are given the filter in the time domain
it is easy to find its transfer function and poles/zeros
by the following steps:
Move all the ys to one side and xs to the other
  to create the symmetric form
Write the equation in terms of signals using delay operators
Take the zT of both sides using our rule zT(-1 x) = -1 zT(x)
Divide leaving Y(z) on the LHS
Change numerator and denominator into polynomials (discard zM)
Find the roots of the polynomials

## Slide 74: Transfer function exercise
1.
2.
3.
4.
5.
6.

## Slide 75: Summary - filters
FIR = MA = all zero
IIR: AR = all pole
ARMA = zeros and poles
The following contain everything about the filter
(are can predict the output given the input)
a and b coefficients
a and b coefficients
impulse response hn
frequency response H(w)
transfer function H(z)
pole-zero diagram + overall gain
How do we convert between them ?

## Slide 76: Conversions

## Slide 77: Exercise
yn = xn + xn-1
this filter is causal MA
we can immediately guess that it is low-pass since
  it averages!
  H(DC) = 2 (from H = 1 + 1) – gain=2!
  H(Nyquist) = 0 (from H = 1 +1)
impulse response is 1, 1
frequency response: H(ω)eiωn = eiωn + eiω(n-1)
so H(ω) = 1 + e-iω = e-iω/2 (e+iω/2 +e-iω/2 ) = phase*2cos(ω/2)
causality results in phase!
transfer function
y = ) x so H(z) = 1 + 1/z → z+1
Try yn = xn - xn-1
n=0
IR
PZ
FR
π

## Slide 78: Exercise
yn = xn-1 + xn+1
this filter is noncausal MA
we can immediately guess that it is band-stop since
  H(DC) = 2 (from H = 1 + 1)
  H(Nyquist) = 1 (from H = 1 +1)
  H(mid) = 0 (use x = -1 0 +1 0)
impulse response is 1, 0, 1
frequency response: H(ω)eiωn = eiω(n-1) + eiω(n+1)
so H(ω) = eiω + e-iω = 2 cos(ω)
transfer function
y = ( + ) x so H(z) = z + 1/z = z2+1 = (z+i)(z-i)
Why are there 2 zeros?
n=0
IR
FR
PZ

## Slide 79: Exercise
yn = xn + ½ yn-1
this filter is causal AR
we can immediately guess that it is LP since
  H(DC) = 2 (from H = 1 + ½ H)
  H(Nyquist) = 2/3 (from H = 1 – ½ H)
impulse response is 1, 1/2, 1/4, 1/8, …
frequency response: H(ω)eiωn = eiωn + ½ H(ω)eiω(n-1)
so H(ω) = 1 / (1-½e-iω) = 2/(2 - e-iω)
|H(ω)|2 = 4 / (5 – 4 cos(ω))
transfer function
(1 – ½ ) y = x
so H(z) = 1/(1- ½ z-1) = 1 / (z- ½)
i.e., 1 pole at ½
n=0
IR
FR
PZ

## Slide 80: Exercises - filters
Try these:
analog differentiator and integrator
yn = xn + xn-1 causal, MA, LP find hn, H(w), H(z), zero
yn = xn - xn-1 causal, MA, HP find hn, H(w), H(z), zero
yn = xn + ½ yn-1 causal, AR, LP find hn, H(w), H(z), pole
Tricks:
H(w=DC) substitute xn = 1 1 1 1 … yn = y y y y …
H(w=Nyquist) substitute xn = 1 -1 1 -1 … yn = y -y y -y …
To find H(z) : write signal equation and take zT of both sides
Some solved problems:
IR and FR for MA and AR
zeros and poles for an ARMA filter