## Slide 1: Relationship between TICTOC and NTP
IETF 70
TICTOC BOF
Karen O’Donoghue
karen.odonoghue@navy.mil

## Slide 2: Network Time Protocol (NTP)
NTP grew out of work done by Dr. David Mills at the University of Delaware
  Previous versions: 1985 - NTPv0 (RFC 958), 1988 - NTPv1 (RFC 1059), 1989 - NTPv2 (RFC 1119)
  Current version: 1992 - NTPv3 (RFC1305)
  The NTP architecture, protocol and algorithms have been evolved over the last twenty plus years
The initial objective was to synchronize clocks over the global Internet
Status: Millions of NTP peers deployed worldwide
  Well managed NTP provides accuracies of:
    Low tens of milliseconds on WANs,
    Submilliseconds on managed LANs, and
    Submicroseconds possible using a precision time source, hardware assists, and a managed/engineered infrastructure
  NTP daemon ported to almost every workstation and server platform available today

## Slide 3: NTP – IETF Status
NTP developed outside the structure of the IETF
  Current definitive documents (RFC 1305 and RFC 4330) were independent submissions from Dr. Mills
The Internet Engineering Task Force (IETF) NTP WG was chartered in March 2005 to develop an NTPv4 specification to include:
  Updated NTPv4 algorithms, IPv6 support, Enhanced Security
  SNTP (Simple Network Time Protocol)
  An NTP MIB (for monitoring and management via SNMP)
Status:
  Protocol and Algorithms -08 draft released in November 2007.
    draft -09 available soon
  Plan to complete by 1Q 2008
  MIB, Autokey, and NTP Control protocol drafts also underway

## Slide 4
Is there work yet to be done for NTP?
  Clearly specifying NTPv4 and progressing standards track documents
  Minor modifications / extensions / improvements to NTP (e.g. increased polling interval)
  New requirements / next generation NTP capabilities
  Interworking between IEEE 1588 and NTP

## Slide 5
What is the best way to accomplish this work?
  NTP WG has struggled with:
    Lack of resources
    Lack of clear design authority
  NTP WG has work remaining to complete
  NTP needs to be tightly integrated with TICTOC effort
Are there enough time resources in the IETF to support two independent time related working groups?

## Slide 6: TICTOC Work Plan 1
Define a modular timing architecture
Clarify requirements for “use case”
  Both time and frequency
Analyze existing solutions in terms of the use case and the architecture
Identify existing components that can be leveraged
  Identify and develop any enhancements required to these existing components
Define new components needed to complete the architecture
  Don’t reinvent the wheel
1 As interpreted by the presenter...

## Slide 7
Proposed relationship between NTP WG and possible TICTOC WG?
  NTP WG will complete existing charter items
  TICTOC will address next generation activities in the context of the TICTOC charter
  Potential NTP modifications / extensions independent of TICTOC will be addressed on a case by case basis as drafts are received.

## Slide 8
  Discussion?