## Slide 1: IEEE-1588v2 Profile
Silvana Rodrigues
Silvana.rodrigues@zarlink.com

## Slide 2: IEEE-1588
IEEE-1588 – Standard for a Precision Clock Synchronization Protocol for Networked Measurement and Control Systems
  Defines a Precision Time Protocol (PTP) designed to synchronize real-time clocks in a distributed system
  Intended for Local Area Networks using multicast communications (including Ethernet)
  IEEE-1588 designed to work within a building or factory
    Intended typically for industrial automation and test and measurement systems (e.g. synchronized printing presses)
  Targeted accuracy of microsecond to sub-microsecond
  Approved in September 2002 and published November 2002
  Available from the IEEE-1588 web site
    http://ieee1588.nist.gov/
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: IEEE-1588 – Version 2
The PAR (Project Authorization Request) was approved in March 2005
  Resolution of known errors
  Conformance enhancements
  Enhancements to address new applications (including telecom)
Version 2 of the standard includes key features for Telecom
  Short Frame and higher message rates
  Unicast in addition to Multicast
  Fault Tolerant Clocks
  Allows different methods for Master clock selection
P1588 version 2 draft - letter ballot July 2007
Letter ballot comments resolution is completed
IEEE-1588 standard is expected to be completed Q1 2008
Telecom profile(s) need to be developed
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Profiles in Version 2
Definition of profile: The set of allowed PTP features applicable to a device.
The purpose of a PTP profile is to allow organizations to specify specific selections of attribute values and optional features of PTP that, when using the same transport protocol, inter-works and achieve a performance that meets the requirements of a particular application.
Profile is a set of required options, prohibited options, and the ranges and defaults of configurable attributes

## Slide 5: Profiles in Version 2 cont’d
An IEEE-1588 profile may be developed by external organizations including:
a) A recognized standards organization with jurisdiction over the industry, e.g. IEC, IEEE, IETF, ANSI, ITU, or;
b) An industry trade association or other similar organization recognized within the industry as having standards authority for the industry;
c) Other organizations as appropriate

## Slide 6: Profiles in Version 2 cont’d
A PTP profile should define
  Best master clock algorithm (BMCA) options
  Configuration management options
  Path delay measurement option (delay request-response or peer delay)
  Range and default values of all configurable attributes and data set members
  Transport mechanisms required, permitted, or prohibited
  Node types required, permitted, or prohibited
  Options required, permitted, or prohibited

## Slide 7: Profiles in Version 2 cont’d
A PTP profile shall extend the standard only by:
  TLV mechanism
  Optional BMCA
  Optional management mechanism
  It is permitted to create an implementation based on a Unicast model providing that the behavior of the protocol is preserved (PTP is written based on the multicast model)
Two default profiles are provided in Annex J of 1588v2
  Delay Request-Response Default PTP profile
  Peer-to-Peer Default PTP profile

## Slide 8: A few examples

## Slide 9: Delay Request/Response Mechanism
“Delay_Req messages shall be transmitted as multicast except if:
  The optional Unicast provisions of Clause 16 are used
  Specified otherwise by a profile”
“For applications that distribute only frequency and do not require the measurement of the path delays, an alternate PTP profile may specify that the path delay mechanisms of 11.3 and 11.4 need not be implemented or activated.”

## Slide 10: Best Master Clock Selection
V2 Best Master Clock (BMC) algorithm is similar to the V1 BMC algorithm
  But, there are differences
  e.g. V2 uses Announce message, V1 uses sync messages
V2 allows a PTP profile to specify an alternate BMC algorithm
  There are clear requirements in V2 that need to be met for alternate BMC algorithm

## Slide 11: Some fields Reserved for Profiles
Network Protocol enumeration
  Values F000-FFFD are reserved PTP profiles
PTP clock Class
  Values from 68-122, 133-170 and 216-232 are reserved for PTP profiles
Clock Accuracy enumeration
  Values 80-FD are reserved PTP profiles
Time Source enumeration
  Values F0-FE are reserved PTP profiles
Flag Fields

## Slide 12: Profiles at International Telecommunication Union ITU-T

## Slide 13: Study Group 15 – Question 13
Alcatel-Lucent presented a proposal to develop Telecom Profile(s) at the last meeting
Highlights of the discussion about Profile
  Synchronization requirements for a specific application
    Understand the requirements for the application and then address them through a specific profile that will meet those requirements
  Size of the network, load of the network and variation of loads
  Different profiles to address time and frequency applications
    Most likely several different profiles will be needed
    Performance is different for time and frequency

## Slide 14: Study Group 15 – Question 13 cont’d
Highlights of the discussion about Profile (cont'd)
  IEEE-1588 Network
    Does it include Transparent Clocks?
    Does it include Boundary clocks
    Does it include only non-1588 Bridges/Routers?
  Synchronous Ethernet combined with IEEE-1588
  Clear view of the architecture
    Can we achieve the desired performance in a certain architecture?
  Master clock
    How many do we need, where in the network?

## Slide 15
Thank You