## Slide 1: TICTOC -Topology-Discovery and Clock-Discovery
TICTOC BOF IETF70
Stewart Bryant (stbryant@cisco.com)

## Slide 2: Agenda
What problems do these discovery mechanisms solve?
Why should they be specified in the IETF?

## Slide 3: Time Transfer in a Packet Network
To acquire time a client (slave) needs to receive time-stamped packets from a time server, AND it needs to know how old the packet is when it arrives.
All systems assume that the path is symmetric, and therefore age is half the round trip time.
Link delay is often (but not always) constant, but switch/router delay is load dependent.
There are three approaches to switch/router delay:
  Find the lucky packets that experienced minimum delay.
  Boundary Clocks. Each switch/router becomes a client to its parent router closer to the time server and time server its child routers.
  Transparent Clocks. Measure the queuing time at each switch/router and either
    Correct the timestamp in packet or
    Report the delay to the client.

## Slide 4: Network Topology
Network topology is usually formed dynamically
It is usually the set of paths with the lowest routing metric.
The best metric path is usually chosen for highest bandwidth, but policy may be a factor.
The best data path may not be the best path for time and frequency transfer.

## Slide 5: Lucky Packet Path
Best data path from master to slave is M-A-B-C-S
At each router there is a probability that the timing pkt will be queued - O(phops)
Best time path may be M-D-S
Best timing path may not be available through the existing IGP
Best data path may not be reciprocal.
A
B
C
D
Master
Slave
1
1
1
1
2
3

## Slide 6: Boundary Clock Path
Optimum data path is M-A-B-C-S
Data path A to D is via B and C, but B does not support boundary clock
IEEE1588 uses link local addressing/forwarding, application layer hellos, and application layer routing.
Is this the best approach in the IETF environment?
A
B
C
Master
Slave
1
1
1
3
D
1
10
2
Note that the cascading of the clock servos causes degradation of time quality. The extent is implementation dependent. This was why IEEE1588 introduced transparent clocks.

## Slide 7: Transparent Clock Mechanisms
R1
t1
t2
t1 = t2-t1
R2
t3
t4
t2 = t4-t3
T
T=T+ t1
T=T+ t1 + t2
R1
t1
t2
t1 = t2-t1
R2
t3
t4
t2 = t4-t3
T
T
T
t0
t0+ t1
t0+ t1 + t2
One Step Transparent Clock
Two Step Transparent Clock
T’ = T + t0+ t1 + t2

## Slide 8: Transparent Clock Path
Optimum data path is M-A-B-C-S
Data path A to D is via B and C, but B does not support transparent clock
Sync packet is an ordinary packet, and so cannot be forced using application layer routing.
A
B
C
Master
Slave
1
1
1
3
D
1
10
2
TC
TC
TC

## Slide 9: Diverse Path
If the path to the master is lost the slave needs to go into holdover.
Precision of clock and duration of holdover have a direct effect on the cost of the slave.
Delivering clock over diverse paths can lead to a reduction in slave cost.
Diverse path can also be used to good effect in lucky packet clock algorithms, because the probability of delay is statistically reduced.
A
B
C
Master
Slave
1
1
1
3
D
1
3

## Slide 10: Topology - conclusion
The quality of time transfer is improved if the network topology is optimized for the application.
The optimum time transfer topology may not be congruent with the optimum data topology.
Topology is controlled by routing, thus routing support is needed to optimize time transfer.
The IETF is the design authority for routing protocols.
Therefore to design the highest quality time transfer protocol for IP networks the IETF has to engage with the problem.
The proposal is NOT for TICTOC to design a new routing protocol.
The proposal is for TICTOC to produce a time distribution architecture, to identify the time support routing requirements, and then to work with the existing routing groups to define the required protocol extensions.

## Slide 11: Clock Discovery
As time usage becomes more ubiquitous more nodes need to be accurately synchronized to high quality network clock.
Clock needs to be of adequate quality, have the resources available to support the client and be accessible via a time suitable network path.
When the clock fails the slave needs to find a new clock
Initially clock-slave pairing will be statically configured.
As the number of slaves increases and the demands on time quality/availability increase static configuration does not scale.

## Slide 12: Network Environment
Service Provider and enterprise network environments are different
  Routing protocols are different (e.g. BGP in SP networks, but less likely in Enterprise networks)
  SP networks have sophisticated provisioning systems

## Slide 13: Clock Discovery Protocol
Given the symbiosis between routing and clock distribution a clock discovery protocol based on routing seems likely.
Extension of an IGP seems most likely to be applicable to SP and Enterprise environments
BGP is the “traditional” method used for discovery in SP networks.

## Slide 14: Clock Discovery - Conclusion
It is likely that as high quality time distribution becomes an important element of the network infrastructure a discovery mechanism will be needed.
Given that a slave needs both a suitable clock and a suitable path, there is some symbiosis with routing.
This is an area that can only be effectively addressed in the IETF.

## Slide 15
Questions?