## Slide 1: Use Cases
TICTOC BOF– 70th IETF
4 December 2007
Yaakov (J) Stein

## Slide 2: Three Cases
The proposed charter specifies three use cases:
Service Provider (SP) network
  well engineered
  on-path support
  walled garden security
  1588 preferred
General network (e.g. public Internet)
  best effort network behavior
  no on-path support
  security suspect
  NTP preferred
Interworking case
  on one side - SP network
  on other side - general network
We need to consider frequency and time distribution

## Slide 3: Service Provider Network
Well engineered
  Connection oriented (CO) or explicitly routed
  Low packet loss
  Low Packet Delay Variation (PDV)
On-path support
  Synchronous Ethernet (Sync-E)
  Boundary clocks
  Transparent clocks
Walled garden security
  core network elements under strict control
  client access limited and has well-defined interfaces
This is the environment where
1588
Sync-E combined with 1588
is preferred

## Slide 4: General Network
Best effort network behavior
  packet loss
  PDV and outliers
No on-path support
  PDV degrades frequency recovery
  ranging requires minimum gating
Security suspect
  false clock sources
This is the environment where NTP is widely deployed

## Slide 5: Interworking Case
Both types of network present
NTP and 1588 have roughly similar semantics
  establish local frequency reference
  ranging with minimum gating
  control loop algorithms
but different syntax
  message types
  timestamp format (TAI/UTC, resolution)
In principle, always possible to recreate time source and redistribute
General network
SP network
client
time source
master
IWF
NTP?
1588?